## Slide 1
Peter Monaghan “Hall C January 2011 Users Meeting” 15th January 2011
SHMS Wire Chamber Update
  RECAP from August Review:
    Vendor price quote 5x larger than expected
    Exploring possibility of manufacturing smaller PCBs and then
    laminating several together to make a single plane
  Discussions with Hall D Engineers (their circular chambers are
  made in pieces).
  Do NOT do it!!! (if possible!)
  Vendor Search – industry maximum tooling for PCBs is 40 inches wide.
  Only two vendors in the USA capable of making such large PCBs
    Triangle Labs, Inc, Nevada
    Universal Circuits Inc, Minnesota
  Start to revise our design to accommodate a narrower PCB.

## Slide 2
PCB Redesign – U Plane
Peter Monaghan “Hall C January 2011 Users Meeting” 15th January 2011
  Acceptance unchanged : 80cm X 80 cm
  Overall width reduced to 38.6 "
  Side bar width reduced to 3.15 "
  Frame deflection due to wire tension changes from 0.002" to 0.011" (0.034 % of wire length)
  Working on procedures for transfer of wire planes from stringing jigs to final assembly station

## Slide 3
PCB Redesign – X Plane
Peter Monaghan “Hall C January 2011 Users Meeting” 15th January 2011
  Wire planes now have two HV inputs
  Overall length unchanged (ex. HV in)
  Wire cell spacing unchanged

## Slide 4
PCB Redesign – K (cathode) Plane
Peter Monaghan “Hall C January 2011 Users Meeting” 15th January 2011
  All designs check for consistency
  Advice from Fast Electronics Group taken into consideration
  Redesign means small changes to design and dimensions of front and rear plates
    Changes mounting frame design

## Slide 5
Redesign and PCB Status
  Redesign keeps acceptance unchanged but reduces overall width of pcb to less than 40 inches.
  Final eCAD drawings completed for cathode (K), U and X wire planes.
  Final fabrication drawings to be completed for vendor.
  Complete set of drawings sent to vendor next week.
  Triangle Labs Inc, Nevada, quoted $54 000 for the whole project.
    includes spare boards – 2 X, 2 U and 4 K boards
  Purchase order placed through Hampton University
    received by vendor and material ordered.
Peter Monaghan “Hall C January 2011 Users Meeting” 15th January 2011

## Slide 6
Foil Stretching Jig
  Finished construction of the foil stretching jig.
  Successful full scale test using mylar foil; see videos separately.
Peter Monaghan “Hall C January 2011 Users Meeting” 15th January 2011
Sealed plywood base and wooden sides
Polished polyethylene block in centre

## Slide 7
Foil Stretching Tests
  Several stretching tests completed to check foil tension.
Peter Monaghan “Hall C January 2011 Users Meeting” 15th January 2011

## Slide 8
Foil – Frame Adhesion Test
  Successfully test glued a stretched foil to G10 frame.
Peter Monaghan “Hall C January 2011 Users Meeting” 15th January 2011

## Slide 9
Materials Purchased
  HV wire, signal wire, epoxy, cathode foil and gas window foil purchased.
Peter Monaghan “Hall C January 2011 Users Meeting” 15th January 2011
Signal wire: 25 mm
gold plated tungsten
HV wire: 100 mm
copper-beryllium
Cathode foil is
copper coated
kapton, 1 mil thick
Gas window is
aluminised mylar
1 mil thick

## Slide 10
Summary
  Redesigned PCBs to be able to manufacture each plane as a single piece; acceptance unchanged.
  Received a reasonable price quote from vendor.
  Purchase order for PCBs placed.
  New eCAD drawings complete; fabrication drawings next.
    Full suite of drawings to go to vendor next week.
  Foil stretching jig constructed and tested successfully.
  HV wire, signal wire, epoxy, cathode foil and gas window foil purchased and received; thanks to HCF and SAW.
  Continuing to develop our techniques and procedures.
Peter Monaghan “Hall C January 2011 Users Meeting” 15th January 2011