## Slide 1: Rosen07 Two-Photon Exchange Status Update
James Johnson
Northwestern University & Argonne National Lab
For the Rosen07 Collaboration

## Slide 2: Rosenbluth 2007 JLab E05-017
HMS in Hall C at Jefferson Lab
4cm liquid hydrogen target for elastics
4cm aluminum dummy for endcap subtraction
May 8 – July 13, 2007
Notes: Add picture of HMS

## Slide 3: Rosenbluth 2007
Rosenbluth method
  Plot reduced cross section vs. angular variable ε at fixed Q2
  GE, GM from slope and intercept
Super Rosenbluth
  Detect protons instead of electrons
  Reduces error
I. A. Qattan et. al, Phys. Rev. Lett. 94:142301, 2005
Notes: Epsilon – virtual photon longitudinal polarization

## Slide 4: Rosenbluth 2007
102 Kinematics points
Q2 0.40-5.76 GeV2
13 points at Q2=0.983
10 points at Q2=2.284
Notes: Kinematics taken
Each solid, colored line is a different beam energy, data is where the lines intersect our Q^2 values
In particular, very low- and very high-epsilon points, where there is little previous data
16 Q^2 values
17 Ebeam values, range
At each Q^2, several points for an L-T seperation

## Slide 5: Elastic Spectrum
Hydrogen elastics
  Compare to simulated elastics
Background
  ‘Dummy’ runs for endcap subtraction
  Simulated π0 photoproduction
Notes: Don’t have a simple gaussian peak, there’s a tail because of the radiative spectrum
Q^2 = 0.980 GeV^2, eps = 0.046

## Slide 6: Analysis Steps
Sum data & dummy runs at selected kinematic
Simulate elastics, pion photoproduction, compton scattering
Scale all to charges and efficiencies
Fit dummy + simulations to the data
  Extract ratio of simulation cross-section to actual cross-section
Notes: Maybe example unpeeling here

## Slide 7: Current Status
Calibrations – Completed
  Drift Chamber Offset
Efficiencies
  Tracking, Triggering, Deadtime – Well known
  Target Length Correction
  Proton Absorbtion
  Particle Identification
    Time-of-Flight cuts
    Aerogel cut
Resolution Mismatch
  Smearing, Non-Gaussian Tails
  Finalize Δp cuts
Notes: Picture?

## Slide 8: Drift Chamber Offsets
Shoulder in yptar distribution
Examined in thin-foil and sieve slit targets
Small resolution improvement
Now included in Replay
Notes: Yptar – particle angle at target
Ibrahim Albayrak
Plot from first attempt

## Slide 9: Target Length Correction
4cm cylindrical target
  Off-center beam leads to a shortened target and lower yield
  Beam is rastered 1mm to either side of the center
Survey runs done at different beam positions
  Fit to the yields gives the beam offset
Beam positioned around +1mm during data collection
Shows a half-percent reduction in yield
Notes: Target position shifts slightly during cooling, this was also surveyed but is unnecessary when we fit yield directly in terms of beam position
Graphic – fit of normalized yield to beam position
Fit performed by Vahe

## Slide 10: ToF Cut Efficiency
Time-of-Flight cuts used for particle identification
Refine cut positions
  Different cuts above and below the proton peak
Determine efficiency
  Largest remaining correction
Different issues on positive and negative sides
Notes: Both most strongly momentum dependant
2.055 GeV 47 deg; 0.98 GeV^2

## Slide 11: ToF High Side
Excluding pions, faster than protons
Elastic protons disappear quickly
Pion tail may extend underneath proton peak
Notes: Graph, no elastic peak for high ToF
2.055 GeV 47 deg; 0.98 GeV^2

## Slide 12: ToF Low Side
Excluding deuterons
  Place cut just above deuteron cutoff
Elastic protons extend into this region as they lose energy or scatter
  Need to know the shape of this tail
Notes: Plot – Data w/ deuteron peak subtracted out 3.362 GeV 36 degrees 2.28 GeV^2
3.362 GeV, 36 deg; 2.28 GeV^2

## Slide 13: ToF Low Tail
All deuterons come from the endcaps
  Can be removed with dummy subtraction
Shape of the tail
Determine efficiency
Notes: Plot – Data w/ deuteron peak subtracted out 3.362 GeV 36 degrees 2.28 GeV^2
3.362 GeV, 36 deg; 2.28 GeV^2

## Slide 14: Aerogel Cut Efficiency
Aerogel cut excludes pions
  What rate does it capture protons?
  What rate does it fail to capture pions?
Not necessary at low momentum
Slight angular dependence
Notes: Plot – uniform below pion cutoff, we like this
2.055 GeV, 30 deg; 1.90 GeV^2

## Slide 15: Resolution Mismatch
Data peak was broader than elastic simulation
Shape improved with angle smearing
  0.9 milliradians
Non-gaussian tails are also present
  Can affect integrated counts
Notes: 3.362 GeV 36 deg 2.28 GeV^2

## Slide 16: Non-Gaussian Tails
Possibly due to extra hits in wire chambers decreasing resolution
Applied to angle
  Works better on broad Δp peaks than narrow
  Suggests momentum smearing is also present
Notes: Broad peaks occur at high angles

## Slide 17: Momentum Cuts
Determine the integrated cut region
Preliminary cuts based on width of Δp peak
  Explicit problem with resolution mismatch
  Angular dependence
Refining cuts relies on fixing non-gaussian tails

## Slide 18: Missing Efficiencies
Data/simulation ratio should be ~1
Target length ~0.5%
Non-gaussian Tails, Cuts, ToF, Aerogel few percent each

## Slide 19: Finally
Closing in on final efficiencies
Find cross sections
Extract form factors
Perform linearity testing
Early summer