| Jefferson Lab Alignment Group Data Transmittal |
| --- |
| TO: B. Crahen, T. Whitlatch | DATE: 24 Jan 2014 |
| FROM: J. Dahlberg | Checked: | # : D1538 |

DETAILS:                                                      			DATA: Inspection\HallD\FDC\131205a

Below are the results from the Dec 5th, 2013 survey carried out on the Hall D FDC.  The coordinate system is based on the solenoid center at a distance of 2392.2 mm downstream from the upstream face.  The FDC center is based on an average center Z axis through all four detector packages with the Z = 0 at the upstream side of detector 1 gusset.  The ideal values for the FDC package fiducials are based on a distance of 2408 mm downstream from the solenoid upstream face.  A +X is to the beam left, a +Y is above ideal, and a +Z is downstream.  Values are in millimeters and degrees.

FDC CENTER FROM IDEAL

X:  -0.04	Y:  +0.05	Z:  -102.47

Yaw:  0.0203 ccw looking from above.

Pitch: 0.0158 ccw looking from beam right.

Roll: -0.0060 ccw looking from upstream.