keV Mott Measurement Procedure in Tunnel (rev. 9 April 09)

Turn on detectors in Injector Service Building (+115 V on channels 1 and 3)

| Amp Gains | Coarse Right | Coarse Left | Fine Right | Fine Left |
| --- | --- | --- | --- | --- |
| 100 keV | 200 | 200 | 1.79 (9 clicks from min) | 1.79 (9 clicks from min) |
| 500 keV | 50 | 50 |  |  |

VL beam to Mott viewer

Hall B chopper slit will be needed – use Hall B laser or adjust phase of A or C through B slit

Target ladder to viewer position (motl 24066)

Determine if chopper is on (100 keV if off, 500 keV if on)

Mott line dipoles and solenoids to nominal values for energy

|  | MBO0I06 | MDI0D01 | MFB0D01A | MFB0D01B |
| --- | --- | --- | --- | --- |
| 100 keV | 208 mA | 1338.660 mA | -965 Gcm | +965 Gcm |
| 500 keV | 636 mA | 3924 mA | -2369 Gcm | +2369 Gcm |

VL beam through to Mott target ladder viewer, adjust beam position beam using MHGB0D01H/V

Move Target ladder back to home/reset (motl 65535)

CW Beam to FC1

Adjust beam current: 10 nA for 100 keV, 100 nA for 500 keV, use chopper slit and attenuator

Remove FC1 and measure CW current on polarimeter dump

We are still having an -12 nA offset on dump faraday cup: expert mode, relative zero

Make measurements

FC1 in

Move target ladder to selected value

Verify correct CW current in FC1

Remove FC1 and run beam

Look for peaks on both detectors: if peaks are missing, slight steering adjustments may be needed

Spectrum runs (script prompts for window and lower level settings)

Set Window and Lower Level on amplifiers in ISB

Asymmetry runs

Backout

Target ladder retracted

Dipole magnets back to original values (in injector segmented mode, the 500 keV bend magnet cannot be moved without dropping from beam permit – we need to work out a good protocol that will work in either state.  If we are changing magnet value, cycle, if value staying the same, no cycle?)

Any changes to laser phase to get beam through hall B slit back to nominal.

Correctors on Mott line to zero

Detector HV supplies/scopes off in service building

NOTE: Along bunchlength, turn off buncher or phase all RF elements as beam phase changes!!!! (check spectra at each phase)