LL Gun commissioning (5/11/06)

Part 1….good beam from gun

Observations

- Vertical kick or offset of beam before first solenoid.

- Beam spot size & shape depends upon cathode spot location.

- Why is electrostatic center ~2 mm from activation center?

Done

- Resistance of baked MFH okay?

- Haimson wiring and magnetic fields okay?

- Gun IP hi-potted and now okay

- Laser chamber IP hi-potted => HV cable died, pump okay, but no improvement

- Initial lifetime measurements w/ & wo/ biases.

To Do

- Increase 15 deg dipole window to investigate aperture

- Anode structure current vs. cathode scan tell us something?

- Measure laser spot size/profile w/ Spiricon and razor

- Ken’s results?

- Alignment => where is cathode/anode located wrt ideal line?

- Alignment => where is MFH solenoid wrt ideal line?

Part 2….compare lifetime vs. BP

Grounded anode structure

- Lifetime vs. spot location (4 spots around electrostatic center)

- What is the meaning of current observed on anode and anode tube?

Biased anode structure

- Lifetime vs. anode alone (500,1000,1500,2000) & vs. anode support alone

- Lifetime vs. anode+anode support in 4:1 ratio (up to 2kV/500V)