## Slide 1: NGLS DESIGN STUDY AND ACCELERATOR R&D John Corlett for the NGLS Team March 5, 2012

## Slide 2: Motivation
Weak pulses at
high rep rate
Today’s storage ring x-ray sources
~ nanoseconds
~ picoseconds
~nanojoule
Tomorrow’s x-ray laser sources
~ microseconds
~ attoseconds to femtoseconds
Intense pulses at high rep rate
~0.1 millijoule
Intense pulses at
low rep rate
~ milliseconds
~ femtoseconds
Today’s x-ray laser sources
~millijoule
…
…
Coherent X-rays with high repetition rate, unprecedented average brightness, and ultrafast pulses
Notes: Storage rings and FELs provide beamlines with about 1 Watt average power (0.1% BW)
Next generation superconducting-linac-driven FELs can provide hundreds of Watts, and with flexibility in X-ray pulse characteristics
Orders of magnitude more average power in coherent beams, with many (10) orders of magnitude greater peak brightness than storage rings

## Slide 3: Approach
CW superconducting linac,
laser heater, bunch compressor
High-brightness, high rep-rate gun and injector
Beam spreader
Array of independent FELs
X-ray beamlines and endstations
High average power electron beam distributed to an array of FELs from high rep-rate injector and CW SCRF linac

## Slide 4
High repetition rate soft X-ray laser array
  Up to 106 pulses per second
  Average coherent power up to ~100 W
Spatially and temporally coherent X-rays (seeded)
  Ultrashort pulses from 250 as – 250 fs
  Narrow energy bandwidth to 50 meV
Tunable X-rays
  Adjustable photon energy from 280 eV – 1.2 keV
    higher energies in the 3rd and 5th harmonics
  Polarization control
  Moderate to high flux with 108 – 1012 photons/pulse
Expandable
  Capability
  Capacity
Capabilities
More photons per unit bandwidth
More photons per second
Shorter pulses
Controlled trade-off between time and energy resolution

## Slide 5
Science requirements drive machine design
Tuning range
Maximum photon energy
Peak flux
Average Flux
Repetition rate
Two-color capability
Pulse duration
Bandwidth
Accuracy
Stability
Synchronization
Contrast ratio

## Slide 6: Accelerator Systems R&D priorities
High repetition rate
  Injector “APEX”
  Beam spreader
Advanced FEL operation
  Modeling and optimization
  Seeding approaches
  Seed lasers
  Superconducting undulators
Developing partnerships
SCRF
RF power
Notes: High repetition rate
  Injector (APEX)
  Spreader
Advanced FEL operation
  Seeding
  Lasers
  Undulators
  Instrumentation & diagnostics
  Timing & synchronization
High average power
  Beam dumps
Superconducting accelerator developments
  High Qo
  Higher order mode power
  Field emission
  Harmonic cavity

## Slide 7
APEX gun: high-brightness MHz electron source
APEX cavity is successfully RF conditioned
Notes: Repetition rate 1 MHz
Charge per bunch from ~10 pC to ~1 nC
Emittance <10-6 mm-mrad (normalized)
Electric field at the cathode ≥~10 MV/m (space charge emission limit)
Beam energy at the gun exit ≥~500 keV (space charge control)
Bunch length ~100 fs to ~10 ps for handling space charge effects, and for allowing different modes of operation
Compatible with magnetic field control within the gun (emittance exchange and compensation)
10-11 Torr vacuum capability (cathode lifetime)
Accommodates a variety of cathode materials

## Slide 8: APEX in the Beam Test Facility
Notes: Installation almost complete
Laser beam on cathode plug
Photoemission test about to start

## Slide 9
APEX Activity and Plans
F. Sannibale
Yb fiber photocathode drive laser
1 MHz reprate Yb fiber laser
  LLNL/UCB/LBNL collaboration
Notes: 0.7 W @ 1052 nm (systems being optimized)
  240 mW @ 526 nm
    ~ 1.5 nC, 1 MHz CsK2Sb
  55 mW @ 263 nm
    ~ 190 pC, 1 MHz Cs2Te
Other lasers available for future use
  1 MHz, 2 W, 1052 nm (Calmar)
  1 MHz, >100 W,1064 nm, cryo-cooled Yb:YAG (Qpeak Inc., STTR)

## Slide 10
High QE
Good lifetime at
10-9 mBar
Low transverse
momentum
Photocathode materials R&D
K2CsSb:
6% QE at 532 nm
0.36 microns / mm rms en
>> 1 week lifetime
Notes: Padmore leads
ALS, surface & materials science expertise

## Slide 11
APEX stages
Diagnostics systems in collaboration with Cornell CLASSSE
Accelerating cavities in collaboration with ANL AWA
Phase I:
Beam characterization at gun energy (750 keV)
Phase 0:
Gun and photocathode tests
Planning for final installation in 2013
Phase-II:
Beam characterization at 15–30 MeV
6-D brightness measurements
Notes: Phase 0 (1 MHz)
Photocathode tests
  QE Vs time
  QE maps
  Cathode emittance
  High current cathode performance (~mA)
  Energy measurement with correcting coil
Phase 1 (1 MHz)
Beam characterization at the gun energy (750 kV)
  Space charge emittance
  Time and energy resolved measurements
Phase II (10 Hz)
  Beam characterization at the injector exit (15-30 MeV)
  6D brightness measurement
  Jitter measurements
  Review held November 28
      Chair I. Bazarov (Cornell)

## Slide 12
Electrostatic
septum
Magnetic
Septum
DC Bends
Electrostatic allows 5x weaker kickers (1/5 stability tolerance)
Footprint reduced ~1/3
Optimizing the beam spreader
Kicker
(0.6 mrad –
was 3 mrad)
Notes: Further optimization under way (CSR, impedance, footprint, diagnostics)

## Slide 13
Electrostatic allows 5x weaker kickers (1/5 stability tolerance)
Footprint reduced ~1/3
Optimizing the beam spreader
Pulsed Kicker
1 m, 0.6 mrad
z
x
Magnetic Septum
1 m, 45 mrad
Electrostatic Septum
2.0 m, 9.6 mrad
Linac line
ARC
D
D
D
F
Notes: Further optimization under way (CSR, impedance, footprint, diagnostics)

## Slide 14
HL
CM1
CM2
CM3
CM9
CM10
CM30
Bunch compressor 1
Laser heater
Spreader
Linac developments – “10/25/11” layout
Injector
Accelerating cryomodules
Linearizer cryomodules
Bunch compressor 2
Accelerating cryomodules
BC1
168 MeV
BC2
640 MeV
GUN
1 MeV
Heater
70 MeV
SPRDR
2.4 GeV
~670 m
Notes: Balancing demands on systems
Using common components
Next steps:
  Integrate spreader kicker and septa with transport lattice
  Work with partner Lab to improve SCRF linac performance
    Increase gradient from 13 MV/m to 16+ MV/m
    Increase Qo from 1x1010 to 2x1010

## Slide 15
1 keV
5 keV
Pareto front of genetic optimization
300 pC, ~70 MeV design point
Delivers required beam brightness
RMS bunch length (mm)
Projected normalized emittance (m-rad, 100%)
RMS energy spread
Injector optimization
Gun
Buncher
Notes: Uses main linac cryomodule
Genetic algorithm

## Slide 16: Beam dynamics modeling through linac
Two-stage compression
2.4 GeV
  APEX-gun generated beams (300pC)
  ≥ 600 A peak current and small residual energy chirp within usable beam core
  limited CSR-induced projected emittance growth
Twiss functions through the Linac
Current profile
*’Elegant’ simulation through the linac starting from an ASTRA-simulated beam out of the APEX-gun based injector
Longitudinal beam phase-space
at entrance of FEL beamlines*
Notes: ASTRA
ELEGANT
IMPACT
<0.6 micron
<100 keV

## Slide 17
e- chicane
1st undulator
2nd undulator with taper
SASE FEL
Self-seeded FEL
Single crystal: C(400)
SASE FEL spectrum
~ 20 eV
Seeded FEL spectrum
~ 0.5 eV
Near Fourier Transform limit
LCLS Soft X-ray Self Seeding – in planning stages
Initial results: 40x reduction in BW (40x increase in peak brightness)
Self-seeded FELs

## Slide 18: Laser seeded FEL – ”ECHO”
Developing R&D plans
  Beam experiments
  Laser developments
EEHG
HHG
HGHG
Notes: Our approach for a future machine is to use a range of FEL designs, including the ECHO technique under development
We will develop seeded FEL capabilities in an R&D program – Echo, HHG, self-seeding, oscillators, … etc
Need 10’s micro-Joule in UV (200 nm) – i.e. 10’sto 100 Watts in IR
Simulations use GENESIS and GINGER codes
Stupakov, G., Using the Beam-Echo Effect for Generation of Short-Wavelength Radiation, Physical Review Letters 102 (2009) 074801

## Slide 19: HHG seeded FEL R&D
1 kHz, 40 mJ, HHG source for seeding R&D
HHG seeding at ~50–100 eV
HGHG to reach 1.2 keV
Notes:       ~100 kW (peak) seed power at ≤50 nm
      ~10’s nJ per pulse
  Needs laser development for higher repetition rate
      ~kW average power @ ~4µm
      Phase-matching in capillaries
      Tunability
      Development of long-pulse capability
      Diagnostics, control, reliability

## Slide 20
FEL harmonics measurements at LCLS
Daniel Ratner
Now using filters
Future using spectroscopic fast CCD detector
  LBNL detector
Fit to detected signal level with attenuators

## Slide 21: Superconducting undulator R&D
Cryostat for test and measurement
HTS tape undulator
Planar Nb3Sn undulator
Notes: Motivation
  Reduce costs and enhance performance
  Shorter FELs
  Shorter, lower energy linac
  Higher photon energy
  Greater tuning range
  Potential radiation damage resistance

## Slide 22
DOE has approved Mission Need for a Next Generation Light Source
  LBNL led the effort
  We are:
    Developing science case and experimental requirements
    Evolving machine design to best meet science needs
    Executing and developing R&D plans
    Strengthening and building collaborations
Summary