## Slide 1
Status Report for the MAX IV project
Magnus Sjöström, on behalf of the MAX IV project team
MAX IV site, Jan 2012
MAX IV site, the future
Notes: The MAX IV facility is a 3rd generation light source currently under construction in Lund, Sweden. It includes two storage rings at 1.5 and 3 GeV, along with a 3 GeV linear accelerator that will act both as injector for the storage rings as well as a source for a Short Pulse Facility (SPF). The current status of the project will be presented, with an emphasis on the 3 GeV storage ring.

## Slide 2: Outline
Overview
Project status
3 GeV storage ring updates
  Optics
  Injection studies
  Vacuum
  Magnets
1.5 GeV storage ring updates
Injector updates
  Electron guns

## Slide 3: Facility layout
Injector
3 GeV ring
1.5 GeV ring
SPF
e- guns

## Slide 4: Storage Rings Parameters
Notes: Why does horizontal emittance vary?

## Slide 5: 3 GeV ring: optics modification
Motivation: Dynamic correction of IDs is now done only with quadrupole doublets in long straights.
Old Optics
New Optics
Notes: Motivation:
Dynamic correction of IDs is now done only with quadrupole doublets in long straights
Advantage because:
PFSs introduced a significant dipole kick (size?) which cannot easily be compensated for dynamically
  FOFB mainly locks down the trajectory in the straights
  Achromat interior is stabilized by SOFB primarily, FOFB only compensates if any DOF happen to be available; trajectory variations lead to coupling variations due to the sextupoles
Each strong ID required 0.2% tuning range in the dipole gradient. With roughly 10 strong IDs expected this is expected to be an issue; the PFS tuning range is limited by the air cooled design.
Bipolar PS capable of supplying a very large current would be needed, and the switching issue may introduce issues.

## Slide 6: 3 GeV ring: optics modification
Vertical tune increased two units, natural chromaticity increased 6 units. Non-linear correction re-optimized
Old Optics
New optics, bare lattice
Notes: Dynamic aperture essentially unchanged
What is the required aperture set by?
– Injection process: ~5 mm maximum amplitude after PSM
– Margin for error (misalignments, injection tuning)
➡ ± 7 mm @ LS center
– Lifetime concern (coupling)
– In-vacuum ID pmuL: min. gap 4.2 mm, total length 3.8 m
➡ ± 2 mm @ LS center (incl. 0.5 mm safety margin)

## Slide 7: Modified Storage Ring Optics: non-linear
Vertical tune increased two units, natural chromaticity increased 6 units. Non-linear correction re-optimized
Bare Lattice
10 IVU

## Slide 8: Error Modeling
Alignment Errors
Field Errors
0.05 % rms with cut-off at ±2 σ

## Slide 9: 3 GeV ring: dynamic Aperture

## Slide 10: 3 GeV ring: lattice momentum acc.
Notes: Approximations:
Standard 11 mm aperture chambers throughout the achromat
Bare lattice
1 MV corresponds to commissioning: 4 cavities á 250 kV
1.8 MV corresponds to final configuration: 6 cavities á 300 kV

## Slide 11: 3 GeV ring magnets
Each cell is realized as one mechanical unit with several magnet elements in each

## Slide 12: 3 GeV ring magnets
Features:
Designed to be dismountable at mid plane
Coils can be exchanged without breaking vacuum!
Magnets connected to same PS can be shunted to same strength

## Slide 13: Main challenges for manufacturing:
Tight Mechanical tolerances.
Production capacity: 140 cells -> 1320 magnet elements -> 5800 magnet coils, 6840 yoke parts
Field meas. accuracy and throughput
Correct wiring: XX XXX trim- and ts-connections to terminals with correct position, polarity and marking.

## Slide 14: Main challenges for us, during manufacturing:
Evaluation of mech. meas. data (6840 parts -> 2640 magnet halves).
Evaluation of field meas. data (1320 magnet elements)
Time schedule monitoring, investigations, inspection visits… Emphasis on reaching tolerances in first stage, then production pace.

## Slide 15: Status – magnet design
Basic design (pole shapes, coil design, etc) completed early 2010
3D cad started mid 2010 -> first draft set of drawings in October -> request for quotation set of drawings Jan 2011 ->
Technical spec for purchase completed Feb 2011.
Concept is purchase complete assembled magnets with cabling and everything from subcontractors. We are responsible for magnetic design. They are responsible for mech. tolerances and perform field meas. to our specs.

## Slide 16: Status – magnet manufacturing
Iron blocks (294 pcs, ca 300t) delivered July 2011.
Contract for 3 GeV Ring Magnets Signed September 12th, 2011.
Danfysik (M1, M2, U3) and Scanditronix Magnet (U1,U2,U4,U5)
Both companies will build measuring benches.
Delivery of pre-series planned for ~9 months after contract signature.
Delivery of all magnets by December 2013.
Lower half of a sextupole yoke

## Slide 17: 3 GeV ring vacuum
Detailed Design done by ALBA.
Call for tender for the 3 GeV chambers is out, offers back in mid-February
Main Technical Issues
Chamber is mostly a copper tube. SS/Al needed at some locations.
High Heat load from IDs.
Tight mechanical tolerances – minimize BPM motion.
NEG Coating (small apertures)
Magnet aperture = 25 mm
Section length = 22 m
Notes: Collaboration established with CERN to develop the coating procedure for the more complex chambers (VC1, VC2).
Prototype work going on at CERN.

## Slide 18: 3 GeV ring typical chamber

## Slide 19: Outline
Overview
Project status
Storage ring status/updates
  Magnets
  Pulsed multipole injection
  Vacuum
Injector status/updates
  Electron guns

## Slide 20: 3 GeV Ring Vacuum System

## Slide 21: Vacuum System Design 3 GeV Ring
First Version of CFT drawings and specification documents delivered by ALBA July 2011. Version 2.0 ready October 2011:
    Stainless steel chambers in existing correctors replaced with copper.
    Simplified cooling circuits.
    Simplified Geometry for VC1, use regular OFHC copper, rather than glidcop – reduced heat load from insertion devices.
    New weak fast correctors added.
    Detailed design for chamber supports and cooling tubes – integration with magnet blocks cross-checked.

## Slide 22: Steel to Copper: Why ?
Simplifies construction – reduce the need for joining dissimilar materials (brazing).
Simplifies cooling circuits.
Eliminates or reduces the need for chamber tapers to protect the stainless steel parts from incidence of synchrotron radiation
Reduces risks in NEG coating: if a brazed piece has coating problems (peel off) it cannot be recoated – the cleaning will attack the braze and the whole piece may need to be scrapped.
But, …. this means that fast orbit correction has to be done with other correctors (see later)

## Slide 23: VC1
A
B
C
D
E
F
VC1injection: (3.01VC1)
Keyhole apertures in first part
See VC10injection and Injection path in M1
(slides 15-16)
Heat absorber E simplified for less SR?
(Aperture the same for emittance measurement if dipole kicker goes out)
From left to right:
  Stand alone BPM; will be moved/prolonged with a 43 mm neck and flange for fast corrector
  Flange with bellows
  Copper part
  Copper tube
  Heat absorber for 6 kW, will be simplified to 1 kW for Wiggler, Helical 220 W
  Stainless pipe welded to BPM shaped for extraction of ID radiation
M1

## Slide 24: New Heat Load Limits from IDs

## Slide 25: VC5
A
B
C
D
E
From left to right:
  Stand alone BPM
  Flange with bellows
  Copper tube, taper removed
  Corrector copper and cooled
H
F
G
  Copper tube, taper removed
  Corrector copper and cooled
  Copper tube
  Flange with bellows
U3

## Slide 26: Vacuum System Procurement
Prequalification Tender published. 7 Companies selected.
CFT for main chambers by the end of 2011.
CERN collaboration established:
    Development of coating procedure for special chambers.
    Certification of cleaning at manufacturing companies.
    Training. (Max lab staff at CERN for about 9 months from November)

## Slide 27: Status Manufacturing
  Final Manufacturing Drawings (Yokes) released.
    Changes to corrector magnets (steel rather than ferrite) – new weak correctors to be designed.
    Changes to yoke due to integration of vacuum chambers (chamber supports, cooling tubes)
    Many smaller corrections to drawings.
  Prequalification Tender for Magnet Power Suplies published September.

## Slide 28: Prototype 3 GeV Ring Magnet Block
Several Magnets Machined out of a Single Solid Iron Block

## Slide 29: mc prototype measurements
No showstoppers in machining of large yoke block halves
Practical feedback to mechanical design/drawings
Field strengths, temperature rises, etc verified
Dipole field shape close to spec
Pole face strips gives 4% gradient adjustment, but also produces a dipole component.
QFend and 8poles – no surprises
No cross talk, except QDend(DIPm) .

## Slide 30: Example Measurements
MAC Meeting May 2011
Mechanical Measurement – Bottom yoke
Dipole Field Map
Cross-Talk
Pole Face Strips

## Slide 31: Magnet Prototype Measurements
Mechanical Measurements: Mid-plane flatness, Guiding Surfaces, pole profile

## Slide 32: Magnet Prototype Measurements
Mechanical Measurements – Dipole gap

## Slide 33: Magnet Prototype Measurements
Dipole Field Map

## Slide 34: Magnet Prototype Measurements
Dipole Field Map: Slice by Slice Analysis
Dipole Component
Quadrupole Component

## Slide 35: Magnetic Prototype Measurements
Pole Face Strips
Allow trimming pf quadrupole field, but also produces a dipole component
Changed scheme for ID compensation

## Slide 36: Magnet Prototype Measurements
Cross Talk: Effect of Dipole on Qdend. Hall Probe Measurements

## Slide 37: Magnet Prototype Measurements
Ramping Studies. Hall Probe meas. of Qfend at different ramping speeds

## Slide 38: Magnet Prototype Measurements
Cross Talk: Effect of Dipole on Qdend : Rotating Coil Measurement

## Slide 39: RF Systems, storage rings
Main Cavities (100 MHz Capacity loaded, MAX-lab design):
Contract Signed with RI in Feb 2011
Cavity Design Review Meeting June.
Pre-series cavity delivery : April 2012.
120 kW Power couplers ordered.
First delivery: April 2012.
Design Issues
RF
Thermal
EB welding
Tuning mechanism
RF
Thermal
Tuning plate
Tuning Mechanism

## Slide 40: Pre-series Cavity
Mantle brazing finished
EB welding of end pieces by the end of March

## Slide 41: RF System – Harmonic Cavity
Prototype Landau Cavity finished testing with beam in MAX III
RI will manufacture the Landau cavities for both rings
Minor design changes due to MAX III testing

## Slide 42
RF Systems: Low Level RF
Design by A.Solom
Prototype Assembled and Tested at MAX-lab
First Successful tests with Beam at MAX-III in
September 2011.
200 mA ramped with voltage and frequency loops engaged.

## Slide 43: RF Systems: LLRF Test Results

## Slide 44: Orbit feedback in the 3 GeV Ring
Status:
Design change to two separate, non-overlapping actuator sets. Cost driven change driven primarily by the vacuum system.
  Slow set is 200+180 solid iron magnets based on the old design, installed over Cu vacuum chamber.
  Fast set is 80+80 weak (max. 10 µrad) “air-coil” magnets installed over existing steel chambers at ion pumps and BPMs
Dual global controller solution based on the SOLEIL implementation [1].
New design evaluated in SimuLink/MATLAB model:
  It is stable with no “fights” between the controllers
  It meets the 200 nm stability requirement on the long straights, assuming a noise spectrum equal to that in the MAX II hall.
[1] N. Hubert et al., “Global orbit feedback systems down to DC using fast and slow correctors”, DIPAC’09, Basel, Switzerland, May 2009, MOOC01.

## Slide 45: VC2: Positions for fast correctors
From left to right:
  Flange; no bellows
  Copper tube with ∞-profile
  Stainless section with ports for pumping and crotch absorber (pump center at 835mm) Fast corrector added at exit on OD 27 mm stainless pipe
  Manual gate valve for service
  Heat absorber 1 kW
  Bellows
  Photon pipe towards HA1
  Copper tube ended with bellows and flange
A
B
C
D
H
G
F
E
VC2injection: (3.O1VC2)
No beam pipe out
Dipole kicker magnet in section B:
22x12 mm inner aperture
LCF40= 600, center-center to SDend 620 mm
(386-986 mm from chamber start, move pump port)
VC2emittance: (3.20VC2) See slide 5
Chamber with ports for mirror etc
Replace the pump port with a chamber with ports for a mirror, a thin heat absorber, and a port for the light.
It should be as far down as possible
No beam pipe (G)

## Slide 46: VC1: Position for fast correctors
A
B
C
D
E
F
VC1injection: (3.01VC1)
Keyhole apertures in first part
See VC10injection and Injection path in M1
(slides 15-16)
Heat absorber E simplified for less SR?
(Aperture the same for emittance measurement if dipole kicker goes out)
From left to right:
  Stand alone BPM; will be moved/prolonged with a 43 mm neck and flange for fast corrector
  Flange with bellows
  Copper part
  Copper tube
  Heat absorber for 6 kW, will be simplified to 1 kW for Wiggler, Helical 220 W
  Stainless pipe welded to BPM shaped for extraction of ID radiation
M1

## Slide 47: Orbit feedback, actuator bandwidth
Estimated actuator BW, power supplies excluded
Fast set: ~11 kHz, limited by vacuum chamber
Slow set: 30-35 Hz, limited by the solid iron core.
11 kHz is far more than needed, but power supplies are not included and will determine the final BW of the fast actuators.
30-35 Hz means the slow actuators will stay slow.
Fast set
Slow set

## Slide 48: 1.5 GeV Ring
1st iteration of 3D magnet design completed October 2011  modified optics.
2nd iteration of 3D magnet design completed early 2012
Vacuum design on-going at ALBA.
RF cavities same as for 3 GeV Ring.

## Slide 49: 1.5 GeV ring - Magnets

## Slide 50: 1.5 GeV Ring Vacuum System

## Slide 51: 1.5 GeV ring - vacuum

## Slide 52: Construction Work Geologic Properties

## Slide 53: Examples: Green Field Vibrations

## Slide 54: 3 GeV Ring Achromat Mock-Up

## Slide 55: Project Milestones

## Slide 56: Status - injector
Modulators being built by Scandinova
Acc. structures being built by RI
CFT for Magnets published
Gun test stand at MAX-lab

## Slide 57
The Max IV Injector

## Slide 58: Modular RF System

## Slide 59: New e- gun lay-out
Notes: Arrows show the evolution in time, from the current thermionic gun for MAX I/II/III injection, to photo-cathode RF gun for the MAX-lab test-FEL, to the decision to use a photo-cathode RF gun for the SPF and a thermionic RF gun with 180 degree bend and chopper for injection.
Final arrow is a “may-be”.

## Slide 60: Status - guns
SLED-driven photo-cathode gun under commissioning
First “beam” achieved
Thermionic gun in design stage
Gun test stand at MAX-lab
Gun SLED cavity

## Slide 61: Time Structure

## Slide 62: Injection studies
Injection scheme:
Single multipole kicker injection has been chosen as the standard injection scheme for both rings
Single horizontal dipole kicker in each ring will be used as injection kicker during beam commissioning
For details, see
S. C. Leemann, “Injection with a Single Dipole Kicker into the MAX IV Storage Rings”,
to be published
S. C. Leemann, “Pulsed Sextupole Injection for Sweden’s new light source MAX IV”,
to be published

## Slide 63: Injection studies

## Slide 64: Injection studies

## Slide 65: Injection studies, multipole kicker
Tracy-3 tracking results showing injection and capture in 3 GeV ring
Notes: Tracy-3 tracking

## Slide 66: Injection studies, multipole kicker
Notes: DIMAD tracking data at injection point
Gaussian particle distribution, 1000 particles with a 3 sigma cut-off
En = 10 mm mrad (corresponds to ex 1.7 nm rad)
Sigma_b = 0.1%
Beta_x = 13.286 @ injection point

## Slide 67: Injection studies, dipole kicker
Accumulation (θ = -2.3 mrad)
Emittance blow-up (εx = 60 mm mrad)
Energy spread blow-up (δ = 0.8%)
Invariant minimization (θ = -3.9 mrad)
Notes: Press the following points:
- Accumulation is possible

## Slide 68: Multipole Kicker Specification
* H. Takaki et. al, “Beam injection with a pulsed sextupole magnet in an electron storage ring”, Phys. Rev. ST Accel. Beams 13, 020705 (2010)
*
Notes: Dipole kickers will be made by Budker institute.
Contract signed with Budker
Turn-key system
Delivery during September 2013
Multipole kickers will be handled under a framework agreement with Synchrotron SOLEIL
Swedish government pay the French government some money and we may use this for the PSM development/manufacturing
Looking into collaboration with SOLEIL as there is common interest in the turn-key multipole kicker system
What should I emphasize?

## Slide 69: Dipole kicker specifications
Dipole Kickers | Integrated Field [1E-4 T.m] | Tot. length (flange to flange) [cm] | Pulse Duration [µs] | maximum rep. rate [Hz] | Horizontal Full Beam Stay-Clear [mm] | Vertical Full Beam Stay-Clear [mm]
Injection Kickers |  |  |  |  |  | 
3 GeV Ring Dipole Injection Kicker | 430 | 35 | 3.5 | 10 | 47.5 | 16.5
1.5 GeV Ring Dipole Injection Kicker | 150 | 45 | 0.64 | 10 | 48 | 15
Diagnostic Pinger Magnets |  |  |  |  |  | 
3 GeV Ring Vertical Pinger | 110 | 20 | 3.5 | 1 | 22 | 22
1.5 GeV Ring Vertical Pinger | 70 | 20 | 0.64 | 1 | 40 | 20

## Slide 70: Thank You!

## Slide 71: Collective Instability
Single Bunch
Microwave Instability
Transverse Mode Coupling
Multi-Bunch
Transverse multi-bunch instability driven by RW.
Coupled Bunch Instabilities driven by HOM.
Impedance Modeling (Gdifdl + modeling for tracking)

## Slide 72: 3 GeV Ring Collective Effects
Impedance of additional vacuum chamber elements calculated (T.Günzel, ALBA)

## Slide 73: Collective Effects in 3 GeV Ring
Studies of RW (freq. domain) by R.Nagaoka (SOLEIL) now including BB impedance (fr=22 GHz).

## Slide 74: Collective Effects in 3 GeV RIng
HC OFF
HC ON
Calculations by Ryutaro Nagaoka (SOLEIL)

## Slide 75: Project Critical Path

## Slide 76: Milestones – 3 GeV Ring Magnets

## Slide 77: Milestones - 3 GeV Ring Vacuum System

## Slide 78: Milestones - 3 GeV Ring RF System

## Slide 80: Collective Effects in the 3 GeV Ring: Study Plan
Study Program on Collective Effects in the 3 GeV ring has been initiated:
Purpose: Extend the work reported on the DDR, in order to check that achieving stable operation at 500 mA is indeed feasible.
This program is a joint effort of MAX-lab staff and Ryutaro Nagaoka (SOLEIL) and Thomas Günzel (ALBA).
A presentation this afternoon will highlight preliminary results of that program.