## Slide 1
Staged Eigen-Emittance Reduction Techniques
Operated by Los Alamos National Security, LLC,
for the U.S. Department of Energy
Kip Bishofberger, Micha Ben-Naim, Bruce Carlsten,
Leanne Duffy, Rod McCrady, Nikolai Yampolsky
Los Alamos National Laboratory
Notes: 1
MaRIE = Matter Radiation Interactions and Extremes, a la Ms. Curie

## Slide 2: Eigen-emittances: Achieving 10e10 photons at 42 keV
 | UNIT | LCLS | MARIE 1.0 baseline
Wavelength | Å | 1.5 | 0.293
Beam energy | GeV | 14.35 | 12.0
Bunch charge | pC | 250* | 100 (250)
Pulse length (FWHM) | fs | 80* | 30 (75)
Peak current | kA | 3.0* | 3.4
Normalized rms emittance | mm-mrad | 0.3-0.4 | 0.2 (0.1)
Energy spread | % | 0.01 | 0.01
Undulator period | cm | 3 | 1.86
Peak magnetic field | T | 1.25 | 0.70
Undulator parameter, aw |  | 2.48 | 0.86
Gain length, 1D (3D) | m | (3.3)* | (6.0)
Saturation length | m | 65 | 80
Peak power at fundamental | GW | 30* | 8 (17.6)
Pulse energy | mJ | 2.5* | 0.24 (2.4)
# of photons at fundamental |  | 2 x 1012* | 2x1010 (2x1011)
*Y. Ding, HBEB, 11/09
Normalized emittance | PITZ photoinjector | REDUCTION TECHNIQUES
0.1 mm | 25 pC | 250 pC
0.2 mm | 100 pC | 1 nC
PITZ photoinjector scaling:
Notes: 2

## Slide 3: Eigen-emittances: Two new concepts
  With the common discussion of highly-correlated beams, the term eigen-emittance has emerged to define the emittances of a particle distribution once all correlations are removed.
  It has been shown that the eigen-emittances are constants of linear, symplectic (Hamiltonian) transforms. The FBT is a perfect example of a beam with unique eigen-emittances, then removing correlations so the observed emittances equal the eigen-emittances.
  In addition, non-symplectic transforms are our method to change eigen-emittances.
symplectic
non-symplectic
conventional
beamline
elements
FBT (14x),
wedge foil,
ISR, etc?
Our motto: “Create a correlation non-symplecticly; then remove it symplecticly.”
Notes: 3

## Slide 4: Initial Emittance Partitioning: Flat-Beam Transformer
Start with 250 pC round beam at cathode (0.35/0.35/4 mm)
FBT in the usual way gives 1.2, 0.1, 4 um emittances
Our motto: “Create a correlation non-symplecticly; then remove it symplecticly.”
Notes: 4

## Slide 5: Initial Emittance partitioning: x-z, x-y Correlations
In order to reduce two eigen-emittances, two associated correlations must be generated non-symplecticly. Along with an FBT, hitting the cathode with the laser at an oblique angle generates a strong x-z correlation. Alternatively, a highly elliptical cathode (x-y correlation) with a tilted laser pulse is a possibility.
A major concern with all initial correlations is nonlinear forces before the beam is accelerated. Emittance dilution will impair the extreme emittance MaRIE requires.
Notes: 5

## Slide 6: Second-stage XZ-FBT: Canted Wiggler
  Being a non-collective phenomenon, ISR acts as a non-symplectic transformation. By varying the magnetic field across the horizontal dimension of the the undulator, different electrons lose differing amounts of energy, generating the x-pz correlation.
E in [GeV]
ΔE in [eV]
otherwise [mks]
  Our motto: “Create a correlation non-symplecticly; then remove it symplecticly.”
  We believe a canted-wiggler is the most promising approach to an XZ-FBT.
  With an intrinsic energy spread of a few keV, a 10-GeV beam only demands a 1E-4 energy slew. A 100-keV variation, using a 1-T undulator, requires 5 meters of length.
Notes: 6

## Slide 7: Second-stage XZ-FBT: Wedge-shaped foil
  A second approach to generating a proper x-pz correlation is a wedge-shaped foil that the beam passes through. One side of the beam loses more energy than the other side. However, the foil also scatters particles, creating an additional uncorrelated spread δind.
E in [GeV]
ΔE in [eV]
otherwise [mks]
  Our motto: “Create a correlation non-symplecticly; then remove it symplecticly.”
  While not as ideal as a canted wiggler, this setup is easier for demonstration purposes. In addition, at lower energies, the canted wiggler’s length becomes extremely large.
Notes: 7

## Slide 8: Second-stage XZ-FBT: Asymmetric chicane
  Both the canted-wiggler and wedge-foil techniques are non-symplectic methods to alter the beam’s eigen-emittances. In order to remove the correlations (symplectically), we can use a dogleg.
  An asymmetric chicane can also be used, and keeps the beam on the same trajectory (making it adjustable as well).
Notes: 8

## Slide 9: Simulation results: Wedge-shaped foil
  Using G4Beamline (Geant4), scattering and energy loss through the foil can be simulated. The following shows particle plots at 1 GeV:
  Due to the large energy distribution, it is necessary to collimate the remaining particles.
  The effectiveness of this technique increases with the severity of the collimation. Therefore starting with 1 nC to 5 nC, and collimating to 250 pC are considered for the wedge approach.
Notes: 9

## Slide 10: Simulation results: Wedge-shaped foil
  Similar results are shown for 100 MeV:
  At both energies, emittances of roughly 0.23 μm are achievable.
  Due to the simplicity of a wedge-shaped foil, we have proposed a number of demonstration options/collaborations: LANL NCRF injector, LANSCE, Fermilab, SLAC.
Notes: 10

## Slide 11: Demonstration option: Protons at LANSCE
  Simulation results for pushing 800-MeV protons through a foil are being performed (McCrady). With good emittance-reduction options being simulated, a possible demonstration is being considered in FY13.
  This would be the first demonstration of an XZ-FBT. Other experiments of a combined FBT/XZ-FBT beamline would be pursued elsewhere.
Chart: emittance vs x-window
| 99.0 | 99.0 | 99.0 | 99.0 | 98.0 | 98.0 | 98.0 | 97.0 | 96.0 | 95.0 | 93.0 | 91.0 | 88.0 | 84.0 | 79.0 | 73.0 | 65.0 | 56.0 | 45.0 | 34.0 | 21.0
At focus | 0.46576 | 0.46289 | 0.45888 | 0.45568 | 0.45092 | 0.44595 | 0.44037 | 0.43314 | 0.42181 | 0.40962 | 0.39414 | 0.37471 | 0.35339 | 0.32757 | 0.30147 | 0.26973 | 0.23416 | 0.19536 | 0.15449 | 0.11428 | 0.070601
Initial | 0.31178 | 0.30435 | 0.29638 | 0.28736 | 0.27534 | 0.26529 | 0.25468 | 0.24326 | 0.23045 | 0.21838 | 0.20643 | 0.19305 | 0.1788 | 0.1641 | 0.14879 | 0.13414 | 0.11902 | 0.10321 | 0.086721 | 0.07188 | 0.055027
no energy spread
1e-3 energy spread
2e-3 energy slew (not enough)
Notes: 11

## Slide 12: Summary
  Several options exist for production of a 0.1-µm-emittance beam at significant charge (250 pC) for future XFEL applications.
  It is possible that future photoinjectors possess this capability with built-in correlations.
  It is more attractive to have adjustable, staged FBT and XZ-FBT emittance reduction options. The XZ-FBT stage has yet to be demonstrated.
  Canted wigglers appear far superior to wedge-foil approaches. At high energies, the wiggler dimensions are not unrealistic.
  In the meantime, demonstrations of XZ-FBTs, using a foil at low energies, is an active pursuit of our group.
Notes: 12

## Slide 13
Notes: 13