## Slide 1
J. Teichert, A. Arnold, U. Lehnert, P. Michel, P. Murcek, R. Xiang (HZDR)
R. Barday, T. Kamps, S. Schubert (HZB)
Unwanted Beam Observations
at ELBE
FLS2012 ICFA Workshop on Future Light Sources
March 5-9, 2012, Thomas Jefferson Lab, Newport News, VA

## Slide 2
INTRODUCTION – SRF gun for the ELBE CW Accelerator
Application
high peak current operation for CW-IR-FELs with 13 MHz, 80 pC
high bunch charge (1 nC), low rep-rate (<1 MHz) for pulsed neutron and positron beam production (ToF experiments)
low emittance, medium charge (100 pC) with short pulses for THz-radiation and x-rays by inverse Compton backscattering
Design
medium average current:
1 - 2 mA (< 10 mA)
high rep-rate:
500 kHz, 13 MHz and higher
low and high bunch charge:
80 pC - 1 nC
low transverse emittance:
1 - 3 mm mrad
high energy:
≤ 9 MeV, 3½ cells (stand alone)
highly compatible with ELBE cryomodule (LLRF, high power RF, RF couplers, etc.)
LN2-cooled, exchangeable high-QE photo cathode

## Slide 3
INTRODUCTION – Unwanted beam
Unwanted beam …particles produced and accelerated with wrong properties
in space and time …
produces beam loss that increases radiation level and activation
(at ELBE permission is 1% beam loss of 1 mA = 10 µA)
causes acute or chronic damage of accelerator components
(experience is <~ 1 µA preventing long-term damage)
produces additional background for users
Superconducting RF Photo electron gun:
Cavity & cathode: dark current, discharges …
Laser: halos from scattered light, energy tails, parasitic pulses …
RF: microphonics, phase and amplitude instabilities …
beam: wake fields, resonant HOM excitation …

## Slide 4
INTRODUCTION – Unwanted beam
Compton backscattering experiment at ELBE with SRF Gun
e-beam: 25 MeV, 10 … 50 pC @ 10 Hz (rep. rate of TW laser)
RF of gun & ELBE modules in CW
The SRF gun produces a lot of dark current, similar to normal conducting RF photo guns
The dark current has similar properties as the beam. A large fraction was accelerated
and transported to the user station without further losses.
nearly the same dark current as in the Fcup near gun

## Slide 5
DARK CURRENT – Cavity field
field profile on axis
stored energy U | 32.5 J
quality factor Q0 | 1010
dissipated power Pc | 25.8 W
maximum beam power PB | 9.4 kW
geometry factor G | 241.9 Ω
accel. voltage Vacc accel. gradient Eacc | 9.4 MV 18.8 MV/m
Ra/Q0 | 166.6 Ω
Epeak/Eacc | 2.66
Bpeak/Eacc | 6.1 mT/(MV/m)

## Slide 6
gun operation mode | CW | pulsed RF
acceleration gradient | 6.0 MV/m | 8 MV/m
electron kinetic energy | 3 MeV | 4 MeV
peak field on axis | 16.5 MV/m | 21.5 MV/m
peak field at cathode (2.5 mm retracted) | 6.5 MV/m | 8.4 MV/m
cathode field at launch phase (10°) | 1.1 MV/m | 1.5 MV/m
cathode field at 10° and -5 kV bias | 2.2 MV/m | 2.6 MV/m
cathode field at 90° and -5 kV bias | 7.6 MV/m | 9.5 MV/m
40% at cathode
DARK CURRENT – Cavity field
80% at edge
cathode
110% at iris
Important for emitted dark current:
cathode surface field is ~ 40 % of peak field
field at cathode hole edge is ~ 80 % of peak field
without field enhancement (scratch in our cavity)
40% at cathode
field profile on axis
surface electric field

## Slide 7
DARK CURRENT – Measurement
Dark current in Faraday cup (~1.5 m from cathode) versus gradient for different cathodes
about 20 % dark current from cathode,
80% from cavity (scratch)
only cathodes with CsTe layer have dark current,
exception: #060410Mo, but without direct comparison

## Slide 8
DARK CURRENT – Properties
dark current
30 pC beam (Ekin= 2.8 MeV)
100 keV
100 keV
Measurement of kinetic energy and energy width of dark current and comparison
with low-bunch-charge beam – 180° bending magnet in diagnostic beamline
largest fraction has nearly beam energy (emission from backplane near cathode)
small fraction with lower energy (other high-field iris regions in cavity)
parameters:
6 MV/m CW, 5 kV DC bias
120 nA dark current,
1.5 µA @ 50 kHz beam

## Slide 9
DARK CURRENT – Fowler Nordheim analysis
Fowler Nordheim formula for tunneling (field emission) current:
with AFN=1.54 x 106 , BFN=6.83 x 103 , electric field E in MV/m, work function ϕ in eV,
is the field enhancement factor, A the emission area. (see book of H. Padamsee, J. Knobloch, T. Hays)
Time averaging for a RF field yields:
(J.W. Wang and G.A. Loew, SLAC-PUB-7684 October 1997)
ϕ = 4.3 eV (Nb)
= 591
A = 0.63 nm2

## Slide 10
Maximum (pulsed):
Eacc = 8 MV/m
Epeak = 21.5 MV/m
Maximum for operation
Eacc = 16 MV/m
Epeak = 43 MV/m
DARK CURRENT – Cavities with higher gradients
existing cavity at ELBE with high field emission
new cavity

## Slide 11
DARK CURRENT – Cavities with higher gradients
Extrapolation of Fowler Nordheim results for new cavity:
New cavity will be operated at the high-field limit of 16 MV/m. Here we
expect the same field emission level as for 8 MV/m for the old cavity (blue curve)
-> smaller field enhancement factor (= 591)
FN fit for 20 % of current emitted from cathode (ϕ = 4.3 eV for Cs2Te, 40% peak field)
and extrapolation to 16 MV/m (read curve) gives 40 µA cathode dark current

## Slide 12
DARK CURRENT – suppression for low rep. rate at ELBE
Compton backscattering experiment
For higher rep. rates and CW the dark current kicker is a great technical challenge,
at 1.3 GHz CW (BERLinPro ERL) the kicker can not help.
100 ms
10 ms
pulsed RF
laser
bunch 100 pC
dark current at 1.3 GHz
10 ms
Qdark < Qbunch = 100 pC
Qdark =10 ms * 40 µA = 400 nC
suppression factor >104
courtesy of
F. Obier/DESY
Adaption of FLASH/DESY RF gun dark current
kicker: 1 MHz sine amplitude, stripeline,
pulsed-mode operation,
Eventually upgrate to CW would allow
application for 500 kHz high-charge mode.

## Slide 13
assuming an unwanted beam of < 1 µA in CW accelerators with SRF guns
there will be a need for photo cathodes with low dark current
proper handling to prevent dust particles and damage
plug materials and roughness
photo layer properties
- roughness, homogeneity, thickness
- high work function
- crystal size and structure
- multi-layer design
- post-preparation treatment (ions, heating)
- pre-conditioning
DARK CURRENT – fighting against it sources

## Slide 14
Acknowledgement
We acknowledge the support of the European Community-Research Infrastructure Activity under the FP7 programme since 2009 (EuCARD, contract number 227579) as well as the support of the German Federal Ministry of Education and Research grant 05 ES4BR1/8.
THANK YOU FOR ATTENTION