## Slide 1: X-ray light source by inverse Compton scattering of CSR
FLS2012
2012. Mar. 6
Miho Shimada
High Energy Research Accelerator Organization, KEK

## Slide 2: Inverse Compton scattering of CSR（CSR-ICS）
Head-on collision
M. Shimada and R. Hajima, PRSTAB 13, 100701,(2010)
Hard X-ray and gamma-ray of laser Compton scattering
is planned at the Compact ERL.
CSR - ICS
laser- ICS
Photon energy due to inverse Compton scattering
CSR-ICS is proposed as a soft X-ray light source at the compact ERL.
CSR is reflected at a mirror and
collides with the following electron bunch.

## Slide 3: CSR-ICS at the Compact ERL
X-ray expected by the inverse Compton scattering of cERL
Corurtesy S. Adachi
This area is expected at the cERL

## Slide 4: Comparison CSR-ICS with conventional ICS
 | Laser-ICS | FEL-ICS | CSR-ICS
Equipment | External laser | Undulator | Only mirror
Synchronization | Difficult | Easy | Easy
Spot size of laser (depends on wavelength) | Smaller | Smaller | Larger
Bandwidth | Narrow | Narrow | Relatively narrow ~ white light
Electron energy | Lower | Lower | Higher
Bunch compression | Difficult | Difficult | Easy
Emittance | Larger | Larger | Smaller

## Slide 5: Proposals of the ICS of CSR and CDR
N. Sei and T. Takahashi, APEX 3, 052401,(2010)
N. Sei et al, APEX 1, 087003,(2008)
A. P. Porylitsyn et al, PRE 60, 2272,(1999)
It’s proposed as a real time THz Spectroscopy.
THz is converted to visible region.
Flux is very small.
A. Aryshev et al, IPAC’10, 196,(2010)
ICS of Coherent Diffraction Radiation
Compact X-ray light source.

## Slide 6: Optics 1: Magic mirror scheme for white light source I
Electron Beam 200 MeV, 77 pC
Acceptance angle of magic mirror
300 mrad [H] x 20 mrad [V]
Transverse electron beam size
70 um [H] x 30 um[V]
The spot size is assumed to be the same with that of the transverse beam size, which is estimated with betatron and dispersion function.
The transverse beam size is smaller than the wavelength of CSR.
S. Kimura et al, Infrared Phys. & Tech 49, 147,(2006)

## Slide 7: Magic mirror scheme for white light source II
Example :
Electron charge : 77pC/bunch
Electron energy : 200 MeV,
Bunch length : 100 fs
CSR (190mm)
: 3 x 1014 phs/pulse 10%BW , 4 x 1023 phs/s 10%BW (1.3 GHz)
X-rays (4 keV)
: 5 x 103 phs/pulse 10%BW , 6 x 1012 phs/s 10%BW (1.3 GHz)
Scattered Photons
: 4 x 105 phs/pulse 100%BW, 5 x 1014 phs/s 100%BW (1.3 GHz)
Pulse duration : 100 fs
Pulse duration of CSR becomes longer because of narrow bandwidth.
Timing jitter should be smaller than the pulse width of CSR.
The cutoff effect is ignored..

## Slide 8: Optics 2 : Optical Cavity scheme for narrow bandwidth
Incoherent stacking because the fluctuation of longitudinal position (a few hundreds um) is larger than wavelength of CSR.
Electron bunch emits CSR inside a cavity.
Four mirrors is necessary for two focus points. One is for collection of CSR and another is collision point.
CSR - ICS
ICS by an external laser
Coherent stacking
External laser is injected from outside a cavity. It passes though a multilayered mirror with low transmittance.
Two mirrors are enough for single focus point.
E.R.Crosson et al, Rev. Sci. Instrum. 70, p.4 (1999)
In both cases, pulse power is stacked by 1000 times with reflectivity of mirrors 99.97% .
Pcav:Power in a cavity, Pin:Input power, R: Reflectance, T:Transmittance, n:Number of mirrors

## Slide 9: Timing jitter in cERL
N. Nakamura, Proceedings of IPAC 10, p.2317-2319
Shift of arrival time caused by RF amplitude error
Layout of a 1-loop ERL
Source of error | error | Jitter of arrival time
RF amplitude | 0.1 % | 400 fs
RF phase | 0.1 degree | 200 fs
Injection timing | 200 fs | 10 fs*
*jitter of arrival time is shorter than error of injection time because it is compensated by the error of RF phase.

## Slide 10: Wavelength of CSR for pulse stacking in an optical cavity
Wavelength of CSR stacked in an optical cavity is chose as follows,
Total radiation power : P(k)
Incoherent
Coherent
P(k) : Total radiation power
N : Number of electron
p(k) : Radiation power per an electron
r(z) : Longitudinal electron density distribution
F(k) : Form factor
Gaussian beam with bunch length sz

## Slide 11: Mode matching
Acceptance angle is limited for Mode matching
Acceptance angle Q is determined
to satisfy the mode matching.

## Slide 12: Optimization of collision area : 1
In the case of bandwidth Δλ/λ, pulse duration of CSR is lengthened by a factor 1/(Δλ/λ).
Half cycle of CSR is destroyed by an narrow band mirror.

## Slide 13: Optimization of collision area : 2
CSR in optical cavity is assumed to be Gaussian beam.
Hour glass effect is considered at the collision.
zR < λNc, Nxis independent to zR.
Beam size w(z) of Gaussian beam
Small zR :
small spot size is easy to spread
The Rayleigh length is zR = λNc,
to minimize the effect of the timing jitter of electron bunches.
to avoid the non-linear effects.

## Slide 14: High reflectivity mirror
In the wavelength range of a few 10 um ～a few 100 um,
Reflectivity of metal is lower than 98 %.
It is difficult to fabricate multilayered mirror with larger than 99% reflectivity by conventional method.
M.Tecimer et al, PRSTAB 13,
030703,(2010)
Stacking up photonic crystal separated by vacuum layer.
Bandwidth is narrow at the higher order wavelength.
Wavelength, which depends on thickness of the layers, is controllable without losing the high-reflectivity.
Development of high reflectivity mirror for terahertz region

## Slide 15: X-ray at 60-200 MeV ERL
Number of photons of X-ray (b.w.10%)
  Number of photons per pulse : ~ 104-5 phs/pulse.
  Flux : ~ 1013-14 phs/s.
Energy range of X-ray
  From 0.04 to 4 keV.
  10 keV X-ray is possible at electron energy of 200 MeV and bunch length 50 fs, which is accomplished in tracking simulation.
Pulse duration of X-ray is 100 fs – 1 ps.
Electron transverse beam size is much smaller than the focus size of focused CSR.

## Slide 16: Summary
We proposed the inverse Compton scattering of CSR.
  ERL is a nice platform for both high-intensity CSR source and inverse Compton scattering.
Two optical schemes
  Magic mirror : White light with pulse duration of 100 fs.
  Optical cavity : Narrow bandwidth. Power amplification by pulse stacking is estimated almost 1000 times.
Scattered photon expected in ERL (Optical cavity)
  Generation of soft X-ray with energy range of 0.04 – 4 keV is expected at 200 MeV ERL. Pulse duration is from 100 fs to 1 ps.
  Number of photon per pulse is 104-5 phs/pulse, Flux 1013-14 phs/s.