## Slide 1: Electron Sources for ERLs – Requirements and First Ideas
Andrew Burrill FLS 2012
“The workshop is intended to discuss technologies appropriate for a next phase of photon user facilities providing high peak and average photon brightness focusing on the EUV to x ray region, especially CW machines.”
What do ERL class accelerators need from electron sources? What are the limits?
Where is overlap? Are there common issues? What direct beam sources are required in the future?

## Slide 2
Injector
+ Cathode
+ Laser
What do I consider an Electron Source for an ERL?

## Slide 3: What do ERL class accelerators need from electron sources?
What is the purpose of the ERL?
FEL Driver
Storage Ring Replacement (SRR)
R&D Tool or Proof of principle Experiment?

## Slide 4: What is the purpose of the ERL?
FEL Driver or Storage Ring Replacement (SRR)
  Must meet user requirements!
  Reliability, reproducibility, stability
  High Brightness Beams
    Short bunch, small transverse size and divergence, small and linear longitudinal emittance.
Bn
f
=
e0mc2
2p
Ecath
MTE
max
Notes: High electron beam brightness translates to high photon brightness, allows for the reduction of the size and cost of expensive X-ray FEL and ERL facilities. Minimum achievable emittance depends on charge/bunch, lower charge, lower emittance. From this workshop a common set of measurement criteria needs to be defined!!!

## Slide 5: What is the purpose of the ERL?
R&D Tool or Proof of principle Experiment?
  Clearly defined deliverables
  Must deliver meaningful results while meeting schedule and budget constraints!
  Obligation to push the state of the art
    Reliability can be relaxed (not a user facility)
    Great opportunity to investigate entire possible operating regime of the machine
    Perfect time to collaborate!
Notes: Since this is a workshop we should strive to identify current outstanding issues that need to be addressed and/or studied and make sure as a community we are working to do so.

## Slide 6
Operational ERLs +1 | Gun | Cathode | Laser λ (nm) | Avg Current | Charge per bunch | Bunch Length | Rep Rate | Norm Emitt. (mm*mrad) | Energy at Gun Exit
JLab FEL | DC | GaAs | 523 | 10 mA | 135 pC | 3.4 ps | 75 MHz | 8 | 350 keV
Daresbury | DC | GaAs | 532 | 13 uA | 80 pC | 7 ps | 81.25 MHz1 | 2 | 230 keV
BINP | DC | Thermionic | N.A. | 30 mA | 2.5 nC | 1.1 ns/ 100 ps | 22.5 MHz | 30 | 300 keV
HZDR | SRF | Cs2Te | 266 | 1 mA | 77 pC | 4 ps | 13 MHz | 2 | 4 MeV
ERLs under Construction (hopefully) |  |  |  |  |  |  |  |  | 
BNL | SRF | CsK2Sb | 355 | 50 mA | 5 nC | 70 ps | 10 MHz | 9.2 | 2.5 MeV
Cornell | DC | GaAs/ CsK2Sb | 520 | 100 mA (52 mA) | 77 pC | 2 ps | 1300 MHz | 0.8 | 500 keV
HZB | SRF | CsK2Sb | 526 | 100 mA | 77 pC | 2 ps | 1300 MHz | <1 | 1.5-2 MeV
PKU | DC/ SRF | Cs2Te | 266 | 1-5 mA | 60 pC | 3 ps | 81.25 MHz | 1.2 | 3-5 MeV
JAEA/KEK | DC | GaAs | 530 | 100 mA | 77 pC | 20 ps | 1300 MHz | 1 | 550 keV

## Slide 7: Injector / Cathode 0pportunities to address for FLS
Opportunity | DC Gun | SRF Gun | Hybrid (DC/SRF) | NCRF Gun
HV Insulator Development | X |  | X | 
Vacuum condition for high QE cathodes (10-11 Torr or better) | X | ? | ? | X
Ion back bombardment mitigation | X | ? | X | X
Cavity recovery procedure following a “catastrophic event” | X | X | X | X
Zero reduction in cavity/cathode performance when cathode is installed | X | X | ? | ?
Cathode longevity study at >50 mA for >168 hours | X | X | X | X
Demonstration of 100 mA sustained operation providing high brightness beam | X | X | X | X

## Slide 8: Laser Opportunities
Stability & Reproducibility
Power handling capabilities of components
  100 mA machines will be punishing
Flexibility
  Variable repetition rate ( single shot – CW)
  Variable pulse structure
  Pulse shaping – spatial, temporal
Beam quality preservation for laser room to gun
  Optical transport is critical
  Final mirror, especially if located in vacuum, is critical
Reflected light from the cathode must be addressed

## Slide 9: So what are the requirements for an ERL electron source?
Deliver high brightness beams to users
Capable of c.w. operation
DC gun or RF gun 700 MHz – 1.5 GHz
Highly flexible (single shot – c.w.)
10-100 mA
77 pc – >1 nC charge/bunch
100 fs – 20 ps pulse length
It must work all the time!

## Slide 10: What Needs to be clarified
Common defintions need to be used when talking about injector performance, irrespective of the choice of gun technology!
  Brightness
  Emittance (100%, 90%, 0%)
  Cathode Lifetime
  Maximum sustained current (1 hour, 1 day?)
  Maximum charge extracted

## Slide 11: Final Thoughts
Collaborations that are on-going are providing good data that would not necessarily be possible on our own.
Injectors can not be designed to operate reliably at the maximum gradient they can achieve in a vertical test!
Thank you! Thank you to the presenters from ERL 2011 for some of the material used in this talk.