## Slide 1: Progress in CW-Timing Distribution for Future Light Sources
Russell Wilcox, Gang Huang,
Larry Doolittle, John Byrd
ICFA Workshop on Future light sources
March 7,2012

## Slide 2: Outline
How the CW/RF system works
Timing requirements for NGLS
CW systems running and developing
Conclusions

## Slide 3: One timing channel
Note: this is a synchronizer/controller, not just an RF clock delivery system
When controlling a low noise VCO, it contributes <10fs RMS (200m, 20 hours to 2kHz [loop BW])
Rb
lock
0.01C
AM
CW
laser
0.01C
FS
RF phase
detect,
correct
optical
delay
sensing
FRM
FRM
fiber 1
fiber 2
d1
d2
wFS
wRF
transmitter
receiver
Laser or klystron

## Slide 4: Information flow in the receiver
All implemented digitally on an FPGA
Phase sensitivity <0.01º, thus 10fs for 3GHz
FS
PI
PI
phase
shifter,
VCO
or
laser
optical
delay
correction
RF
delay
correction
signal
calibration
reference
calibration
reference
sig - ref
interferometer
error
transmission
fiber
light
phase information
group/phase
factor

## Slide 5: Next Generation Light Source
High repetition rate electron source
CW SC linac
Output photon properties
  100kHz FEL (seed and experiment lasers, diagnostics)
  Wavelength: 1 to 4nm
  Pulse width 200fs to 200as

## Slide 6: Jitter Tolerances Estimated (CD0 Design)
CD0 Jitter Tols:
1.8 GeV,
300 pC,
One BC only,
Gaussian input,
70-MeV start
“10/25/11” better?
3.9
CM1
CM2
CM3
CM9
CM10
CM30
BC1
168 MeV
R56 = 75 mm
BC2
640 MeV
R56 = 48 mm
GUN
1 MeV
Heater
70 MeV
R56 = 4 mm
L0
j = ?
Ipk = 60 A
L1
j = -28°
Ipk = 120 A
Lh
j = 180°
L2
j = -31°
Ipk = ?
L3
j = +18°
Ipk = 600 A
SPRDR
2.4 GeV
R56 = 0
L0 RF Phase: 0.050°
L1 RF Phase: 0.010°
Lh RF Phase: 0.100°
L2 RF Phase: 0.010°
L3 RF Phase: 0.010°
L0 RF Voltage 0.010%
L1 RF Voltage 0.010%
Lh RF Voltage 0.010%
L2 RF Voltage 0.010%
L3 RF Voltage 0.010%
Gun Timing: 0.1ps
Bunch Charge: 2.0%
Heater R56: 1%
BC1 R56: 0.005%
SPRDR 10fs
670 m
to spreader end

## Slide 7
3.9
CM1
CM2
CM3
CM9
CM10
CM30
BC1
168 MeV
BC2
640 MeV
GUN
1 MeV
Heater
70 MeV
L0
L1
Lh
L2
L3
SPREADER
2.4 GeV
Stabilized clock reference distribution - <10 fsec
RF Control – 0.01%,0.01 deg at 1.3 GHz
Beam-based Feedback
ΔE
Δστ
SP
ΔE
Δστ
SP
Δt
ΔEτ
SP
Optical synchronization between arrival time and user lasers- ~1 fsec
Master
BAT
User laser
NGLS timing system overall

## Slide 8: High reprate enables better sync
Faster “beam-based” feedback
  Error terms are correctable up to ~100kHz with 1 MHz sampling
Faster averaging for slow but precise drift
  Keep as precision for long term

## Slide 9: An integrated timing approach
Control lasers to minimize high frequency jitter
Use final cross-correlator to correct for FEL and thermal slow drift
TX
modelocked
oscillator
power
amplifier
FEL
experiment
clock transmitter
modulator
seed lasers
experiment
lasers

## Slide 10: X-ray/optical cross-correlator example
Optically streaked photoelectron spectra
  From A. R. Maier, FEL 2011
  New J. Phys 13, 093024 (2011) (similar, longer pulse)
Runs next to experiment, but with special laser

## Slide 11: Existing and developing CW systems
  Existing FERMI@ELETTRA LLRF system
  Existing LCLS user laser timing
  Developing SPX SCRF and user laser timing
  Developing 1fs sync in lab

## Slide 12: Fermi@Elettra RF timing configuration
11 links now used (?), 32 possible
  Separate 3GHz system being replaced channel by channel

## Slide 13: The Fermi transmitter is compact
Transmitter rack
sender
Sync head In
accelerator
tunnel

## Slide 14: Fermi@Elettra results
Initial out-of-loop test showed 87fs RMS for controlling cavity
Final arrival time jitter due to many sync channels, may average
Electron bunch arrival time measurement
Drive KLY3 unstable
Mario. Ferianis, FEL 2011
All-optical femtosecond timing system for the Fermi@Elettra FEL

## Slide 15: LCLS laser timing configuration
System has 16 channel capability, 6 used
Typical 300m fibers, 10ps correction (thermal)
linac
undulator
bunch
arrival
monitor
AMO
SXR
XPP
CXI
NEH
laser
room
timing
TX
laser
laser
laser
laser
MEC
laser

## Slide 16: 16 channel transmitter fits in a rack
Transmitter is simple
  All smarts are in RX
“Sender” has only EDFA, local ref arms
Amplifier and splitter (“sender”)
Modulator
Wavelength locker
CW laser

## Slide 17: In-loop LCLS jitter
When controlling a nice RF phase shifter, performance is better than with lasers
In-loop laser jitter a good indication of experimental jitter
125kHz BW (gray): 120fs RMS
1kHz BW (black): 25fs RMS
125kHz BW (gray): 31fs RMS
1kHz BW (black): 8fs RMS
Phase shifter loop (reference)
Laser loop (to experiment)

## Slide 18: LCLS experimental (out-of-loop) jitter
Variability probably due to readjustment of laser
120fs RMS
J. M. Glownia et al, Opt. Exp. 18, 17620 (2011)
delay, fs
Andreas Maier, at SLAC Oct. 2011,
also New J. Phys. 13, 093024 (2011)
60fs RMS
Optically streaked photoelectrons from Ne
Ionization of N2

## Slide 19: SPX at APS proposed configuration
F. Lenkszus, “Phase Reference Distribution for SPX – Notes for Discussion”, APS Internal
Note, Jan 2011.

## Slide 20: Current SPX LLRF system results

## Slide 21: Some conclusions from experience
Failures, out-of-spec performance due to ancillary systems
A good interface is essential
Most jitter due to laser (LCLS)

## Slide 22: LCLS user and maintenance interfaces
Prevent failures due to operator error
Enable quick parameter check for maintenance

## Slide 23: Our laser jitter studies at LCLS
Single side band phase noise measurement
At the ~2kHz resonance, gain <1 to avoid oscillation
This limits noise suppression at lower frequencies
  Where most of the jitter comes from
Look for mechanical resonances, acoustic noise
reference
free run
locked

## Slide 24: Our laser jitter studies at LBNL
Modelocked fiber laser tuned with piezo mirror
Laser control loop pinged with step
Transfer function analyzed
Compensation added to loop gain
This should allow for higher gain, lower noise

## Slide 25: Syncing CEP-stable laser to carrier
Envelope is locked to carrier, transmit single frequency, beat with carrier to get error signal
  Wilcox et al, J. Modern Opt. 58, 1460 (2011)
Like chain and sprockets
We are using the full optical bandwidth
reprate
comb1
line
picker
line
TX
line
RX
comb2
hetero-
dyne

## Slide 26: Line picker/transmission experiment
CW
ML
÷5
interferometer
controller
+FS
-FS
FS
PI amp
VCO
stability B
100m
stability A
0.95fs RMS
(picking)
Transmission = 0.41fs RMS
(B-A)
1550nm fiber lasers
No attempt to stabilize long term

## Slide 27: Laser sync experiment with Menlo
Erbium doped fiber laser used here
By adding an EO phase modulator in the cavity, control BW can increase, cut jitter to ~1fs
Previous experiments (e.g. Opt. Lett. 28, 663 (2003)) have shown ~1fs jitter with similar schemes, Ti/Sapphire laser used here
comb1
comb2
reprate
control
cross-correlator
CW
hetero-
dyne
hetero-
dyne
Experiment done at Menlo Systems:
current piezo BW
<8fs integrated jitter
EO modulator BW

## Slide 28: Interferometer noise is small
Length sensor for our 3GHz system
Can track 10ns time shift within bandwidth
  Impervious to all but fast, hard shocks to fiber
1.4fs, unlocked
52as, locked

## Slide 29: Conclusions
We currently have two timing systems in operation in FEL facilities, and another in development for a storage ring
Using operational experience, we are both improving the existing systems and designing the next one for the NGLS
To meet new NGLS requirements, we are developing a ~1fs laser sync system