## Slide 1: The Heavy Photon Search experiment in Hall B
Takashi Maruyama SLAC
Searching for a New Gauge Boson at Jlab
September 20-21, 2010

## Slide 2
Springboard
Focus on Point B

## Slide 3
HPS HEAVY PHOTON SEARCH
A Proposal to Search for Massive Photons at Jefferson Laboratory

## Slide 4
Authors
W. Cooper, M. Demarteau Fermi National Accelerator Laboratory, Batavia, IL 60510-5011 S. Bueltmann, L. Weinstein Old Dominion University, Norfolk, VA 23529 A. Grillo University of California, Santa Cruz, CA 95064 M. Holtrop, K. Slifer, S. Phillips, E. Ebrahim University of New Hampshire, Durham, NH 03824 P. Schuster, N. Toro Perimeter Institute, Ontario, Canada N2L 2Y5
R. Essig, C. Field, M. Graham, G. Haller, R. Herbst, J. Jaros (Co-Spokesperson), C. Kenney, T. Maruyama,
K. Moffeit, T. Nelson, H. Neal, A. Odian, M. Oriunno, R. Partridge, D. Walz SLAC National Accelerator Laboratory, Menlo Park, CA 94025 S. Boyarinov, V. Burkert, A. Deur, H. Egiyan, A. Freyberger, F.-X. Girod,
V. Kubarovsky, S. Stepanyan (Co-Spokesperson) Thomas Jefferson National Accelerator Facility, Newport News, VA 23606 A. Fradi, B. Guegan, M. Guidal, S. Niccolai, S. Pisano, E. Rauly, P. Rosier and D. Sokhan Institut de Physique Nucleaire d'Orsay, 91405 Orsay, France
M. Khandaker, C. Salgado Norfolk State University, Norfolk, VA 23504 N. Dashyan, N. Gevorgyan, R. Paremuzyan, H. Voskanyan Yerevan Physics Institute, 375036 Yerevan, Armenia
M. Battaglieri, R. DeVitta INFN, Sezione di Genova, 16146 Genova, Italy

## Slide 5
Philip Schuster
Fixed Target Experiments are an Ideal Hunting Ground

## Slide 6
Philip Schuster
Unique Fixed-Target Kinematics

## Slide 7: Backgrounds
Thin target to reduce the rate
Magnetic field to remove low energy e-
Define dead zone
Multiple Coulomb scattering in the target
Secondary particle production in the target
  Bremstrahlung
  Delta-rays
Pair conversion of bremstrahlung photon
  Two step process; the rate ~(target thickness)2
Virtual photon conversion and Bethe-Heitler processes
Target thickness is 0.25% X0
  (ee) << (*ee)
A’

## Slide 8: Heavy Photon Signatures
A heavy photon appears as an e+e- resonance on a large background of QED tridents.
S/B depends on  and resolution.
The heavy photon lifetime depends on mass and . For suitable values, a secondary decay vertex can be identified, distinguishing the A’ from the trident background.
c ~ 1 mm (/10)(10-4/)2 (100 MeV/mA’)
Trident Background
A’ Signal
 2/m

## Slide 9: Present Limits
Prompt decays
cm-m decays
> m decays
Region preferred by
Astrophysics DM Models

## Slide 10: Designing a 6 GeV Fixed Target Experiment
Detecting A’ Decays needs large, forward acceptance Remember EA’  Ebeam A’  0 decay = mA’/EA’ (~200 MeV/6 GeV = 33 mrad) Accept decay /2 <  < 2 decay ( 16 mrad <  < 66 mrad )
Sensitivity to small cross-sections requires large luminosity Need Qtot ~ 1C for T=.25% X0
Manageable occupancies require high duty cycle, fast electronics. Need to spread out 1 C worth of angry electron backgrounds as much as possible. Jlab Bkg (data at 40 MHz) <<<<< SLAC Bkg (data at 100 Hz)
Good Mass and Vertex Resolution Needed for low momentum tracks  low mass, high precision detector

## Slide 11: Layout of the HPS experimental setup behind the CLAS detector in Hall B
CLAS
Quads
M1
M2
M3
ECal
Muon
M2/Tracker
W target

## Slide 12: HPS Beamline
Beam Tail ~ 10-5
Hall B Optics
Excellent beam quality, stability
10 m spots possible with additional quads
Constrains A’ decay and allows
significant background reduction
With New Quads
~40 m
~10 m

## Slide 13: HPS Concept
Thin Target Close to Tracker for vertexing
Compact Si Tracker/Vertexer in 1T dipole
Fast, segmented Ecal for triggering, e ID
Muon detector for alternate trigger, muon ID
Split detectors vertically to avoid “Dead Zone” occupied by primary beam, brem photons, etc.

## Slide 14: Set Up: Si Tracker/Vertexer (Nelson)
6 Layers of Si detectors mounted on CF modules supports, split into upper and lower planes:
Layers 1-3: VH, VH, VH Precision vertexing
Layers 4-6: VS, VS, VS
Robust track finding and
precision momentum analysis
Entire assembly in vacuum to minimize backgrounds
Rolls in/out for installation and servicing.

## Slide 15: Set Up: Electromagnetic Calorimeter (Holtrop)
Inner cal uses 1.3 cm2 PbWO4 crystals, readout with APDs, at 250 MHz
Outer cal uses 4 cm2 Pb/scint Shashlyk Towers, readout with PMTs
No crystals in “dead zone”
Beam, radiated photons, and off energy e- pass through in vacuum
PbWO4 Crystal
Shashlyk Tower

## Slide 16: HPS Trigger (Holtrop)
GEANT4 simulations are used to study trigger occupancies and rates.
High occupancies for 32ns window, 10 MeV thresholds
Manageable occupancies for 8ns window and 100 MeV thresholds
Cluster, Energy, and Geometry cuts can produce a trigger rate < 20 kHz
Background trigger rate: 17 kHz
Trigger 2 clusters 0.5 < E1,2< 4.4 GeV E1 + E2 < 5.1 GeV E < 3.2 GeV
Co-planar

## Slide 17: Set Up: Muon System (Holtrop)
Additional decay mode A’ →+- for mA’ > 200 MeV
Provides independent trigger and muon ID
Much reduced EM backgrounds
4 layers of 5 cm wide horizontal scintillator strips, readout at both ends with MAPMTs.
75 cm Fe absorber
~1% pion punchthrough
(,) vs thickness Fe

## Slide 18: DAQ (Boyarinov)
Ecal and Muon data in 250 MHz FADCs
*Crate Trigger Processors receive
signal every 16ns and perform
cluster finding
*Subsystem Processor generates final trigger decision
Tracker uses SLAC ATCA crates *APV25 signals go to Readout Boards every 25 ns
*Trigger Interface board accepts and distributes Jlab trigger
*Cluster Interconnect Module connects to Jlab DAQ
Level 1 Trigger <50 kHz
Level 3 Selection 1/10
Data Rate <100 Mbyte/s

## Slide 19
HPS Reach: Bump Hunt and Vertex Search
(Graham)
HPS 5.5 GeV
HPS 3.3 GeV
Bump hunt
Vertexing
1 month run @400nA

## Slide 20: Search for True Muonium
True muonium will decay to e+e- with m=2m, a decay length of c=14mm, and kinematics just like those of the A’ .
The production cross section is low, but within reach. The dissociation cross section is large, so most dimuons dissociate before leaving the target. For Ebeam=5.5 GeV, 400nA beams, 3 x 106 sec, expect 20 n=1 triplet states produced 2 events detected Not good enough, but within reach with longer running, higher energies, and multiple targets. Under study.
An important test of QED made more topical by recent anomalies in the muonium Lamb shift result.

## Slide 21: Conclusions
The vertexing capability has a potential of discovering heavy photon with cm ~ m decay length.
Together with bump-hunting, the A’ search can be extended into a large parameter region.
The experiment capitalizes on CEBAF’s excellent duty cycle and recent advances in very high rate detector readout technologies.

## Slide 22
Backup

## Slide 23: Hall B “Photon Dump” was also considered, but rejected.
100 nA, 6 GeV e-, post-radiator “primary beam”
Beam size  100 m
Tight ~5m space
Beam must be directed to the dump.
  Chicane magnets
Parasitic run with CLAS
Possible location for heavy photon search
Photons
Dump
Chicane
CLAS
The degraded beam compromises the physics reach.