## Slide 1: Hall A Tritium Target Status
Dave Meekins
7 December 2015

## Slide 2: Overview
Target Design
  System design
  Cell design
  Exhaust system
  Beamline
  Performance
Status
  Review Status
  Documentation
  Construction
  Timeline

## Slide 3: Information and Documentation
New wiki for the tritium target:
  https://wiki.jlab.org/jlab_tritium_target_wiki/index.php/Main_Page
  Reports: design and technical
  Drawings
  Procedures
  Calculations
  Presentations
  Review
    Presentations, Responses, Committee reports

## Slide 4: Target System
Repurposed Qweak H2 Target
Alter existing Cryostat
  Alter internal piping
  Add two valves
H2 Loop piping and cell removed
Alter cryo piping and instruments
15 K He from ESR
Motion in “X” and “Y” directions
Control system is similar to Hall A cryotarget
“New Construction” pressure system

## Slide 5: Target Ladder
Heat sink cooled by ESR to 40K
Stabilized by heater

## Slide 6: Target Cell
Main Body and Entrance Window
ASTM B209 AL 7075-T651
Valve assy:
SST 316 and 304
1090 Ci of T2 (0.1 g)
~200 psi at 295K
25 cm long
ID of 12.7mm
Volume = 34 cc
Aluminum CF seals

## Slide 7: Cell Cross Section
0.018” wall

## Slide 8: Operational Limits
Beam Current
  25 µA on all others
Raster
  2x2 mm minimum
Beam Trip limit (18000 trips)
Temperature
  Heat sink must be ~40K
Target Operator 24/7 when cold
Tritium effects access procedures and training requirements

## Slide 9: Exhaust System
36” OD 20m tall Stack
12000 cfm blower multispeed
2” pump exhaust
  Run parallel to stack
Stack must also serve as smoke removal
Provides controlled release of secondary and tertiary containment
Pump exhaust is continuous
Blower activated:
  Manual
  Interlocks

## Slide 10: Exhaust Routing

## Slide 11: Beamline Alterations
No plans to substantially alter beamline
Upstream beamline shall be isolated by a Be window
  0.008” thick 1” ID.
  Water cooled (3W beam power 25 µA)
  Reentrant (Resides in chamber)
Downstream beamline to be isolated if effects to the physics are not unacceptable
Window is 15 cm from entrance to cell
Densimet collimator 10 cm long installed in tube upstream of window. (W 90% , Cu 8%, Ni 2%)
Maintenance is possible if required.
12 mm thick collimator attached to cells
Collimators should prevent steering error from affecting cell
  Last steering element is 8 m upstream and 2” radius beam pipe.

## Slide 12: Be Isolation Window
0.008” Be window
Cooled by self contained water chiller to 10C
Integrated collimator Densimet

## Slide 13: Cryo-System
ESR 15K He for cooling
Must return ~25K
PID Control heater
  40K
Return mixed with bypass.
Bypass valve on PID
Alarms/interlocks on TS-5 (a/b) and TS-6 (a/b)
Similar controls to Cryotarget

## Slide 14: Performance Characteristics
½ life for tritium is ~12 .5 years
  5% conversion to He-3 over 1 year run
  Conversion starts immediately
  Fill as close to run date as possible
Fill purity 99.8% T2 +/- 0.02%
Quantity of T2 from
Where is the compressibility of tritium at the fill pressure of 200 psia.
The uncertainties on the quantities above are:
This gives an uncertainty of
r=0.0026 g/cm^3

## Slide 15: Density Change in Beam

## Slide 16: Status
Successful review on 15 September 2015
  Report available on wiki
  Pressure system calculations reviewed by 2/1/2016
  Final ladder assembly fixed by 3/1/2016
  ERR 3/16/2016
Design of platform complete
Construction of handling hut complete
Cell design and prototyping/testing complete
  Fabrication underway for actual cells
Modifications to Qweak target underway
  Cryo sytem/piping ~50% complete
Material testing is underway at SRS/SRTE/SRNL
Working through unresolved issues regarding shipping
NEPA analysis is complete should be presented to our site office by 2/1/2016

## Slide 17: Schedule
Hut and Platform
  Fabrication complete by 3/1/2016
  Test install June 2016
T2 Exhaust system
  Internal vent install April 2016
  External May and June 2016
Target
  Complete modifications to Qweak 3/1/2016
  Assembly complete 8/1/2016
  T2 cell install 10/1/2016
Interlocks
  Checkout complete 8/30/2016
ERR 3/16/2016
Checkout review 9/1/2016
Dates are estimates

## Slide 18: What We Need from Experiments
Decision on Bit Bite
  Affects access and work procedures
  Affects installation plan
  Affects experiment scheduling
Target Ladder
  Final list of targets due by 3/1/2016
ERR preparation
Training

## Slide 19: Materials-2
Al 7075 is unlisted
  Design basis
    for tension
    = 80% of 24 ksi for shear
    = 150% OF 24 ksi bending
Other wetted materials are SST
  304/304L
  316/316L
  ER316L Filler for welds

## Slide 20: Materials 3
Tritium and Hydrogen Compatibility
  Extensive experience with H2
  Beam induced corrosion not expected below 180K (Flower et. al.)
  Beam assisted embrittlement
    Increases fugacity
      Atomic tritium recombines rapidly
    Modeled room fugacity ~3100 psi
    Below threshold for H2 embrittlement
    Many orders of magnitude below He-3 swelling threshold (Louthan)
Test SRNL/SRTE using precracked coupons exposed to 2500 psi T2 underway
  Test follows ASTM 1820 G168 (Precracked Stress Corrosion Testing)
  Samples exposed for 4, 8, 12 months
  M. Morgan, A. Duncan (SRNL)
Tritium is expected to permeate through the cell and seals
  ~0.5 Ci /year very conservative
Calculations given in TGT-CALC-103-010

## Slide 21: Load Conditions
At room temp
  P = 200 psi
At 40K Beam Off
  Pressure = ~30 psi
  Max Temperature = 40K
Beam On
  Pressure = 36 psi (avg temp of T2 = 53K)
  Max Temperature = ~125K
Cyclic loads
  Cool down/warm up operating cycles = 20
  17800 beam trips (cycles between Beam On and Off)
    150 days, 33% duty factor, 15 trips/hr

## Slide 22: Analysis
Applicable Code ASME B31.3 (2014)
  Section 304.7.2 because of odd geometry
  Used both Hand Calculations and FEA
  Analysis conforming to ASME BPVC VIII D2 with load factors from B31.3 (i.e. 3 instead of 2.4 on P)
Used cyclic screening analysis from D2
  Depth of loads do not require a fatigue analysis
    175 psi pressure cycle (it is closer to 10 psi)
    Considers temperature cycle from 40K to 125K
Design pressure 675 psi
No source of overpressure
Calculations: TGT-CALC-103-002, 7, 8, 12, 13, 14, 15, 17.

## Slide 23: Thermo-Mechanical Model-1
Full temperature load
  Beam on at 20 µA 2x2 mm raster
  Pressure load 400 psi internal (more than 10x)
  Cooling using 40K heat sink
Using an elastic-plastic model
  Model solves and stresses are still below allowable even for over conservative case
  Local plastic failure requirements met
  Analysis not required because of screening analysis

## Slide 24: Thermo-Mechanical Model-2

## Slide 25: Thermo-Mechanical Model-3

## Slide 26: Mech Therm Model of Raster Off

## Slide 27: Raster Off Time Dependence

## Slide 28: Density Model
T2 properties derived from H2
  Viscosity, Thermal Conductivity, Heat Capacity, etc.
  Assumed a Real Gas model
  Buoyancy, convection on wall included
Assumed fixed 2.8W from 20 µA and 2x2 mm raster (11 mW/mm linear power density)
  Did not correct heat load for density
Averaged 20% reduction in density along beam path

## Slide 29: Vacuum System
Scattering chamber (standard Hall A)
  1900 liters
  Thin sections for recoil particles (0.014” aluminum)
Two 800 l/s turbos backed by Leybold D60 Mech pump
NEG Pump with backing turbo and mech pumps
Vacuum exhaust part of Tritium Exhaust System and is continuously purged with N2 (1 cfm)
Isolated from upstream beamline vacuum (Be window)
Remote RGA may help diagnose leaks. Serve as leak detector.

## Slide 31: Materials
Main Body and Entrance
  Aluminum 7075-T651 ASTM B209
  Extensive use of this allow for 15 years
  Strong, ductile, hard, non weldable
Seals are Al 1100
Valve assembly
  SST 304/304L Fitting
  Swagelok valve all metal bellows sealed (316L)
  Butt welded ER316L (100% VT in process and RT)

## Slide 32: Beam Heating
Max beam current min raster
3W in Entrance
3.3 W in Exit
on exit on entrance

## Slide 33: Summary of Test Results
Multiple hydrotests on components and assemblies
Entrance: Minimum burst above 2900 psi
Main body: Minimum burst above 3400 psi (0.014” section)
Assembly with covers
  Leaked above 4000 psi (seal was damaged)
  Failed above 5500 psi

## Slide 34: Raster Off
Initial conditions:
  Beam on full raster
  20 microA
Exit window is worst case
Beam spot no raster
  0.150 mm diameter
  Square profile
For high energy beam this spot size is very conservative
Tune shall be checked at each energy
Long term operations at these conditions are forbidden
Typical FSD for raster failure
  < 10 ms
Red curve is upstream section temperature

## Slide 35: General Requirements
Collect T2 from any release inside Hall A and exhaust in a controlled fashion
Exhaust point shall be 20 m above grade at site boundary
Must serve as part of the smoke removal system (at least 1/3 of the 36000 cfm required)
Must have at least two modes to service hut and to exhaust from Hall A. (500 and 12000 cfm)
Must stack vacuum pump exhaust
  Scattering chamber, dump line, getter system
Makeup air comes from new louvered door at bottom of ramp.
  Prevents overpressure on ramp door.
  Test required for louver system
  Air from outside from smoke removal system on ramp with damper removed

## Slide 36: Exhaust Summary
Exhausts secondary (vacuum chamber) and tertiary (Hall A) containment to 20 m stack
Two speed
  ~500 cfm
  12000 cfm
Exhaust system activated
  Vacuum switch failure (interlock)
  Truck ramp lower door (interlock)
  Manual activation (Hall and Counting House) (manual)
  Low speed activated manually for hut (manual)
  T2 monitor (interlock)