## Slide 1
    Brief status update of DAQ/Trigger production hardware
    Firmware development for HPS application
    CLAS12 CTP ‘upgrade’ notes
    Summary
Status of the Front-End Electronics
5 June 2013
R. Chris Cuevas

## Slide 2
All Trigger Modules In Production
2
Front End Crate
FADC250, (FADC125), (F1TDC)
Crate Trigger Processor
Signal Distribution
Trigger Interface
Trigger Control/Synchronization
Trigger Supervisor
Trigger Distribution
FADC250
CTP
SD
TI
SSP
GTP
TS
TD
L1 Trigger ‘Data’
MTP Ribbon Fiber
Trigger ‘Link” Control
Clock, Sync
MTP Ribbon Fiber
Global Trigger Crate
Sub-System Processor
Global Trigger Processor
SSP

## Slide 3: Hardware Status
3
All 726 VXS FADC250 boards have been received
  -- There will be plenty of spare units for HPS
  -- Overall production lot had ~10% of boards that did not pass initial
  acceptance testing. These boards will be evaluated and repaired.
All Signal Distribution boards have been received and tested.
Trigger Interface boards have been received and tested. At least one TI unit will operate in Trigger Supervisor mode for HPS.
Hall D Crate Trigger Processor is in production.
  -- Requirements for CLAS12 Trigger Processor have been defined
  -- CLAS12 Trigger Processor will have upgrades that allow for new requirements defined for HPS cluster finding and other advanced triggering needs. (See Scott Kaneta’s talk for details)
Sub-System Processors have been received and tested by Ben.
  -- Production SSP take advantage of a single FPGA to manage up to 8 front end crates and will communicate to new CLAS12 Trigger Processor at 5Gbps.

## Slide 4: Present Flash ADC Implementation Energy Sum Trigger (Hall D application)
Xilinx FPGA Trigger Function
Pre-Processing
To Crate
Trigger
Processor
(VXS Switch Card)
APD Signals
12 Bits
12 Bits
CH-1
CH-16
+
VXS Gigabit serial Transfer rate of 4Gb/s* per board
*(2 full duplex lanes @2.5Gb/s * 8/10b)
Transfer 16-bit Energy Sum every 4ns
Energy Sum
16 Channels
Energy & Time Algorithms
VME
Readout
8μs ADC Sample Pipeline
Global Trigger
Round Trip Latency <3us
CH-1
CH-16
4

## Slide 5: Technique for using channel sums and timing for cluster finding
5
32ns ‘frame’ begins with SYNC
Each channel sum value is a selectable 5-bits of 20-bit sum
Common threshold register for all channels
Common registers for Number of Samples Before and After Threshold
  NSA
  NSB
If channel does not pass threshold transfer zero sum and clock bits
Retain existing FADC250 features for channel readout
  -- Counters (scalers) for every channel
  -- EPICs or CODA readout for scalers
Definitions of ‘framing’ technique for synchronous transfer of individual sum
for every channel
Methods for cluster finding algorithm defined for Crate Trigger Processor
Multi-crate cluster collection and final trigger  Sub-System Processor
HPS Test Run

## Slide 6: Framing the Trigger Data from the FADC250
6
5 bit value extracted from
Channel energy sums
3 timing bits used to encode
4ns clock for TOT sample time
16 Bytes every 32ns
(5ADC + 3 timing bits)
1 Byte per channel
HPS trigger process runs @4ns
‘Integrate’ over 4 frames
Report every 128ns
FADC250 retains functions for
VME data readout of signals
when system trigger is received
For HPS a 13 bit value will be
extracted for the channel energy
sums. 3 bits will be used for timing
encoding to resolve 4ns TOT.
Requires 32bytes in 32ns so serial transfer speed must double to 5Gbps per lane
HPS Test Run

## Slide 7: Implementation for encoding data to CTP Hall B – HPS Test Run Implementation
Xilinx FPGA Channel Sum
Processing
To Crate
Trigger
Processor
(VXS Switch Card)
APD Signals
12 Bits
12 Bits
CH-1
CH-16
VXS Gigabit serial fabric
Transfer rate of 4Gb/s per board
(2 full duplex lanes @2.5Gb/s)
Use 32ns ‘frame’ to Transfer 16-bytes
Each channel is 1 byte:
5 bit Sum + 3 bits for timing
3 bit clock encoding
Allows 4ns clock recovery
in 32ns ‘frame’
16 Bytes in 32ns
Meets the 4Gb/s transfer bandwidth
Per board
CH-1
CH-16
32 ns
7
The TDC algorithm feature of the FADC250 was removed to allow for the
HPS firmware modifications
The TDC feature provided 6-bits of resolution with 62.5ps LSB

## Slide 8: Performance Summary (Updated since September Collaboration Meeting)
8
Successful implementation of full two crate FADC250 system for HPS spring 2011 test run!
FADC250 boards were not final production versions, but this was
the first time that a two crate system was installed and operated
in a beam experiment. Gigabit serial lanes @2.5Gb/s from all boards in two crates without any significant issues with VME 2eSST readout
The requirements for the new CLAS12 Trigger Processor include
5Gbps links from each of the FADC250 boards for much higher charge resolution from each channel. The new information will be used for the Calorimeter cluster finding algorithm.
All issues identified during HPS Test Run have been documented and will be resolved. Need significant test time to verify 5Gbps requirement.

## Slide 9: CLAS12 (HPS) Firmware Upgrade Notes New FADC250 Firmware and New CTP Design
Xilinx FPGA Channel Sum
Processing
To Crate
Trigger
Processor
(VXS Switch Card)
APD Signals
12 Bits
12 Bits
CH-1
CH-16
VXS Gigabit serial fabric
Transfer rate of 8Gb/s* per board
*(2 full duplex lanes @5Gb/s
=10Gb/s * 8/10b encoding)
Use 32ns ‘frame’ to Transfer 16-bytes
Each channel is 16 bit word:
13 bit Sum + 3 bits for timing
3 bit clock encoding
Allows 4ns clock recovery
in 32ns ‘frame’
32 Bytes in 32ns
Will require that the FADC250 transfer bandwidth doubles to 8Gb/s
CH-1
CH-16
32 ns
9
Existing CTP used close to 70% of FPGA resources
For HPS Test Run Trigger Application
CLAS12 will use CTP for three plane calorimeters
- PCAL, ECAL
- Possibility for more complex trigger algorithms
Proposal for CLAS12 wire chambers to use CTP
Output Fiber Transceiver will be upgraded
Requirements document complete
New hardware design

## Slide 10: Design Goals for FADC250 Firmware and Trigger Boards
10
Double the transmission speed from FADC250 boards to CTP
  Allows for higher energy resolution information from each channel
  Allows for timing resolution of 4ns
  Preliminary testing shows promising results with 5Gb/s per ‘lane’
  Must continue testing @5Gb/s with VME 2eSST bus activity to resolve issues
Restore the TDC function to FADC250
  -Will require firmware optimization and timing verification efforts
  -Successful implementation would eliminate need for signal splitting, discriminators, TDC modules and additional Crates.
Add ‘coefficient’ (Gain) registers to be programmed for each FADC250 channel

## Slide 11: Draft Activity Schedule for Two Quarters ( June-13  January-14)
11
June-13 | July-13 | Aug-13 | Sep-13 | Oct-13 (FY14) | Nov-13 | Dec-13 | Jan-14
Hall D GTP Testing | Hall D GTP Testing | Initial testing with Hall D Global Trigger crate | Continue Hall D Global Trigger Testing | Pre-commissioning Hall D |  |  | 
CLAS12 Trigger Processor Requirements | Begin Schematic changes. Evaluate parts | Initial Layout and design analysis | Post layout modeling evaluation and analysis | Firmware Engineering for new FPGA including HPS requirements | Firmware development Timing verification Initial testing |  | 
 | HPS proposal approved!  |  |  | Prepare procurement strategy for ALL Trigger Processors |  | Place order for CLAS12 Trigger Processors | 
 |  | Review changes required for Calorimeter APD mother board and connection board |  New APDs? Calorimeter Geometry change? Muon detector electronics? |  |  |  | 

## Slide 12: Design Goals for FADC250 Firmware and Trigger Boards
12
Double the transmission speed from FADC250 boards to CTP
  Allows for higher energy resolution information from each channel
  Allows for timing resolution of 4ns
  Preliminary testing shows promising results with 5Gb/s per ‘lane’
  Must continue testing @5Gb/s with VME 2eSST bus activity to resolve issues
Restore the TDC function to FADC250
  -Will require firmware optimization and timing verification efforts
  -Successful implementation would eliminate need for signal splitting, discriminators, TDC modules and additional Crates.
Add ‘coefficient’ (Gain) registers to be programmed for each FADC250 channel

## Slide 13
Summary
ALL 12GeV pipelined DAq and Trigger custom electronic modules are in production with most designs completely tested and accepted.
Many detector groups are using FADC250 boards for testing and full crate performance testing is ongoing for each Hall Group.
New requirements for CLAS12 Trigger Processor have been completed and include all trigger processing ideas for each detector subsystem. Planned FPGA device will exceed requirement specification but will allow for future improvements of triggering applications.
Significant challenges remain and testing is crucial to verify that FADC250 boards will be reliable at the 5Gbps serial transmission rate.
Electronics group will support re-design work needed for Inner_Calorimeter circuit boards and any other electronic needs for the experiment.
Acknowledgement of continued significant hardware and firmware contributions from:
Hai Dong, Scott Kaneta, Nick Nganga, Ben Raydo, Ed Jastrzembski, and Bryan Moffit, William Gu
13

## Slide 14
All sorts of good stuff
Backup Slides

## Slide 15
CODA
MTP Fiber
MTP Fiber
LINUX
LINUX
Two crate Trigger Signal
From SSP to TI(TS)
8
Successful HPS Beam Test with New 12GeV Cluster Finding Trigger App
HPS Test Run in Hall B used two full VXS crates
432 APD channels  27 FADC250
Cluster finding algorithm in Crate Trigger Processor -- Pushing the resource limit!
New firmware to encode individual channel sums
CTP firmware will report cluster centroid to SSP
SSP will create trigger from CTP output
Exploits the use of the 4Gb/s VXS bandwidth from each FADC250 module
New technique to report signal threshold crossing with 4ns resolution and 5bit amplitude for every channel
Experiment shows that Hall D L1 Energy Sum algorithm for Calorimetry will clearly ‘fit’ into CTP
Ebeam 5.55 GeV Radiator 10^-4 r.l. Au Collimator 6.4 mm Pair spectrometer convertor 1.8x10^-3, 4.5x10^-3 and 1.6x10^-2 r.l. Pair spectrometer field - -760A and +760A
HPS DAq rates:
Ecal +20KHz
With Si Tracker: 4KHz

## Slide 16: HPS Firmware Design – Implementation Brief History
2
26-May-2011 HPS collaboration meeting
-- Initial ideas on what information was needed for HPS trigger
-- Existing stable firmware was designed for Hall D Energy sum
18-Oct-2011 HPS collaboration meeting
-- Firmware requirements document created
-- Clear definition of what information was required for cluster finding
-- Methods were coded, simulated, and verified (FADC250)
-- Crate Trigger Processor firmware requirements defined
-- Sub-System Processor firmware requirements started
Nov-11->Feb-12
    --Pre-Production FADC250 units configured in a two crate
    test station for full test of new trigger firmware
    -- Test station includes Trigger Interface, Signal Distribution (Timing)
    and CODA library development plus GUI
March-2012
    -- CTP cluster finding algorithm fine tuning and test with fully instrumented crates
13-April-2012
    -- Installation of FADC250 and Trigger modules in Hall B
    -- Cabling, debug, interface to APD electronics, TEST
17-May-2012
    -- HPS test run with beam in Hall B! (Even the flooding could not stop this event)

## Slide 17: Crate Trigger Processor Point of View Cluster Finding with Energy Resolution/Channel
4 x 2.5Gb/s fiber links
From crates to
Sub-System Processor
Final Cluster Algorithm
To process all calorimeter channels
Cluster Energy Trigger
Will have much more resolution than initial DVCS implementation
Crate Trigger
Cluster Combiner
APD Signals
Serial Stream
Board 1
Board 16
Serial Stream
6 Bit Sum
CE1
CE0
CH-1
6 Bit Sum
CE1
CE0
CH-16
32 ns
6 Bit Sum
CE1
CE0
CH-1
6 Bit Sum
CE1
CE0
CH-16
32 ns
Sub-System Processor
8Gb/s
8Gb/s
11

## Slide 18: Flash ADC Implementation
Energy & Time Algorithms
Event #1
Event #2
Readout
FADC
Trigger #1
Trigger #2
8μs ADC Sample Pipeline
Trigger Pulse
Pre-Processing
To trigger
logic
Trigger Input
detector
signal
Sampling Flash ADC stores digitized signal in 8us memory
Trigger input copies a window of the pipeline and extract pulse charge and time for readout
Trigger output path contains detailed information useful for cluster finding, energy sum, etc.
Hardware algorithms provide a huge data reduction by reporting only time & energy
estimates for readout instead of raw samples
Sample Clock
Capture Window
21

## Slide 19
16 Channel, 12-bit
  4ns continuous sampling
  Input Ranges: 0.5V, 1.0V, 2.0V
  (user selectable via jumpers)
  Bipolar input, Full Offset Adj.
  Intrinsic resolution – σ = 1.15 LSB.
  2eSST VME64x readout
  Several modes for readout data format
    Raw data
    Pulse sum mode (Charge)
    TDC algorithm for timing on LE
  Multi-Gigabit serial data transport of trigger information through VXS fabric
  On board trigger features
    16 Channel SUM every 4ns
    Channel coincidence, Hit counters
  Automatic Test Station is complete
  Engineering Run – 40 Delivered!
    18 Hall D
    17 Hall B
    Production Procurement FY12
      ~ 700 Boards for all Halls
Flash ADC 250MHz
Fast Electronics
DAQ Groups
23-Sept-2011
2