## Slide 1: Considerations on Interaction Region design for Muon Collider
Muon Collider Design Workshop
JLab, December 8-12, 2008
Guimei Wang, Muons,Inc., /ODU/JLab
Yaroslav Derbenev, Jefferson Lab
Notes: Yaroslav Derbenev, Jefferson Lab

## Slide 2: OUTLINE
Major issues of IR design
Final focus optimization
Bent chromatic compensator
Bent beam extension
Optics control
Conclusions
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008

## Slide 3: Interaction region
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
Courtesy of A. Bogacz
Notes: Courtesy of A. Bogacz

## Slide 4: Major issues of the IR design
Design the tightest star focusing
Design preventive chromatic compensation
Design compensation for higher order aberrations, if needed
Eliminate or minimize no-bend sections, to spread neutrino radiation
Develop optics control and star point feedback
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008

## Slide 5: Design the tightest star focusing
Achievable low beta is determined by admissible aperture of quadrupoles and beam transverse emittance
6D ionization cooling (including PIC) delivers a minimum 6D emittance.
REMEX reduces the 4D emittance for expense of the longitudinal one. One may admit some further increase of longitudinal emittance due to beam recombining if needed.
However, bunch length should be shorter than the low beta, while energy spread should not be too large (1% or less)
In result, luminosity is determined by aperture and achievable the 6D beam emittance (after cooling and recombining)
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008

## Slide 6: Optimum FFB design
;
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
/This emittance should be compared with a minimum one available with use of REMEX/
Notes: ;

## Slide 7: Design the tightest star focusing /recommendations-in-principle/
Extend the FFB aperture, as possible
Design the shortest bunches in collider ring
Reach minimum 6D emittance by cooling
Imply REMEX to reach the optimum or minimum transverse emittance
Imply beam recombination, if needed
Develop IR optics and collisions control
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008

## Slide 8: Design FFB
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
Design principle: high school optic bench lesson
A parallel beam enters a thick lens, becomes 100% focused
However, there is a huge chromatic spread of the star point
(frequently exceeds both, low beta and bunch length)
Notes: A parallel beam enters a thick lens and gets focused

## Slide 9: Chromatic compensation
There is a long, difficult history…
with many good names
It continues to go on…
To be exhausted some day?
May be never
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008

## Slide 10: Chromatic Compensation theory
Iterations:
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
General equations including sextupoles:
Expansion:
Unperturbed trajectory:
+ octupoles
These equations are integrated along the growing mode of particle betatron motion
Notes: These equations are integrated along the growing mode of particle betatron motion

## Slide 11: Chromatic compensation conditions
These three conditions are satisfied “automatically” due to symmetry features of the compensating block
“Standart” conditions:
Conditions connected to the betatron and
dispersion beam sizes:
Next iteration (including octupoles) can be calculated if needed
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
Notes: Next iteration (including octupoles) can be calculated if needed

## Slide 12: Zigzag CCB linear optics
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
Courtesy of A. Bogacz
Courtesy of P. Chevstov
Notes: Courtesy of P. Chevstov

## Slide 13: Chicane CCB linear optics
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
Courtesy of A. Bogacz
Blue: dispersion
Red: x-beta (anti-symmetric trajectory)
Green: y- beta
Notes: Blue: dispersion
Red: x-beta
Green: y beta

## Slide 14: No-bend beam extension
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
Courtesy of A. Bogacz
Notes: Extension in strait

## Slide 15: Bend everything
Bend :
Beam extension section (BES)
Chromatic compensation block (CCB)
Final focusing block (FFB
-Continuous dipole field (only technical gaps)-
-Use combined magnets for focusing-
Why bent IR?
Space and cost economy
Spread neutrino radiation (NR) from IR
(note: beam divergence in detector area frequently exceeds the inverse gamma)
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
Notes: Continuous dipole field (only technical gaps)

## Slide 16: Bent beam extension theory
Continuous bend, alternating quads (combined magnets)
Periodic solution for orbit dispersion ever exists despite of beam “betatron” expansion
However, one should not allow the dispersion beating too much in a single cell
So, the extension rate is limited but not small
Extension process is type of parametric resonance through a number of cells
Match the periodic dispersion with arcs
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008

## Slide 17: Bent beam extension optics test
Blue: combined magnets
βx max (m) | 104241
βy max (m) | 80897
Dx max (m) | 0.12
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
Blue magnets: combined;
Red magnets: quadrupoles
Notes: Red: quadrupoles

## Slide 18: Periodic dispersion in bent BES
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008

## Slide 19: Bent CCB test
A CCB schematic with an even symmetry dispersion
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
Courtesy of P. Chevstov

## Slide 20: Bent CCB test
Betatron trajectories are plotted
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008

## Slide 21: Bent CCB test
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
Dispersion (blue) and beta-functions are plotted
Notes: Dispersion (blue) and beta-functions are plotted

## Slide 22: Bent FFB test
Total Length: 26m
G[kG/cm]=19.72098
B[kG]=20 G[kG/cm]=-19.29932
G[kG/cm]=26.25493
Note: Neutrino beam spread in detector area (straight)
frequently exceeds the inverse gamma!

## Slide 23: Precision IR control
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008
The star point transverse position should be controlled with accuracy about 1 micrometer. To be only achieved by lumi-feedback ?
Precision required to control the focal parameter:
Precision required to control chromatic compensation
seems to be ease:
Betatron phase control between arcs: Same as control the
collisions? Seems so…
<<

## Slide 24: Conclusions
We achieved knowing an exact algorithm how to design the achromatic star focus for best of the MC luminosity
The interaction region can become part of arc, to benefit one with two improvements:
- space economy (better luminosity)
- large reduction of neutrino flux concentration along the IR
Full scale simulation on the way…
Almost continuous bend IR to be shown
Thank you!
Y. Derbenev, Muon Collider Design Workshop, Jlab, December 8-12, 2008