## Slide 1: CEBAF Source and Injector Status PREx-II Collaboration Mtg Feb. 26, 2016
Matt Poelker and Joe Grames
Center for Injectors and Sources

## Slide 2
Experiment | Beam Energy (GeV) | Pol (%) | I (µA) | Target (Length) | Apv (ppb) | Charg Asym (ppb) | Position Diff (nm) | Angle Diff (nrad) | Size Diff (δσ/σ)
HAPPEx-I (Achieved) | 3.3 | 38.8 68.8 | 100 40 | 1H (15 cm) | 15,050 | 200 | 12 | 3 | 
G0-Forward (Achieved) | 3.0 | 73.7 | 40 | 1H (20 cm) | 3,000-40,000 | 300±300 | 7±4 | 3±1 | 
HAPPEx-II (Achieved) | 3.0 | 87.1 | 55 | 1H (20 cm) | 1,580 | 400 | 2 | 0.2 | 
HAPPEx-III (Achieved) | 3.484 | 89.4 | 100 | 1H (25 cm) | 23,800 | 200±10 | 3 | 0.5±0.1 | <10-3
PREx-I (Achieved) | 1.056 | 89.2 | 70 | 208Pb (0.5 mm) | 657±60 | 85±1 | 4 | 1 | <10-4
QWeak-I (Achieved) | 1.155 | 89.0 | 180 | 1H (35 cm) | 281±46 | 8±15 | 5±1 | 0.1±0.02 | <10-4
QWeak | 1.162 | 90 | 180 | 1H (35 cm) | 234±5 | <100±10 | <2±1 | <30±3 | <10-4
PREx-II | 1.0 | 90 | 70 | 208Pb (0.5mm) | 500±15 | <100±10 | <1±1 | <0.3±0.1 | <10-4
MOLLER | 11.0 | 90 | 85 | 1H (150 cm) | 35.6±0.74 | <10±10 | <0.5±0.5 | <0.05±0.05 | <10-4
CEBAF Polarized Electron Injector

## Slide 3
Spring 2016
Laser System
  Still operating with 3-lasers
  Each now has capability for 249.5 or 499 MHz
High-Polarization Photocathode
  Retired 5247-1 work horse of 6 GeV era 2009-2012
  Installed 5756-4 for 12 GeV (QE > 1%, P ~87%)
Gun
  Still operating at -130 kV (more on upgrade later…)
  Baked gun/activated NEG’s => Charge lifetime >150C
Parity Controls
  Intact from 6 GeV program

## Slide 4
Summer 2016
Must add support for an additional 4th laser – big job
  New laser table layout, RF sources and SCAM (beam mode)
3-laser
configuration
IHWP
Pockels Cell
RWP
IA

## Slide 5
Summer 2016
IHWP
Pockels Cell
RWP
IA
New
4-laser
configuration
Retain geometry downstream of polarization combining cube

## Slide 6
Chopper
FC#1
FC#2
Buncher
Capture
Bunchlength
Cavity
Cryounit
Cryomodules
Synchrotron
Light Monitor
500 keV Spectrometer
5 MeV Mott
Polarimeter
Injection Chicane
123 MeV
Spectrometer
PreBuncher
Gun#2
Gun#3
V-Wien Filter
H-Wien Filter
Apertures
12 GeV CEBAF Polarized Electron Injector
DC HV Load Lock
Polarized e- Source
(130 keV)
Spin Control, Bunching, Transverse Acceptance
Synchronous RF Photoinjection, Longitudinal Acceptance
Bunching & Warm Acceleration
(500 keV)
SRF Acceleration
(6.3 MeV)
SRF Acceleration
(123 MeV)
Spin Solenoids
Brock
Cavity
10 MeV
Spectrometer
10 MeV R&D
Beam line
C20
R100
Helicity
Magnets
Stewart
Platform

## Slide 7
New Points to Know About
Stewart Platform – remote positioning of Pockels cell
  Wes Moore wrote EPICS driver for embedded machine linux
  John Hansknecht planning for 3D printing of components
  Summer intern for calibration and testing
Brock Cavity – non-invasive charge asymmetry monitor
  Installed after A1 for bunch length profile measurement
  Brock & BCM0L02 span (A2+Chopper+A3+A4)
Helicity Magnets
  Retained if needed for sensitivity or feedback, but…
  ...if desired requires ioc/hardware upgrade + new? locations.
Mott Polarimeter
  3 year upgrade + study effort wrapping up

## Slide 8
Run I – January 2015
Instrument systematics
Extrapolation I (SLSP-5247)
Run II – October 2015
Beam systematics
Extrapolation II (SLSP-5756)
We are planning publication this Spring, but Users benefit immediately from this work
Future Run 3 may test largest systematic (theory) with low-Z target
CEBAF 5 MeV Mott Polarimeter
Expected Range of Uncertainty |  | 
Source | 2014 Expectation | 2016 Preliminary
Theory | 0.5 – 1.0% | 0.5 – 0.6%
Extrapolation | 0.2 – 0.5% | 0.2 – 0.3%
Instrumental | 0.2 – 0.4% | 0.2 – 0.3%
BUDGET | 0.6 – 1.2% | 0.6 – 0.7%

## Slide 9
Commissioning of CEBAF Upgrade at UITF
TESTING MORE ROBUST (>300KV) INVERTED GUN
COMMISSIONING NEW 2/7 CELL CRYOUNIT
TEST 200KV WIEN FILTER

## Slide 10
CEBAF – ILC 200 kV Inverted Gun
Developed and ready for installation
Commissioned at Test Cave to 225 kV w/o field emission
Large grain Niboium electrode
-200kV
light in
e- out
photocathode

## Slide 11
Testing > 300 kV Inverted Guns at GTS / UITF
8 MV/m
11 MV/m
Commissioned to 325 kV

## Slide 12
Status of New ¼ CM
2016 Commissioning plan at Test Lab
  Spring, ¼ assembly + cryo/RF @ UITF
  Summer, SRF commissioning @ CMTF
  Fall, install ¼ beam planned up to ~8 MeV (klystrons)
Installation timeline at CEBAF in advance of Moller TBD

## Slide 13
Summary
CEBAF Injector
  Reliable high polarization (~85%) polarized electron source
  6 GeV era source basis for initial parity program
  4-Laser Upgrade / Laser Table configuration planned summer 2016
  We will allocate time for setup and characterization
CEBAF Injector Upgrade and UITF Operations
  200 kV “tee” inverted gun is ready, likely consider “ball” inverted gun
  New ¼ assembly/testing/beam ops planned for 2016
  Extend Wien filter capability from 130kV to 200kV planned
  PQB tests at UITF e.g. low-noise receiver can be considered
Polarized beam R&D
  Stewart platform development highest PQB R&D priority for FY16
  Brock cavity and helicity magnets are available
  Submit Mott results for publication late-Spring