## Slide 1: HRSMC, A Geant4 Simulation for HRS
Jixie Zhang
CREX Collaboration Meeting
April 2014

## Slide 2: Introduction
HRSMC is a Geant4 program developed to simulate the physics for HRS, especially for the G2P and GEP experiments. It was also designed to support other HRS experiments.
Geometry:
  Full G2P|GEP geometry: g2p target, target field coil, g2p scattering chamber, local dump, septum, platform itself, 3rd arm
  HRS QQDQ magnet geometry (no field, using SNAKE transportation )
  BigBite
  Hall A Neutron Detectors (HAND)
  BoNuS RTPC
  SuperBigBite
  HMS
  CREX: HallA scattering chamber, CREX target, Septum.
Fields: g2p chicane fields, target field, septum fields, BigBite field. HRS QQDQ fields are not included yet.
The HRS transportation came from the program SNAKE and MUDIFI.(Thanks to J. LeRose and M. Huang)

## Slide 3: Geometries in HRSMC
Detectors and fields can be turned on or off in configuration files.

## Slide 4: G2P|GEP Geometries
G2P|GEP Geometries include the following: chicane magnet, target platform, scattering chamber, target coil, target nose and the target itself, local dump, sieve slits, septum magnet, plastic shielding blocks, 3rd arm.

## Slide 5: CREX Geometries
CREX Geometries include the following:
scattering chamber (need tuned), target
sieve slits (same as G2P’s)
septum magnet(same as G2P’s)
From http://ace.phys.virginia.edu/HAPPEX/2866
NO SNAKE model yet!

## Slide 6: Reference

## Slide 7: Target Reference

## Slide 8: Adding New Geometries
Different experiments usually vary from geometries on the target platform.
Each target or detector is hard coded, associated with a configuration file to turn each individual component on or off.
CREX target + G2P septum
HRSMC can support any new experiment by adding a new geometry class.
All sensitive detectors share a standard hit processing but vary in Sensirtive Detector ID. All hits will be recorded automatically.
HRS
Detector.ini
G2P
Detector_G2P.ini
CREX
Detector_CREX.ini
XXX, Future Exp
Detector_XXX.ini
RTPC
Detector_RTPC.ini
SBS
Detector_SBS.ini
HMS
Detector_HMS.ini

## Slide 9
How to simulate HRS
transportation and reconstruction
in G2P|GEP ?

## Slide 10: Strategy for without Target Field
Vertex to Sieve: propagated by Geant4 with a physics model (i.e. MSC, Decay, Ionization, EM physics...)
Sieve to Focal: linear project the particle from sieve to target then using SNAKE forward model, 8-10 software collimator cuts are applied along the trajectory to make sure that particle can really hit the focal plane.
Focal to target: using SNAKE backward model or real optics matrix.
Target to Vertex: linear projection.
Target plane
Vertex plane
Sieve plane
Virtual boundary
Focal plane
Snake forward
Snake backward
Propagated by Geant4

## Slide 11: Strategy for with Target Field
Vertex to Sieve: propagated by Geant4 with a physics model
Sieve to Focal: project sieve to target then using SNAKE forward model, 8-10 software collimator cuts are applied along the trajectory to make sure particle is really hitting the focal plane.
Focal to Sieve: using SNAKE backward model or real optics matrix from focal to target, then project from target to sieve.
Sieve to Target: using Drift-In-Field model.
Target to Vertex: using Drift-In-Field model.
Target plane
Vertex plane
Sieve plane
Virtual boundary
Focal plane
Snake forward
Snake backward
Propagated by Geant4
Drift-In-Field

## Slide 12: Sieve to Focal
Sieve2Focal = Sieve2Target + Target2Focal
Sieve to Target: linear projection to get the effective vertex
Target to Focal: using SNAKE forward model to propagate effective vertex to focal plane, 8-10 software collimator cuts are applied along the trajectory to make sure particle is really hitting the focal plane.
Target plane
Vertex plane
Sieve plane
Virtual boundary
Focal plane
Snake forward
Hit at sieve, propagated in Geant4
Image the hit at sieve plane to target plane, this is the effective vertex ... Very important

## Slide 13: Effective BPM X0_tr and Theta_tr
Variable in target plane imaged by NO target field SNAKE model
Thrown variable in target plane
X0_tr is the BPM vertical measurement, it will be used to reconstruct the focal plane to the target plane. When the target field is on, the BPM measurement is no longer the one we should use in the NO target field SNAKE model.
5.0 T target field

## Slide 14: With Target Field: Focal to Sieve
Focal2Sieve = Focal2Target + Target2Sieve
Focal to Target: using SNAKE backward model or real optics matrix
Target2Sieve: linear projection
Sieve to Target: using Drift-In-Field model to swing the particle in a field.
Target plane
Vertex plane
Sieve plane
Virtual boundary
Focal plane
Snake backward
Drift-In-Field

## Slide 15: HRS Transportation
HRS transportation function usually come from SNAKE and MUDIFI.
Always fitting from target plane to focal plane.
There will be 8 -10 end planes along the trajectory to make sure that the particle do not hot the magnet blocks.
Currently the following SNAKE models are ready to use:
  Standard HRS, 12.5 degrees, NO septum
  Two models of 6 degrees HRS with septum for E97-110. One is for larger X0 and the other is for normal X0
  Several models of 5.65 degrees HRS with septum and 3 cm circular raster for G2P|GEP, varying in the active septum coils in the right septum: 48-48-16 No Shims, 48-48-16, 40-32-16 and 40-00-16
  Can add more SANKE models (Min Huang and John LeRose are the experts)
Usually need to make correction in focal plane in order to match real data
Alternate method: use optics calibration result, generate data from focal plane to target, then run MUDIFI to fit a forward transportation function. this will guarantee to match the real data!

## Slide 16: Documentation
Source code is available in SVN: https://jlabsvn.jlab.org/svnroot/halla/groups/g2p/HRSMC/
Instruction for Geant4 installation, environment setup and update history are available.
Usage manual will be printed by typing these commands:
  HRSMC -h, HRSMC --h, HRSMC -help, HRSMC --help
Usage: HRSMC [option1 argument_list] [...] [optionN argument_list]
To get the detail usage of an option, just type 'help' after it. For example: HRSMC -physicsmodel help
Description for internal commands (html format) are already: https://jlabsvn.jlab.org/svnroot/halla/groups/g2p/HRSMC/Menu/
Output root ntuple structure description is ready here: https://jlabsvn.jlab.org/svnroot/halla/groups/g2p/HRSMC/HRS_nt_structure.txt
A lot of macro files and root scripts are available: https://jlabsvn.jlab.org/svnroot/halla/groups/g2p/HRSMC/macros

## Slide 17: Resolution of HRSMC Using SNAKE Model 484816+shim, No Target Field
Raster=2.4cm, BPM resolution: 1 mm in vertical, No target field

## Slide 18: Resolution of HRSMC Using SNAKE Model 484816+shim, Stop at Target Plane,5T
Raster=2.4cm, BPM resolution: 1 mm in vertical, 5.0 T target field
Reconstructed to the target center

## Slide 19: G2P Optics Data, All Sieve Holes
G2P Optics data:
HRS Angle = 5.7 deg
HRS P0 = 2.251 GeV/c
No target field
Delta_P = 4.4 MeV/C
12C
4He
12C and 4He
Yfp
Xfp
Can not separate in focal plane!
5.5 cm width
5.5 cm width
Thanks to M. Huang

## Slide 20: G2P Optics Data, 3rd Row Sieve Holes
G2P Optics data:
HRS Angle = 5.7 deg
HRS P0 = 2.251 GeV/c
No target field
Delta_P = 4.2 MeV/C
12C
4He
12C and 4He
Yfp
Xfp
Can separate in the focal plane if cut by vertical sieve position (Out-Plane-Angle|Position)

## Slide 21: To Separate 2 Elastic Peaks
G2P Optics data:
HRS Angle = 5.7 deg
HRS P0 = 2.251 GeV/c
No target field
Delta_P = 4.2 MeV/C
12C and 4He
Yfp
Xfp
At center hole: dP = 0.19%  dXfp = 2.6 cm
To separate 2 elastic peaks in the focal plane without other helps, the difference between these 2 deltas should larger than 0.4%!
Only for NO Raster beam.

## Slide 22: Test SNAKE: to Separate 2 Elastic Peaks
From snake: to separate 2 elastic peaks in the focal plane without other helps, the difference between these 2 deltas should larger than 1%!
For 4 mm raster beam. Not consider energy loss and multipole scattering yet for outgoing electrons.

## Slide 23: Geant4 Simulation: The Target
Momentum at Sieve Plane

## Slide 24: Summary
HRSMC is designed for multiple HRS experiments, especially for G2P and GEP.
SBS, BB, HMS, HAND and RTPC are ready to use. It can be easily modified to support other experiments by adding the geometries.
HRSMC has been used to simulate the optics for G2P|GEP. We have another dedicated program, g2psim, too.
One can use real optics matrix to reconstruct simulated focal plane data. In other words, HRSMC can cross check the quality of optics matrix and help to improve it, which is useful for those experiments with large raster.
The strategy of the reconstruction with target field is:
No-Target-Field-HRS + Drift-Sieve-to-Target-in-field .
A lot advance features are included.
Need support for SNAKE models. Thanks to Min Huang and John, need their continuous contribution.

## Slide 25: Acknowledgment
Thank John LeRose for providing guidance and SNAKE models
Thank Min Huang for providing SNAKE models and her hard work in optics optimization for real data
Thank Chao Gu for helping in both simulation and optics optimization
Thanks to all G2P Collaborators