## Slide 1: Detector Support Group Select Projects
Amrit Yegneswaran

## Slide 2: DSG Staff
Mary Ann (20) Peter (27) Aaron (<1)
Pablo (4) Brian (20) George (5)
Mindy (20) Tyler (4) Marc (23)
Give me the child for the first seven years and I will give you the man. Jesuit maxim widely attributed to Ignatius Loyola
DSG is all about teamwork

## Slide 3: Contents
Hall A
  SBS & BB: cable fabrication; super-module fabrication; GEM gas system
  HRS: dipole magnet power supply's controls and monitoring system
Hall B
  RICH: cooling; humidity and temperature sensor
  Torus & Solenoid: readout system
Hall C
  HMS/SHMS: magnet HMI screens → CSS-BOY; HV Tcl/Tk screens → CSS-BOY
  NPS: testing of CAEN SY4527
Hall D
  Solenoid: upgrade of PXI system; WEDM screens
DSG
  Accelerator: populating VME fast shutdown board, wire-bonding tests
  R&D & Safety: Test stations; focus on safety

## Slide 4: Hall A: SBS Cable Fabrication and Routing
Cable fabrication for HCAL
  Search, seize, and secure cables in ESB
  95% of ~1888 cables fabricated
HCAL HV cable labeling and routing
~300 HV cables routed on HCAL in Test Lab
Search, seize, and secure cables in ESB
DSG Note 2019-45
“He believed in youth and youth made him its confidant”
dedication to George Edward Cunnigham, Berkeley CA

## Slide 5: Hall A: BB ECAL Super-module Assembly
126/191 super-modules assembled.
Each super-module has:
  Nine lead-glass blocks with light guides
  Wrapped in aluminum foil and copper
  Support frame with screws, springs, and plates hold them in place
DSG Note 2019-48
Top: diagram of BigBite ECAL showing configuration of 191 super-modules
Left: Partially assembled super-module showing the nine wrapped lead-glass blocks. Light guides are on opposite end of blocks in photo

## Slide 6: Hall A: SBS & BB GEM Gas System
M1
M2
M3
M4
INFN Layer Configuration
3 modules per layer
1 gas line per layer
UVA Layer Configuration
4 Modules per layer
4 Gas line Per layer
M1
M2
M3
Ar/CO2
70%:30%
M1
M2
M3
M1
M2
M3
M4
Layer
Layer
DSG Talk 2019-17
Ar/CO2
70%:30%

## Slide 7: Hall A: SBS & BB GEM Gas System
manifold 2

## Slide 8: Hall A: SBS & BB GEM Gas System
Developing 3D-CAD model of gas system in NX-12
Isometric View of GEM Gas System’s components
Isometric View of GEM Gas System’s rack assembled

## Slide 9: Hall A: SBS & BB GEM Gas System
DSG Talk 2019-17, DSG Note 2019-49, DSG Note 2019-50
Honeywell Zephyr Evaluation

## Slide 10: Hall A: Dynapower PLC Control System
Upgrade of PLC used in HRS Dipole Magnet Power Supplies
  Evaluated potential systems (different vendors & products)
  Setup (code development) and deployed selected system
DSG-Note 2019-29, DSG-Note 2019-40
OLD – SLC500
NEW - CompactLogix

## Slide 11: Thanks Jack
Dsg-halla <dsg-halla-bounces@jlab.org>
on behalf of Jack Segal <segal@jlab.org>
Tue 6/11/2019 8:34 PM
Brian, Many thanks to you and the DSG. The Left Dipole finally seems to be doing what it was intended to do 24 years ago. It now has redundant protections that function correctly. Your prompt help while I was trying to understand how things were configured and how to correct the errors is much appreciated. Again, thanks!
DSG’s inner child

## Slide 12: Hall B: RICH Cooling Investigation
Electronic Panel
Internal cabling
Red ~ HV
Gray ~ LV
Light gray ~ Sensor
Green ~ Data

## Slide 13: Hall B: RICH Cooling Investigation

## Slide 14: Hall B: RICH Cooling Investigation

## Slide 15: Hall B: Sensors for New RICH
Improve temperature and humidity slow-controls measurement systems for next RICH sector.
Sensirion SHT85 Sensor
  New product released on 11/2018
  Accuracy
    Humidity: ±1.5% RH, temperature: ±0.1°C
Compare to currently used Honeywell/Omega
  Smaller size of sensor assembly
  Reduced # of cables/connectors
  Compatible with existing slow-controls electronics
  Compatible software support (including EPICS)
  Lower cost
DSG Note 2019-43

## Slide 16: HallB: Sensors for New RICH
Developing FPGA code
  Addressed issue with single-shot readout sequence
  Testing in progress
  DSG Note 2019-44
  DSG Note 2019-47
Serial Communication Timing Test Screen

## Slide 17: Hall B: Solenoid and Torus Magnet Readout System
Replace current LV Chassis FPGA with DE0-Nano-SoC or some other improved FPGA board
  LV cRIOs have failed, removing them eliminates point of failure
  New board would communicate directly with PLC
Present readout configuration
DSG Talk 2019-24
DSG Note 2019-53

## Slide 18: Thanks Ruben
Dsg-hallb_magnets
on behalf of Ruben Fair
Thu 9/5/2019 10:11 AM
Tyler and the DSG, This is excellent work. Great report and summaries.
We very much appreciate your contribution and your continuous improvement efforts. Looking forward to seeing which solution is the most reliable and cost effective.
Thank you
Ruben
DSG’s inner child

## Slide 19: Hall C: HMS/SHMS Magnet HMI screens to EPICS CSS-BOY
Motivation
  Standardization
  Enables data archiving and thereby facilitates debugging
  Enhancements of display and functions facilitates magnets’ controls and monitoring
275 HMI screens need to be addressed
DSG Note 2019-20
DSG Note 2019-22
DSG Note 2020-02
DSG Talk 2019-07
DSG Talk 2019-13

## Slide 20: Hall C: HMS/SHMS Magnet HMI screens to EPICS CSS-BOY
CSS-BOY screen for SHMS – Horizontal Bender magnet’s Helium and Nitrogen temperatures.
This screen combines Helium and Nitrogen HMI PLC screens.

## Slide 21: Hall C: HV Tcl/Tk system to EPICS CSS-BOY
Motivation for CSS
  Standardization
  Faster
    Opens screens in seconds as opposed to minutes (yawn)
    Screens are static and do not have to be rebuilt unless configurations change
  Uses a Python script to build screens based on configuration files.
    Script builds all screens in seconds
  Includes CSS-compatible backup/restore program and start-up script.
  Start-up script allows multiple instances of screens to be opened simultaneously and provides a consistent user experience for all users
DSG Note 2019-27, DSG Note 2019-34, DSG Note 2019-36, DSG Note 2019-42
DSG Talk 2019-13

## Slide 22: Hall C: HV Tcl/Tk system to EPICS CSS-BOY
List-view controls screen for HMS Hodoscope 1 Y.

## Slide 23: Hall C: Investigation of CAEN SYS 4527 and HV cards A7030TN
Issues with SY4527 and HV card A7030TN
  Changing set values of parameters
  Ramp-up latency
  Ignoring commands
DSG Note 2019-46
DSG Note 2019-54
DSG Note 2020-01
DSG Talk 2019-18
DSG Talk 2019-23
DSG Talk 2019-28
HV CAEN Expert Controls CSS-BOY screen developed for testing

## Slide 24: Hall C: Investigation of CAEN SYS 4527 and HV cards A7030TN
Ramp-up latency

## Slide 25: Hall C: Investigation of CAEN SYS 4527 and HV cards A7030TN
Test system configuration possibilities

## Slide 26: Thanks Alberto
Dsg-hallc_controls <dsg-hallc_controls-bounces@jlab.org>
on behalf of
Alberto Lucchesi <a.lucchesi@caen.it>
Fri 9/13/2019 8:25 AM
Dear Pablo, thanks to your suggestions we were able to reproduce the same test as described in your document and we found some interesting information…
Dsg-hallc_controls <dsg-hallc_controls-bounces@jlab.org>
on behalf of Alberto Lucchesi <a.lucchesi@caen.it>
Mon 9/30/2019 7:26 AM
Dear Pablo, from the log I'm convinced that the ramp delay is something related to the board firmware. I say this because looking the log it is clear that all the power on commands are received by the boards at the same time, but for a reason that we have to understand, sometime a channel doesn't perform the ramp correctly but its first 5/6 steps are anomalous…
DSG’s inner child

## Slide 27: Hall D: Upgrade of PXI system
Upgrade and maintenance of PXI system used for FastDAQ (10 kHz to EPICS) of solenoid signals
  LabVIEW upgraded to 2019, ADC module calibrations performed
  DSG Note 2019-52
ADC Calibration for Slot 2

## Slide 28: Hall D: WEDM
19 CSS screens converted to WEDM for off-site monitoring.
  WEDM allows read-only EPICS screens to be viewed from offsite from a web browser with a JLab CUE login.
Solenoid Strain Gauges CSS screen
Solenoid Strain Gauges WEDM screen
DSG Note 2019-51, DSG Talk 2019-19

## Slide 29: Thanks Tim
whitey@jlab.org
Re: [Dsg-halld_plc] Hall D WEDM status
Dsg-halld_plc
on behalf of Timothy Whitlatch
Mon 6/24/2019 9:25 AM
Hi Tyler, This is a great start.
ComCal Environment is fine
DIRC Environment is fine
Main Gas System GUI is fine
CDC Gas system not needed
FDC gas system not needed Gas system solenoid valve monitor not needed
hall temperature is fine
Solenoid Cryo is fine
Solenoid Interlocks is fine
Solenoid strain gauges is fine
Solenoid vacuum is fine
Solenoid voltage taps is fine Can the Hall camera screens be linked?
Thanks,
Tim
Dsg-halld_plc
on behalf of Timothy Whitlatch
Mon 7/15/2019 10:30 AM
Hi Tyler,
This is very nice and very useful! Thank you for following through on this.
Tim Whitlatch
Hall D Engineer Jefferson Lab
757-269-5087
DSG’s inner child yet again!

## Slide 30: DSG: Accelerator
Populating of VME fast shutdown boards for accelerator
DSG Note 2019-25
Wirebonding
  Sample made of superconducting Nb3Sn, and what is patterned on the surface is a resonator.
  Will be cooling down sample to 4K - 2 K and measure how much energy gets dissipated in heat at a frequency around 2-3GHz. (Junki Makita)

## Slide 31: DSG: R&D and Safety
NI cRIO Test Station development
  LabVIEW program to test 18 different types of cRIO modules
  18 different types of modules tested
    DSG Note 2019- 17, DSG Note 2019-30
PLC Test Stand development
    DSG Note 2019- 23
Prevented three potentially dangerous incidents in EEL
  “An ounce of prevention …”

## Slide 32: Thanks Patrizia!
Patrizia Rossi
Thu 10/3/2019 4:45 AM
Dear Marc,
many thanks for sending out this note to let us know about the commendable behaviour of Mary Ann and Mindy.
I am very proud of my group. patrizia

## Slide 33: END
DSG makes crucial and critical contributions to all Halls
DSG staff well versed with detector hardware and software
  Controls and Monitoring systems
  Safety Interlock Systems
  Detector modelling and detector performance analysis
  Research and design
DSG staff
  Tenacious problem solvers
  Capable communicators
  And most importantly have infectious pleasant personalities

## Slide 34: Questions?