## Slide 1: Pion photo-production in the intermediate energy regime at JLab using GEANT4
Sokhna Bineta Lo AMAR
Cheikh Anta Diop University, Dakar (SENEGAL)

## Slide 2: Introduction
Pion photo-production, alternative to probe the matter
Electromagnetic and hadronic Interactions combined
GEANT4, tool to simulate Pion photo-production in comparison with Jefferson Lab physics

## Slide 3: Outline
Pion photo-production
Overview of GEANT4
GEANT4 & Hadronic models
Comparison of Cross Sections
Conclusion & future work

## Slide 4: Pions photo-production
Study of nucleonic spectrum
Combine electromagnetic & hadronic interactions
Intermediate energy range (1 ~ 30 GeV)

## Slide 5
GEANT4 : GEometry ANd Tracking 4
  Developed and maintained by an international collaboration
Purpose: simulate the interaction of particles with matter
Application: high-energy, nuclear, space and material sciences to medical physics
Ingredients
  Large flexible set of models for physical interactions of leptons and hadrons,
  Electromagnetic and hadronic processes (both elastic and inelastic,)
  Range : eV to TeV
  Extensive support of geometry and visualization tools + advanced scoring and tracking options
Overview of GEANT4 : Generalities (1/2)

## Slide 6
Particle-matter interaction
  Quantified by cross section for a given process
  No automatic implementation for cross section calculation (i.e., defined by users)
JLab & Geant4
  Intensively used for its physics and accelerator programs
  In all experimental halls (A, B & C) to model various aspects of detector packages and beam diagnostics
Overview of GEANT4 : Generalities (2/2)

## Slide 7: GEANT4 & Hadronic models (1/3)
Tens of categories of hadronic models

## Slide 8: GEANT4 & Hadronic models (2/3)
Total cross section of elastic & inelastic scattering of GEANT4 models
Physics | QGSP QGSP_BERT QGSP_BERT_EMV QGSP_BERT_EMX QGSP_BERT_TRV QGSP_BIC GSP_BIC_EMY QGSP_FTFP_BERT QGS_BIC FTF_BIC FTFP FTFP_BERT FTFP_BERT_EMV FTFP_BERT_EMX FTFP_BERT_TRV QGSC QGSC_CHIPS QGSC_EMV QGSC_QGSC QBBC_HP QBBCG | LHEP LHEP_EMV | LBE | QGSP_BERT_HP QGSP_BIC_HP | QBBC | QGSC_BERT
Group | G1 | G2 | G2 | G3 | G4 | G5
Energy | 0100 TeV | ≤10 TeV | ≤350 GeV | 0100 TeV | 0100 TeV | 0100 TeV
Elastic | Same to G2 | Same to G1 |  | Same to G4 | Same to G3 | 
Inélastic | Same to G3 |  |  | Same to G1 |  | 

## Slide 9: GEANT4 & Hadronic models (3/3)
Different models considering incidents particles
Models | Incident particles | Incident energy | Applications
Parameterized Low Energy Parameterized (LEP) High Energy Parameterized (HEP) | p, n, π, K, , , Ω, , , t, d. | 0  ~30 GeV ~10 15 TeV | Describing showers in detectors
Pre-compound (PRECO) | p, n | 0170 MeV | Used for nucleon-nucleus interactions at low energies
Cascade Bertini (BERT) Binary (BIC) | p, n, π, K, , +, - Ω-, -, 0 p, n. +, - | 0  10 GeV 0  10 GeV 0  1.3 GeV | For intermédiates Energies
String Quark –Gluon –String (QGS) Fritiof (FTF) | p, n, K, . | ~10  ~ TeV Down to much lower energies ~ 3 GeV | Recommended for use in shielding applications as well as in high energy
Chiral – Invariant – Phase – Space (CHIPS) | , , K, anti-p, anti-baryon Gamma | At rest ~1MeV  ~1GeV | For low to medium range energies
High Precision neutron (HP) | Neutrons | < 20 MeV | Requires detailed for neutron transport Can be used for radiation protection
Low Background experiments (LBE) |  | Low energies | 
Other Capture Fission Isotope production | In a nucleus Modeling sequence for - Validation of CHIPS for Pion Neutrons | At rest Low energies < 100 MeV From 100 MeV down to thermal | Useful for activation studies

## Slide 10: Comparison of Cross sections (1/4)
Jefferson Lab: Pion photo-production performed in Hall B
GEANT4: Cascade and CHIPS models
Comparison: GEANT4 and SAID
    - SAID: Scattering Analysis Interactive Dial-in
  (Model supported by a database of world-wide experimental data)
Comparison: GEANT4 & Jefferson Lab experimental data

## Slide 11: Comparison of Cross sections (2/4)
GEANT4-Cascade/SAID
(a)
(b)
(c)
(d)
Geant4 does not reproduce correctly the behavior of SAID
Some resonance states inexistent in Geant4-Cascade
Threshold distribution misrepresented
Comparison of two different physics

## Slide 12: Comparison of Cross sections (3/4)
GEANT4-CHIPS/SAID
(e)
(f)
(g)
(h)
  Excellent description of resonant states by CHIPS

## Slide 13: Comparison of Cross sections (4/4)
GEANT4-CHIPS/Jlab
(i)
(j)
(k)
  Insufficient experimental data for neutron target
  Excellent description of JLab resonant states by CHIPS

## Slide 14: Conclusion & Future work
    Consider only pions as final state:
Chart: Energy (MeV)
JLab data | 38.4553 | 52.0878 | 54.1066 | 43.2812 | 32.3304 | 29.7326 | 30.206 | 34.7054 | 29.4813 | 20.8702 | 15.7766 | 13.7095 | 12.8339 | 12.9721 | 13.0516 | 12.7761 | 12.0026 | 11.0819 | 9.5382 | 8.5212 | 7.4128 | 6.6355 | 6.0484 | 5.4704 | 4.9555 | 4.4166 | 3.9338 | 3.4848 | 3.1007 | 2.7174 | 2.4252 | 2.2136 | 2.0421 | 1.8747 | 1.5124 | 1.4035 | 1.2491 | 1.0992 | 1.0196 | 0.9699 | 0.9149 | 0.8812 | 0.829 | 0.7261 | 0.7004
GEANT4 allows to describe JLab Pion photo-production
Model: CHIPS
Need for a more selective study to better describe the experiments at JLab
    Dissociate the final states :
Overestimation Cross Sections