## Slide 1: Safety Focus for Students
Bob May
EHS&Q Deputy

## Slide 3: Topics
Situational Awareness
What can you expect?
Reporting
Equipment Use
Material Handling
Electrical Safety Reminders
Heat Stress
Where do most of our “bad day” events occur?
Bad day event example
Summary

## Slide 4: Situational Awareness
Wherever you go in the lab, it is your responsibility to understand:
  Fire exits, alarms, evacuation conditions, muster points
  E.g. how we handle bad weather events
Wherever you go in the lab, it is your responsibility to understand
  The hazards associated with your work, work of those around you
  How to mitigate those hazards
    Engineered safeguards (
    PPE (E. g. piano resistant hard hat)
    Administrative controls (procedures and protocols)

## Slide 5: What Can You Expect?
To read, understand, and act in accord with lab safety policy…
  No activity is so urgent or important that we will compromise our standards for environment, safety, and health. (paraphrase of Lab Director’s statement)
  Your work and your safety, as well as the work of those around you, depends on you
To have a JLab staff member who will help you get “connected” to your planned activities safely and efficiently
  Training, work with another experienced person
To have a meaningful and educational time at JLab

## Slide 6: Reporting
What you need to do:
  Report First Aid events to your mentor or supervisor
  Report Injuries to your mentor or supervisor
  Report near misses to your mentor or supervisor
What the Lab will do:
  Get you the help you need
  Learn from your experience
  Share
    Get relevant Tool Box briefing material to you within one work-week

## Slide 7: Equipment Use
Ladders
  Check the label and rating, working order, and select
  best height
  Look at the step treads; then look at your own
  work shoes: got a good match for traction?
Hand tools
  Right tool for the job?
    Improperly sized tools make work harder, not easier or safer
  Good working order?
    Includes tool handles and guards
    Includes wheels, bits, blades
  Do you know how to use it safely?
    This includes tool orientation to the workpiece

## Slide 8: Manual Material Handling
MMH Problem areas:
  Awkward postures (e.g., bending, twisting)
  Repetitive motions (e.g., frequent reaching, lifting, carrying)
  Forceful exertions (e.g., carrying or lifting heavy loads)
  Pressure points (e.g., grasping [or contact from] loads, leaning against parts or surfaces that are hard or have sharp edges)
  Static postures (e.g., maintaining fixed positions for a long time)
Use Team Lift: Try to find a coworker of roughly same height to help with lift

## Slide 9: Manual Material Handling, cont’d.
    Plan the lift:
      Wear appropriate shoes to avoid slips, trips, or falls
      If you wear gloves, choose the size that fits properly
        Depending on the material the gloves are made of more force may be needed to grasp and hold objects: a single pair of heat-resistant gloves can reduce your grip strength up to 40 percent
      Lift only as much as you can safely handle by yourself
      Keep the lifts in your power zone (i.e., above the knees, below the shoulders, and close to the body), if possible
      Use extra caution when lifting loads that may be unstable

## Slide 10: Manual Material Handling, cont’d.
    When lifting:
      Get a secure grip
      Use both hands whenever possible
      Avoid jerking by using smooth, even motions
      Keep the load as close to the body as possible
      To the extent feasible use your legs to push up and lift the load, not the upper body or back
      Do not twist your body. Step to one side or the other to turn
      Alternate heavy lifting or forceful exertion tasks with less physically demanding tasks
      Take rest breaks

## Slide 11: Manual Material Handling, cont’d.
Picking up a sack of ready-mix concrete:
A great example – flexible, can be powdery or slippery, weight at limit for unassisted pickup.

## Slide 12: Electrical Safety Reminders
Don’t forget to:
  Use GFCI protection with power tools
  TEST for zero energy during a Lock/Tag/Try
  Use the blind penetration permit system
  Don appropriate electrical PPE
  Maintain Arc Flash Boundaries
    Refer any changes to breakers, breaker settings, fuse values to FM&L
    Report missing breaker panel schedules to
    FM&L

## Slide 13: Heat Stress
SOTRs and selected individuals now get automatic pages when the Heat Stress Index goes above or drops below threshold values in the EH&S Manual
  If you need access to this information, see Dick Owen
Elevated temperature may mean
  Routine hydration – make it part of the work prep and plan
  Work breaks in the shade/work indoors during hot part of day
  Workplace measurements by IH to evaluate specific work areas
Heat Index 104 – 115°F | DANGER Muscle Cramps, and/or Heat Exhaustion likely Heat Stroke probable for at-risk workers | Text page sent to Supervisor/SOTRs 1040F Implement Stage 3 Process Steps. Limitations of work activity are certain. | If remainder of work day is 2-hours or more.
    Webstock Bottled water: Vendor = FORSUP (Forms & Supply) Part# NLE101243 = 24 cnt
    Webstock : SQWINCHER Vendor = GSSGRA (Grainger) Part# 1UKF(3,4,5,6) or 2EHF(2,3) = 50 cnt
Notes: Bottled water: Vendor = FORSUP (Forms & Supply) Part# NLE101243 = 24 count of 0.5L bottled water SQWINCHER electrolyte replenishment for water bottles: Vendor = GSSGRA (Grainger) Part# 1UFK3 = 50 pack sugar free orange mix 1UFK4 = 50 pack sugar free fruit punch 1UFK5 = 50 pack sugar free mixed berry 1UFK6 = 50 pack sugar free lemonade 2EHF2 = 50 pack sugar free lemon-lime 2EHF3 = 50 pack sugar free grape Also anyone with a pcard could also purchase water from local grocery stores if more convenient. IH will keep approx 100 bottles of water sqwinchers onhand through the summer.

## Slide 14: Where do most of our “bad day” events occur?
Changing work-flow
  If it isn’t going like you planned, stop and reevaluate with coworker, supervisor, EHS&Q, etc.
  If you encounter a new or unanticipated hazard, stop and reevaluate, etc.
Watch out for your co-worker
  They may not thank you, but you can save them injury
Nothing we do is so important that we need to compromise our standards for safety

## Slide 15: Bad day event example
ACC-12-0711 - Experimental RF Cavity Vacuum Window Failure (report date Aug. 12, 2012)
Student built assembly to mentor specifications; only a picture supplied by the manufacturer…
Student ignored suggestions from JLab staff.
Operated for the first time in front of mentor – failed by ejecting glass shards, minor injury, but… major near miss

## Slide 16: Summary
We generally work very safe! This is good!
  However, the way we treat ourselves and our tools in our workplace still results in incidents and injuries that are preventable and avoidable!
Theses injuries are typically to our extremities:
  Fingers, Hands, Arms, Legs
  Related to the way we handle equipment, position our bodies (extremities) and relate to hazards
Continuous questioning is key
  Don’t let your work environment dictate safety outcomes
  Modify your work environment and practices for safety