## Slide 1: Collimator
The collimator is placed about 85 cm from the target and intercepts scattered electrons from 0.78° to 3.8°
Water cooled Cu-W inner cylinder in a W box
2.1 kW power

## Slide 2: Septum Design
HRS only goes down to 12.5°, need septum to “pre-bend”
Magnetic shielding
Tune for CREX

## Slide 3: Region Near the Septum
Collimators
septum magnet
target
HRS-L
Q1
HRS-R
Q1
Former O-Ring location
New Collimator
& Shielding

## Slide 4: Simulation comparisons
D. McNulty
L. Zana
J. Mammei
P. Degtiarenko
We’ve performed comparisons of neutron energy spectra from various simulation packages:
FLUKA
GEANT3
GEANT4
MCNPX
5 mm Pb

## Slide 5: Neutron shielding
PREX II collimator increases neutron production, but localizes it so we can shield it
Background rates from CREX ~10x smaller than PREX II, so shielding scheme for PREX II will be overkill for CREX

## Slide 6: Polarized Beam
velocity
spin
@

## Slide 7: Polarized Electron Source
photoemission of electrons from GaAs
"Bulk" GaAs typical Pe ~ 37%
theoretical maximum - 50%
 "Strained" GaAs = typical Pe ~ 80% theoretical maximum - 100%
"Figure of Merit"  I Pe2

## Slide 8: Helicity reversals
Double-wien
Rapid, random helicity reversal
Electrical isolation from the rest of the lab
Feedback on Intensity Asymmetry
IHWP

## Slide 9: Injector

## Slide 10: Precision Polarimetry
Qweak requires measurement of the beam polarization to
Strategy: use 2 independent polarimeters
Møller Polarimeter
Compton Polarimeter
Use new Compton polarimeter to provide continuous, non-destructive measurement of beam polarization
Known analyzing power provided by circularly-polarized laser beam
Use existing Hall C Møller polarimeter to measure absolute beam polarization to <1% at low beam currents
Known analyzing power provided by polarized Iron foil in high magnetic field

## Slide 11: Compton Polarimeter

## Slide 12: Typical parameters
CDR Eq. 69
for Qweak)
(
From CDR Eq. 22

## Slide 13
(Not to scale)
The electrons hit the detector (light grey strips on darker grey substrate) in a thin stripe (shown as orange)
In the real detector protoype there are 192 strips on a 46x10mm2 detector, so each strip is about 0.240 mm wide
The width of the beam stripe is about 80 μm
The strips are 0.5 to 1 mm thick

## Slide 14
Assume
for diamond
for silicon
Using these numbers I get a total dose of 27 Mrad per strip for both diamond and silicon (approximately twice that of Qweak detectors)
For the 1064 nm laser and 20kW power I get 108 Mrad
for all three runs (344 PAC days)

## Slide 15: Kinematics of Compton Scattering

## Slide 16: Compton asymmetry

## Slide 17: Precision Polarimetry

## Slide 18: P I T A Effect
Laser at Polarized Source
Polarization Induced Transport Asymmetry
where
Transport Asymmetry
Intensity asymmetry
Δ drifts, but slope is ~ stable Feedback on Δ
Perfect DoCP
Scanning the Pockels Cell voltage = scanning the residual linear polarization (DoLP)
Intensity Asymmetry (ppm)
Pockels cell voltage D offset (V)

## Slide 19: False asymmetries from helicity correlated beam properties

## Slide 20: Polarized Beam Properties
Beam Parameter | Achieved (OUT-IN)/2 | “Specs”
charge asymmetry | 0.09 +/- 0.08 | 2 ppm
x position difference | -19 +/- 3 | 40 nm
y position difference | -17 +/- 2 | 40 nm
x angle difference | -0.8 +/- 0.2 | 4 nrad
y angle difference | 0.0 +/- 0.1 | 4 nrad
energy difference | 2.5 +/- 0.5 | 34 eV
Beam halo (out 6 mm) | < 0.3 x 10-6 | 10-6
Charge Asymmetry
Run Number
w/ feedback
Dx (nm)
Dqx (nrad)
DE (keV)
Dqy (nrad)
Dy (nm)
During G0
1 nm is one-billionth of a meter. The width of human hair is 50,000 nanometers!!!

## Slide 21: Intensity Feedback
Adjustments
for small phase shifts
to make close to
circular polarization
Low jitter and high accuracy allows sub-ppm
cumulative charge asymmetry in ~ 1 hour
28

## Slide 22: Charge normalization

## Slide 23: Beam Monitor Calibrations

## Slide 24: Experimental Techniques to Reduce the Helicity-Correlation in the Beam
Careful alignment of the Pockels Cell
Steering Scan
Phase Gradient Scan
Intensity Asymmetry (IA) Cell
Rotatable Half Wave Plate (RHWP)
PITA Scan

## Slide 25: Linear Regression
Just the sum of the parity-violating and helicity-correlated yields
Assume a linear relationship between
helicity-correlated yield and beam parameters
Correlation slopes, detector responses
This is the measured asymmetry
Making all of the above substitutions
yields this expression
Assume the parity-violating yield is much
bigger than the helicity-correlated yield and
substitute this into the above equation.

## Slide 26: Linear Regression (cont…)
Beam parameter difference
Average yield
After some algebra, you get this really
cool expression, where
real asymmetry
false asymmetry due to helicity-correlated fluctuations
But we don’t know the slopes! We use
multiple linear regression to find them.

## Slide 27: Multiple Linear Regression
Just the change in yield due to
helicity-correlations.
least-squares
method
6 equations & 6 unknowns
Eliminate residual helicity correlations by correcting yields through linear regression
Deviations of the measured yield and beam parameter from the means of their parent distributions
We can write this in matrix form and invert
to find the slopes

## Slide 28
Simulation
Dependence on Beam Motion

## Slide 29
Slopes from natural beam motion

## Slide 30: Beam Modulation

## Slide 31: Geometrical Symmetry
Transverse
Reduce sensitivity to beam fluctuations
k’
n
ˆ
Pe
k

## Slide 32: Target
World’s highest power cryogenic target ~2.5 kW!
Designed with computational fluid dynamics (CFD) to reduce density fluctuations
Fluid velocity
46 ppm at 182 µA, 4x4 mm2 raster!
Notes: beam current 180 uA 35cm long

## Slide 33: Target
Notes: beam current 180 uA 35cm long

## Slide 34: Target Studies

## Slide 35: Raster synch