## Slide 1
HUGS June 17 2016
1
9125B ET Photomultiplier Tubes with a Wavelength Shifting Paint for a Gas Cherenkov Counter
Scott Barcus1, Bogdan Wojtsekhowski2, Todd Averett1
1: The College of William and Mary
2: Thomas Jefferson National Accelerator Facility

## Slide 2
Polarization of Quark in Polarized Neutron (A1n )
Precision measurement of the neutron virtual photon asymmetry in the deep inelastic scattering (DIS) region.
  Previously measured up to xBj=0.6.
  Experiment will measure up to xBj=0.71 at 6.6 and 8.8 GeV beam energies.
Constrain theoretical predictions.
  Relativistic Constituent Quark Model (RCQM) and perturbative QCD (pQCD) predict as xBj goes to one A1n will also approach unity.
  Direct comparison of pQCD theory and experiment.
  Study importance of quark orbital angular momentum.
HUGS June 17 2016
2
Notes: -A1n became positive around xBj =0.5.
-Expect A1n to approximately double from x=0.6 to x=0.71.
-Shaded area is RQCM prediction.
-pQCD upper solid line.
2

## Slide 3
New A1n Measurement
Scatter electrons off of polarized 3He target.
  ~50% polarization with 30 μA beam.
Big Bite spectrometer will take most of the data.
  Large momentum acceptance.
  Large solid angle
Expect at least a factor of two improvement in statistics at low xBj.
HUGS June 17 2016
3

## Slide 4
HUGS June 17 2016
4
Gas Ring-ImagiNg CHerenkov (GRINCH) Detector
Previous Big Bite gas Cherenkov had very large background.
  Source determined to be few MeV photons in beam line.
    These photons produced visual photons in glass of 5’’ PMTs. Visual photons kick out Compton electrons which produce Cherenkov radiation in the glass.
    Long ADC gate, large cross sectional area, thick glass faces.
    Highly sensitive to magnetic fields.
  New experiment will run at 30 μA with longer target (50 cm active length).
  Expect at least four times the previous rate.
Need new gas Cherenkov detector.
Notes: -Especially large on side closest to beam line.

## Slide 5
GRINCH Detector
Basic Features.
  ~510 29mm diameter PMTs.
    0.05 times less cross sectional area and three times thinner glass.
    PMT array magnetically shielded.
  Four Cylindrical mirrors reflect light onto PMTs.
  C4F10
  No ADC. Look for timing clusters of about 10 PMTs in 5-10 ns window.
Want to collect as many photoelectrons as possible.
  Expect ~36 photoelectrons per event.
  Cherenkov spectrum is more intense below the PMTs range.
  Apply a wavelength shifting (WLS) paint to shift more photons into the sensitive region.
HUGS June 17 2016
5
Notes: -More PE since we will always collect fewer than predicted due to losses (absorption etc.)
5

## Slide 6
HUGS June 17 2016
6
WLS Paint
EJ-299-31E
  Composed of polyvinyltoluene (PVT) binder and fluorescent dopants dissolved in a xylene solvent.
  Flourescents absorb photons and re-emit them at a higher wavelength
    Decay time of 2 ns.
    >90% quantum efficiency.
  K. Allada et al., PMT Signal Increase Using a Wavelength Shifting Paint, arXiv:1502.01772

## Slide 7
HUGS June 17 2016
7
Cherenkov Photons from Cosmic Rays
Method to produce photons with Cherenkov light spectrum.
  Cosmic rays striking quartz silica crystal produce Cherenkov radiation.
  Spectrum is constant and stable.
Notes: -Novel.

## Slide 8
HUGS June 17 2016
8
Experimental Apparatus
  Two PMTs placed touching the crystal with a scintillator above the crystal to form a coincidence.

## Slide 9
HUGS June 17 2016
9
Painting the PMT Faces
How to Apply Paint Uniformly?
  Place an open cylinder with two wires stretched across the top over the PMT face.
  Apply WLS paint and spread over face with the blunt edge of a razor using the wires as guides.
  Wire diameter then determines the paint thickness.
  Allow 24 hours to dry.

## Slide 10
HUGS June 17 2016
10
Measuring WLS Effects
Once painted each PMT observes a cosmic spectrum for 21 hours.
Thickness is then measured.
  Four small areas of the WLS paint are then scraped with a razor blade.
  A coordinate measuring machine then determines the thickness of the paint layer.
WLS paint is then scraped off of the PMT face with a razor and cleaned with alcohol.

## Slide 11
HUGS June 17 2016
11
Measuring WLS Effects
Unpainted PMT then observes cosmic spectrum for 21 hours.
By analyzing the shift in the peak ADC signal the change in the number of photoelectrons can be determined.
This peak is fit by a Gaussian to describe the pedestal and an exponential to describe the peak signal.
The ratio of these fits' parameters gives the change in photoelectrons detected.
Unpainted Tube
Painted Tube
Notes: -first peak = single PE.

## Slide 12
HUGS June 17 2016
12
Results
WLS paint increased the number of photoelectrons detected by up to ~48%.
Almost always increased photoelectrons detected.
Paint thickness vs. photoelectrons detected roughly quadratic.

## Slide 13
Results
Paint thickness roughly controllable through wire diameter.
Stable region from about 10 – 40 microns.
  Choose wire diameter of 80 microns.
  Average photoelectron gain of 23.7% for 80 micron wire.
HUGS June 17 2016
13

## Slide 14
WLS Paint Model
Do these results make sense?
What do we need to know to check these results?
  Cherenkov light spectrum
    Known
  WLS paint absorption spectrum
    Measured by William and Mary
  WLS paint emission spectrum
    Measured by FermiLab (Dr. Anna Pla-Dalmau)
  WLS paint QE
    Given by company
  Epoxy transmission spectrum
    Measured by JLab (Dr. Carl Zorn)
  PMT QE (company)
    Given by company
HUGS June 17 2016
14

## Slide 15
Measuring the Absorption Spectrum
Use a UV flashlight and a spectrometer to measure the absorption spectrum.
Flashlight emits little light in the deep UV (especially below 300 nm).
  Need long integration times.
Must break absorption spectrum into three segments.
  Deep UV (200-370 nm), Near UV (370-405 nm), Visible (405-615 nm).
HUGS June 17 2016
15

## Slide 16
HUGS June 17 2016
16

## Slide 17
Calculate Photoelectron Gain from WLS Paint
1. Determine the number of photoelectrons detected by the PMT with the WLS paint.
  (a) Determine the total light absorbed and re-emitted by the WLS paint reaching PMT.
  (b) Determine the total amount of light transmitted through the paint reaching the PMT.
2. Determine the number of photoelectrons detected by the PMT without the WLS paint applied.
3. Take the ratio to find the gain in photoelectrons due to the WLS paint.
HUGS June 17 2016
17

## Slide 18
Photoelectron Gain from WLS Paint
HUGS June 17 2016
18

## Slide 19
HUGS June 17 2016
19

## Slide 20
HUGS June 17 2016
20
Conclusions
Cosmic rays can be successfully used to create a Cherenkov spectrum to simulate a detector.
The WLS paint significantly increased the number of Cherenkov Photoelectrons detected.
WLS paint thickness roughly quadratic vs. photoelectron gain.
Model to calculate photoelectron gain is in agreement with experiment.
Upcoming Work:
  GEANT4 Monte Carlo
  New WLS paints
  In situ testing

## Slide 21
HUGS June 17 2016
21
Acknowledgments
Collaborators
  Dr. Bogdan Wojtsekhowski
  Dr. Todd Averett
The W&M Hadronic Physics Group
Department of Energy
JLab
Special Thanks
  Kurtis Bartlett
  Dr. Carl Zorn
  Dr. Anna Pla-Dalmau

## Slide 22
HUGS June 17 2016
22
Questions?