PrimEx Note 049

Event Configuration of PrimEx Data

Liyang Jiang

Aug, 2007

Event Configuration of PrimEx data

Liyang Jiang

UNCW/CIAE

While running the prim_ana program, the PrimEx experimental data are stored in several groups. These groups are called banks. Each bank is consisted of two parts: bank header and bank body.

Bank Header Structure (bankHeader_t)

Every bank has a same bank header structure. The general information about the bank, such as size, name and flags of the bank are stored in this part. (Fig 1)

There are five values in the bank header: number of rows (nrow), maximum number of rows (maxrows), size of data structure for a single row (size), name of the bank (name[16]), bank flags (flags).

Table 1: Data in Bank Header

| Variables | TYPE | Description |
| --- | --- | --- |
| nrow | int | Number of records in this event |
| maxrows | int | Number of rows for which memory is allocated in the bank |
| size | int | Size of data structure for a single row |
| name[16] | char | Name of bank |
| flags | unsigned int | Bit-wise flags |

The banks are divided in two Classes: Event-bank and Nonevent-bank. The event-banks store the data acquired event by event; and the nonevent-banks store the data which can’t be acquired event by event, such as BPM, Beam position, Beam current, Temperature, Humidity etc.

Event-banks

The configuration of event-banks is shown in Fig 2. The data of each event are stored in different banks according the nature of the signals. For example, the data from Tagger T-counter are stored in TAGT bank, from HYCAL are sent to HYCAL bank, and so on..

Depending on the types of data stored in the body of banks, the event banks are divided into four types:

1 Primitive banks;

2 Raw data banks;

3 Pre-analyzed banks;

4 Reconstructed banks;

1. Primitive banks:

The primitive banks store the electronics identity of signals collected in one event. HARDWARE, TRIGGER, TRIGGER_PHASE and EVENTID banks are primitive banks.

The TRIGGER and TRIGGER_PHASE banks save the latch word which indicates which trigger created the event. In TRIGGER_PHASE bank also saves the run number and the phase of the event.

The data in EVENTID bank are created by the data acquisition system. It stores the run number, event number, and the system time when the event was created.

Table 2: Variables and corresponding Data in Primitive banks

| TRIGGER bank |  |  |
| --- | --- | --- |
| Latch | Trigger latch word |  |
| live1 | Live time gated scaler driven by 195kHz clock |  |
| live2 | Ungated scaler driven by same 195kHz clock |  |
| Time | Time of the event according to ROC’s clock |  |
| TRIGGER_PHASE bank |  |  |
| trigger | A structure stores all data in TRIGGER bank |  |
| runnumber | The run number |  |
| Phase | The phase in the run (3 = data collect phase) |  |
| EVENTID |  |  |
| Time | Unix time of the event |  |
| relative_time | Real time passed since beginning this file (sec) |  |
| run_start_time | Start time of the run from online |  |
| roc_start_time |  |  |
| last_time |  |  |
| last_live2 |  |  |
| event_number |  |  |
| event_class |  |  |
| event_status |  |  |
| run_number | The run number |  |

HARDWARE bank stores all the data from the detectors.  The data in HARDWARE bank are stored as rocid, slot, channel and val. The values rocid, slot and channel are the ids of crate, slot and channel, from which the signal was collected. One set of these ids corresponds to one detector and the val stores the output value of this detector.

2. Raw Data Structure and Banks:

Translation is a procedure to map out and rewrite data from HARDWARE bank into several raw data banks which are corresponding to individual detectors.

The data in Raw Data Banks are translated from the HARDWARE bank. Each Raw Data Bank stores the data from a certain detector.

The structure of raw data banks is composed of bank header structure and raw data structure. (Fig 3)

In different banks, the id and val store the raw data from different detectors. The raw data banks are listed in Table 3.

Table 3: The List of Raw Data Banks

| RAW DATA BANKS’ NAMES | id | val |
| --- | --- | --- |
| TAGT | id of T counter | TDC of T counter |
| TAGTL | id of T counter | TDC of T counter left PMT |
| TAGTR | id of T counter | TDC of T counter right PMT |
| TAGE | id of E counter | TDC of E counter |
| PST |  | TDC of Pair Spectrometer paddle |
| PSA |  | ADC of Pair Spectrometer paddle |
| TACA |  | ADC of Total Absorption Counter |
| HYCAL | Crystal ID code | ADC of crystal |
| HTRIGT |  | TDC of HYCAL trigger group |
| HTRIGA |  | ADC of HYCAL trigger group |
| VETOA |  | ADC of Veto Counter |
| VETOT |  | TDC of Veto Counter |
| TRIGT |  | TDC of trigger bits |

For example, the HYCAL bank stores the raw data from Hycal. The id is the id number of Lead glass or PWO crystals. And the val is the adc out put of this crystals.

3. Pre-analyzed banks:

The raw data banks store the digital output of ADC and TDC. To make the values more convenient to use, it is necessary to subtract pedestals and convert these raw numbers into physical values, such as energies, times and etc. The banks store converted values are called pre-analyzed banks. The pre-analyzed banks and corresponding raw data banks are listed in Table 4.

Table 4: List of Pre-analyzed Banks

| Pre-Analyzed Bank | Raw Bank |
| --- | --- |
| TAGTHIT* | TAGT |
| TAGEHIT* | TAGE |
| PSHIT | PST & PSA |
| HYCALHIT | HYCAL |
| VETOHIT | VETOA &VETOT |
| TRIGTHIT | TRIGT |

*the id in the banks is T/E channel id, instead of T/E counter id in corresponding Raw Banks.

4. Reconstructed banks: TAGM, TRIGPHOTON, HYCALCLUSTER etc.

Some physical variables are reconstructed with the raw data, such as the time difference, the cluster energy and position. The banks which store these kinds of data are reconstructed banks. The most important Reconstructed banks are TAGM, TRIGPHOTON and HYCALCLUSTER.

The data in TAGM bank are reconstructed from TAGTHIT, TAGT_LR_HIT & TAGEHIT banks. When the time and energy of a hit in TAGTHIT bank matches to those of a hit in TAGEHIT bank, these hits are considered as a real tag hit. And the e of TAGEHIT and t of TAGTHIT are stored in TAGM bank as the e and t of the real tag hit.

Table 5: Values stored in TAGM bank

| Variable | Comment | Value |
| --- | --- | --- |
| Energy | Energy of the photon (GeV) | E in TAGEHIT bank |
| T | T-counter time (ns) | t in TAGTHIT bank |
| e_t | E-counter time (ns) | t in TAGEHIT bank |
| Status |  |  |
| Tid | T channel id | id in TAGTHIT bank |
| Eid | E channel id | id in TAGEHIT bank |
| Ehit | Index of hit in TAGEHIT bank | nrow in TAGTHIT bank |
| Thit | Index of hit in TAGTHIT bank | nrow in TAGEHIT bank |

TRIGPHOTON:

TRIGPHOTON bank is reconstructed from TAGM bank and TRIGTHIT bank.

Table 6: Values stored in TRIGPHOTON bank

| Variable | Comment | Value |
| --- | --- | --- |
| Energy | Energy of the photon (GeV) | energy in TAGM with t~100ns |
| T | T-counter time (ns) | t in TAGM ~ 100ns |
| Tid | T channel id | tid in TAGM of selected event |
| Eid | E channel id | eid in TAGM of selected event |
| Id | Trigger bit | id in TRIGTHIT |
| Tdiff | T-counter – trigger time diff. | t in TAGM – t in TRIGTHIT |

HYCALCLUSTER bank is reconstructed from HYCALHIT bank. It stores the data of the clusters in Hycal.

Table 7: Some Values stored in HYCALCLUSTER bank

| Variable | Comment | Value |
| --- | --- | --- |
| E | Cluster’s energy (GeV) | Sum of cluster cells’ energies |
| Time | Cluster’s time (ns) |  |
| X | x position | reconstructed with wi=Ei |
| Y | y position | reconstructed with wi=Ei |
| Z | Distance target to hycal |  |
| X1 | x position | reconstructed with wi=a+lnEi |
| Y1 | y position | reconstructed with wi=a+lnEi |

－Calibration constants

The calibration constants used in creating pre-analyzed and reconstructed banks are stored in PrimEx database. The list of currently available constants can be found at the webpage http://clasweb.jlab.org/cgi-bin/primex/caldb/cq.pl.

To switch the calibration constants, you may modify the code of the detector. The code getting the calibration constants for each detector is the “*_brun.cc” file in the “src/libraries/*/”. For example: “gain5_iter” and “pi0_gain” are two options of PWO crystals gains and Lead Glass gains of 5X5 cluster reconstruction. To switch the “gain5_iter” to “pi0_gain” calibration constants of hycal, modify the lines in “src/libraries/hycal/hycal_brun.cc” file as below.

you have to change in place

get_from_db("crystal", "gain5_iter", CRYSTAL_BLOCKS, &HYCAL_GAINS[1000], RunNumber);

get_from_db("glass", "gain5_iter", GLASS_BLOCKS, &HYCAL_GAINS[0], RunNumber);

to

get_from_db("crystal", "pi0_gain", CRYSTAL_BLOCKS, &HYCAL_GAINS[1000], RunNumber);

get_from_db("glass", "pi0_gain", GLASS_BLOCKS, &HYCAL_GAINS[0],   RunNumber);

－Photon flux

The photon flux is not a data stored in the banks, it is saved in “Fluxnnnn.txt” file which is created while running prim_ana program with “–Cconfig.xml” argument. The following is an example of config.xml file, which can be used to generate flux of E channel:

<?xml version="1.0" ?>

<pconfig>

<beam_trip>1</beam_trip>

<flux_output>1</flux_output>

<Eflux_output>1</Eflux_output>

<livetime_sigma>5.0</livetime_sigma>

<DCOMPTON_GAINS>1</DCOMPTON_GAINS>

</pconfig>

To generate flux of T channel, delete the “Eflux_output” line.

Typical size of banks

The size of banks are different between Compton run and pi0 run. The plots of Fig 4 to Fig 7 demonstrate the average size of each bank in levels.

Fig 4: The average size of HARDWARE Bank of pi0 run and Compton run

Fig 5: The average size of Raw Data Banks of pi0 run and Compton run

Fig 6: The average size of Pre-analyzed Banks of pi0 run and Compton run

Fig 7: The average size of Pre-analyzed Banks of pi0 run and Compton run

Fig 8: The relationship of Hardware bank and its daughter banks

# Text boxes

Fig 1. Bank structure and bankHeader structure

Fig 3: Raw data bank structure

Fig 2: Event Data Banks

Fig 3: Different type of Event-banks

H

A

R

D

W

A

R

E

TAGE

TAGT

TAGTL

TAGTR

HYCAL

TACA

PSA

PST

HTRIGA

HTRIGT

VETOT

VETOA

TRIGT

TAGEHIT

TRIGPHOTON

TAGM

TAGT_LR

HYCALHIT

TACHIT

PSHIT

HYCALCLUSTER

VETOHIT

TRIGTHIT

Raw Data

Pre-Analyzed

Reconstructed

HYCALASSOC

TAGTLHIT

TAGTHIT

TAGTRHIT

TAGT_LR_HIT

TACT

PSR

Primitive Data