## Slide 1
SANE Collaboration
( E07-003)
Anusha Liyanage
Hampton University
January 12, 2010
Measurement Of the Proton Form Factor Ratio at High Q2 by Using The Double Spin Asymmetries

## Slide 2: CONTENTS
Experimental Setup
Physics Motivation &
HMS Kinematic
Analysis Status
SIMC Simulation
Work Status

## Slide 3
● BigCal lead glass calorimeter:
main detector used in GEp-III.
● Tracking Lucite hodoscope
● Gas Cherenkov: pion rejection
● Tracking fiber-on-scintillator
forward hodoscope
● BETA's characteristics
– Effective solid angle = 0.194 sr
– Energy resolution 8%/√E(GeV)
– 1000:1 pion rejection
– vertex resolution ~ 5 mm
– angular resolution ~ 1 mr
● Target field sweeps low E background
– 180 MeV/c cutoff
Big Electron Telescope Array – BETA
BigCal
Tracker
Cherenkov
Lucite Hodoscope
Used for electrons detection.

## Slide 4: High Momentum Spectrometer-HMS
DC1
DC2
Cerenkov
S1X
S1Y
S2Y
S2X
Calorimeter
HMS Vacuum pipe exit

## Slide 5: Target
• Refrigerator - 1 K
• Magnetic Field - 5 T
• NMR system
• Microwaves - 55 GHz - 165 GHz
• C ,CH2 and NH3
• Dynamic Nuclear Polarization (DNP) polarized
the protons in the NH3 target up to 90%
• Used microwaves to excite spin flip transitions
• Polarization measured using NMR coils
The Polarized Target Assembly

## Slide 6
● Upstream beam line:
– Chicane Magnets
– Both fast raster and slaw rasters
– BPM's and BCM's
– Target Beam Position Monitor (Secondary Emission Monitor):
● needed to determine beam raster position (1 cm radius spiral)
Downstream beam line:
– In-hall beam dump
(Used at the parallel magnetic field configuration)
– He gas bag plus short beam pipe section
(Used at the perpendicular mag. Field configuration)
SANE – Subsystems

## Slide 7
SANE Layout
BETA (40°)
HMS (14°- 48°)
BigCal
Lucite Hodoscope
Gas Cherenkov
Forward Hodoscope
B at 80° OR 180°
Polarized Target
Target Beam
position monitor
Beam Line
e-
P
ΘP
Θe

## Slide 8: Physics Motivation
The raw asymmetry,
The elastic asymmetry,
The beam-target asymmetry,
Here,
At Q2=6.259 (GeV/C)2
The calculated asymmetry vs μGE/GM

## Slide 9
Dramatic discrepancy !
between Rosenbluth and recoil polarization technique.
HMS Kinematic For Proton
E Beam GeV | 4.725 | 5.891
P GeV/C | 3.585 | 4.170
Θ (Deg) | 22.30 | 22.00
Q2 (GeV/C)2 | 5.170 | 6.259
e-p Events | ~153 | ~948

## Slide 10: Analysis Status
HMS Detector Calibration is Completed.
Detector Efficiency.
Modification of the DC tracking efficiency algorithm is done.
(The tracking efficiency is increased by 15%-20%)
Extracted the elastic events.
Correlation corrections are completed.

## Slide 11: Tracking Efficiency Corrections
Could increase the tracking efficiency
by 15%-20%
by modifying the tracking algorithm.
Tracking Efficiency Vs Run Number

## Slide 12: 1. Polygon cut on the BigCal effective area
Used the polygon cut on the
BigCal effective area
The Tracking Efficiency
increased
only ~ 1-2 %.
Y_clust positions Vs x_clust positions

## Slide 13: Extracted the elastic events
Momentum Difference , dPel_hms
By using slow raster y offset = - 0.66 cm

## Slide 14: X/Y position difference
X position Difference
Y position Difference

## Slide 15: Correlation Corrections for ….
The dPel_hms vs srast_y ....
The Y position difference Vs srast Y ….

## Slide 16: SIMC Simulation
HMS Single Arm Variables
HMS Coincidence with BIGCAL Variables
SIMC Simulation
Experimental Data

## Slide 17: Work Status
HMS Calibration – completed
Elastic event selection – completed
          To Do …..
Improve SIMC simulation
Work on the Efficiency Corrections
Extract the Asymmetry and the GE/GM Ratio