Constraining the ME flux via nu-e elastic scattering
Wenting Tan

---
Physics Motivation
- Incident beam from NUMI beamline
  Neutrino Energy distribution
  has an uncertainty (>10%).
- Get the flux be better determined
  through a standard candle process

---
Neutrino Electron Elastic Scattering
- From SM, cross-section is known to 1% precision, we can infer the flux uncertainty. (better than 10%)
Size 25{ {{dN(T)} over {dT}} = Int { {dE rsub{ν}} * {{dΦ (E rsub{ν})} over {dE rsub{ν}}} * {{dσ (T, E rsub{ν})} over {dT} }}}
size 20{ {ν} } rSub { size 15{μ} } +e rSup { size 15{ - {}} } rightarrow {ν} rSub { size 15{μ} } +e rSup { size 15{ - {}} } {}
size 18{ {ν} } rSub { size 12{μ} } +size 18{e} rSup { size 12{ - {}} } rightarrow size 18 {{ν}} rSub { size 12{μ} } +size 18{e} rSup { size 12{ - {}} }{}
size 12{Z rSup { size 8{0} } } {} size 16{ {ν} } rSub { size 8{μ} } {} size 12{e rSup { size 8{ - {}} } } {} size 16{ {ν} } rSub { size 8{μ} } {} size 12{e rSup { size 8{ - {}} } } {}

---
      Fermi constant
size 20 {G sub{μ}=1.16637(1) times 10 sup {-5} Gev sup {-2} }
size 20 {s sup{2} = sin sup{2} θ sub{W} ≈ 0.23149 ± 0.00015}
SM a and b parameter, here
weak mixing angle:
factor
size 20 {θ sub{W}}
size 20 {θ sub{W}}
size 20 {{2 G sup {2} sub {μ} m sub{e}} over π = 1.5 times 10 sup{-41} GeV sup{-1} cm sup{2}}
 Electron Kinetic
Energy
Distribution
size 20 {{dN(T)} over {dT} = int dE sub{ν} {dΦ sub{i} (E sub{ν})} over dE sub{ν} {dσ sub{i} (T, E sub{ν})} over dT} newline size 20 { == Acceptance times sum sub {j} {{dΦ sub{i} (E sub{ν})} over {dE sub{ν}}} ΔE sub{ν j} times {{dσ sub{i} (T, E sub{ν})} over dT }}
For each Ev bin,
the electron
kinetic energy
T distribution
 Adjusting the Flux;
To re-weight the flux
To get the smallest
size 20 {χ sup{2}}
size 20 {θ}
size 20 {{dN sub{predicted}(T)} over dT}
size 20 {{dN sub{detected}(T)} over dT}
and
  T, vertex x, y, z,
dependent

---
Sensitivity of Electron Kinetic Energy shape vs re-weighted flux (MC)
Flux Error Band

---
Using e-ν elastic scattering to determine flux
- Review Low Energy Beam (Jaewon's work)
  cross-section is small
  low event rate
  not enough statistics
- Scaling studies indicated reasonable statistics for ME
  -- signal events ( ν e ν e ) statistics in ME flux (Genie MC)
  -- background

---
Event Sample in ME and LE
size 36{ 10 rsup{21}}
Pot
LE Ev
We get more statistics using ME
ME Ev

---
Efficiency Energy Cut : KEe>0.8Gev
(energy that can be detected by the detector)
Nev: 2647 (86.6% remained)
LE plot
ME El plot
Nev: 8633 (89.7% remained)

---
Event Rate: ME Compare with LE
Event type: NUE_EL ; 10^21 pot; from Genie MC
iev
Entire Target
Efficiency cut of El>0.8 Gev
3057
2647 (86.6% remained)
LE
9626
8633 (89.7% remained)
ME

---
Fiducial Cut for the signal event
10^21 pot ME NUE-EL
tracker: z vertex: (5.99m, 8.34m)
x,y vertex: radius 0.85m circular
(hexagonal cut later)
1103, bigger events size, Relative more statistics

---
 Related Events in MINERvA
 99% beam, little cross-section
        Elastic Scattering
        Likely dominant background
size 18{ {ν} } rSub { size 12{μ} } +size 18{e} rSup { size 12{ - {}} } rightarrow size 18 {{ν}} rSub { size 12{μ} } +size 18{e} rSup { size 12{ - {}} }{}
{bar { size 18{ {ν} } rSub { size 12{μ} } }} +size 18{e} rSup { size 12{ - {}} } rightarrow {bar {size 18 {{ν}} rSub { size 12{μ} }}} +size 18{e} rSup { size 12{ - {}} }{}
 1% of beam, bigger cross-section
(small fraction but more possible)
size 18{ {ν} } rSub { size 12{e} } +size 18{n} rightarrow size 18{e} rSup { size 12{ - {}} }{} + size 18 {p}
size 18 { { size 18{ {ν} } rSub { size 12{e} } }} +size 18{p} rightarrow size 18{e} rSup { size 12{ - {}} }{} + Δ sup{++} }

---
Background CCQE:
size 18{ {ν} } rSub { size 12{e} } +size 18{n} rightarrow size 18{e} rSup { size 12{ - {}} }{} + size 18 {p}
Purify the signal events;
Cut out:
Hadronic energy > 125Mev, Electron energy>125Mev, to remove CCQE events.
For energy of protons that lower than 125Mev (can not be detected):
      Electron angle
Electrons from these background are always have large and higher energy
Cut out: to remove the rest events
size 20 {θ}
size 20 {θ}
size 25 {E sub{e} (1-cosθ)>0.00025}

---
Geant4 Study
Electron in the detector (applied the Electron reconstruction tool on ME flux)
Electron shower reconstruction
size 20 { {dN(T) } over dT }