## Slide 1
Spin
Asymmetries of the
Nucleon
Experiment
( E07-003)
Anusha Liyanage
APS April Meeting, February 15, 2010
Measurement Of the
Proton Form Factor Ratio
at High Q2
by Using The
Double Spin Asymmetries

## Slide 2: Outline
Physics Motivation
Experiment Setup
Elastic Kinematic
Data Analysis
Error Propagation
SIMC Simulation
Future Work
BETA Detector
HMS Detector
Polarized Target

## Slide 3
Dramatic discrepancy !
Physics Motivation
RSS (Jlab)
Q2 = 1.5 (GeV/c)2
M. Jones et al., PRC74 (2006) 035201
Dramatic discrepancy between
Rosenbluth and recoil polarization
technique.
Multi-photon exchange considered the
best candidate for the explanation
New data points for the
Polarization transfer technique
using the exp. GeP-III, Hall C
at Q2 = 5.2 (GeV/c)2 , 6.7 (GeV/c)2
and 8.5 (GeV/c)2
5.17
6.25
SANE

## Slide 4
Experiment SANE
Elastic (e , e’p) scattering from
the polarized NH3 target using a longitudinally polarized electron
beam
(Data collected from Jan – March ,2009)
HMS for the scattered
proton detection
Central angles are
22.3° and 22.0°
Solid angle ~10 msr
e-p → e-p
Hall C at Jefferson Lab
BETA for coincidence electron
detection
Central scattering angle :40 °
Over 200 msr solid angle
coverage

## Slide 5
BigCal
Tracker
Cherenkov
Lucite Hodoscope
Big Electron Telescope Array – BETA
3 planes of Bicron Scintillator provide
early particle tracking
Forward Tracker
N2 gas cerenkov
Provides particle ID
8 mirrors and 8 PMTs
Cerenkov
28 bars of 6cm wide Lucite
Bars oriented horizontally for Y
tracking
PMTs on either side of bar provides
X resolution
Lucite Hodescope
Lead glass calorimeter
1744 blocks aprx. 4cm x 4cm
energy and position measurement
Big Cal (GEP III Collaboration)

## Slide 6
High Momentum Spectrometer – HMS
X,X’
V,V’
U,U’
α
∆Z = 81.2 cm
Drift Cham I
Drift Cham II
α = ± 15°
(β = L/c x TOF)
Time of particle
detection, T
Length of the
particle trajectory, L=2.2 m
S1 plane
S2 plane
X1, Y1
X2, Y2
4 layers of 10 cm x 10cm x70cm blocks stacked 13 high.
Used as a Particle ID
Lead Glass Calorimeter
Each plane contains 10 to 16 Scintillator paddles
with PMTs on both ends
Each Paddle is 1.0 cm thick and 8.0 cm wide
Fast position determination & triggering
Time of Flight (TOF) = T2-T1 determines β
Hodescopes
Two mirrors (top & bottom) connected to two PMTs
Used as a Particle ID
Gas Cerenkov
Each plane has a set of alternating field and
sense wires Filled with an equal parts
Argon-Methane mixture
Track particle trajectory by multiple planes.
χ2 fitting to determine a straight trajectory.
Drift Chambers

## Slide 7: Polarized Target
• C ,CH2 and NH3
• Dynamic Nuclear Polarization (DNP) polarized
the protons in the NH3 target up to 90%
• Used microwaves to excite spin flip transitions
• Polarization measured using NMR coils
• Refrigerator - 1 K
• Magnetic Field - 5 T
• NMR system
• Microwaves - 55 GHz - 165 GHz
The Polarized Target Assembly

## Slide 8
Run Dates | Beam Energy | Magnet Orientation | Run Hours/ Proposed PAC hours | Average Beam Polarization
Elastic Kinematics
Used perpendicular Magnetic field
configuration
Beam polarization is ~ 73 %
Average target polarization is ~ 70 %
E Beam GeV | 4.725 | 5.891
P GeV/C | 3.585 | 4.170
Θ (Deg) | 22.30 | 22.00
Q2 (GeV/C)2 | 5.170 | 6.259
# of Total runs | ~44 | ~135
e-p Events | ~153 | ~980
ΘB = 180°
ΘB = 80°
( 80 and 180 deg )

## Slide 9: Extracted the elastic events
Data Analysis
ΘP
Xclust
Yclust
e
e’
P
Definitions :
X/Yclust - Measured X/Y positions on
the BigCal
X = horizontal / in-plane coordinate
Y = vertical / out – of – plane
coordinate
Eclust - Measured electron energy at the
BigCal
By knowing
the energy of the polarized electron beam, EB
and
the scattered proton angle, ΘP
We can predict the
X/Y coordinates - X_HMS, Y_HMS and
( Target Magnetic Field Corrected)
The Energy - E_HMS
of the coincidence electron on the BigCal

## Slide 10: Momentum difference
Momentum Difference , dPel_hms
H
M
S
C
O
IN
HMS – abs(dPel_hms ) < 0.02
abs(hsdelta) < 8
hcer_npe < 0.2
hsshtrk/hse > 0.01
COIN - abs(EHMS-eclust+0.37) <1
abs(XHMS-xclust-0.15) < 5
abs(YHMS-yclust+0.41) < 10
Elliptic cut
yi = variable
ai = offset
σi = cut

## Slide 11: From The Experiment
The calculated asymmetry vs μGE/GM
Am =
N+ - N-
N+ + N-
AP = + Nc
Am
f PBPT
PB,PT = Beam & Target Pol.
f = Dilution Factor
Nc = A Correction Term
N+= Helicity + Counts
N- = Helicity - Counts
PT + = ~71.0% , PT - = ~-65.0%, PB = ~73.0%,
At Q2=6.259 (GeV/C)2
and
≈ 102° and = 0
r = GE /GM
a, b, c = kinematic factors
, = pol. and azi. Angles between q and S
≈ 102° and = 0
From the HMS kinematics, r2 << c
The raw asymmetry,
The elastic asymmetry,
The beam-target asymmetry,
Here,

## Slide 12
Error Propagation From The Experiment…..
Using the experiment data at
Q2=6.259 (GeV/C)2,
∆r = 0.118
μ ∆r = 2.79 x 0.118
μ ∆r = 0.3
Where , μ – Magnetic Moment of the
Proton
The error on the μ ∆r from the experimental data with total ep events ~1000,
μ ∆r = 0.3

## Slide 13: SIMC Simulation
HMS Single Arm Variables
- at the Target -
HMS Coincidence with BigCal Variables
σ = 0.79
σ = 1.69
σ = 2.98
σ = 4.21
σ = 0.0041
σ = 0.0055
SIMC Simulation
Experimental Data
SIMC Counts = 1696
Data = 950
• Target Magnetic Field is corrected
• Normalized to Charge, Tracking Efff. and Comp. L.T.
In plane angle
Out of plane angle
X position
Momentum in Fraction
X position diff.
Y position diff.
Momentum diff in Fraction

## Slide 14
To Do …..
Improve the SIMC simulation
Correct the data with the detector Efficiencies
Extract the Asymmetry and the GE/GM Ratio

## Slide 15
Thank You
SANE Collaborators:
U. Basel, Christopher Newport U., Florida International U., Hampton U., Mississippi State U., Norfolk S. U., North Carolina A&M, IHE-PProtvino, Ohio U., U. of Regina, Rensselaer Polytechnic I., Rutgers U., Seoul National U., Temple U., TJNAF, U. of Virginia, William & Mary, U. of Witwatersrand, Yerevan Physics Inst.
Spokespersons: S. Choi (Seoul), M. Jones (TJNAF), Z-E. Meziani (Temple),
O. A. Rondon (UVA)