## Slide 1
F. Sabatié
Slides from D. Attié, S. Procureur
June 18th, 2014
Forward-Tagger Tracker
– Status & Plan –
Notes: I’m here to present a TPC review

## Slide 2: Status
Scale-one detector prototype have been tested and validated
Resistive strip detector option has been selected for better integration (to be manufacture easily and to optimize the cost):
  Smaller size PCB: 540×500 mm² (detector prototype size: 582x546 mm²)
  24 connectors (1536 strips) instead of 30 (1736 strips) per detector
  Electronics: 6 FEU fully operated
  Pitch of readout strip: 500 µm  560 µm
Total cost : 80 k€ (110 k$)

## Slide 3: Final Detector Concept

## Slide 4: Planning
Mechanical drawings are in progress
PCB layout should be ready after 2014 summer break
Production of the PCBs (2+1 spare) in October 2014
Detector production: double-sided resistive layer+Micromegas bulks by the end of the year
Electronics, mechanics and other components will be manufactured in the meantime
Delivery date: end of February 2015

## Slide 5: Latest results on FT proto
Characterization of proto with final electronics (DREAM) and final cables (Hitachi)
1st time that the 2 sides are tested simultaneously
Side A
Side B
2D efficiency with cosmic bench @ Saclay

## Slide 6: Latest results on FT proto
Checked noise level and efficiency plateau compared to previous tests with AFTER
No interference between the 2 sides
Noise lower and more stable than with AFTER
Full efficiency at lower gain (because of better S/N), but size of effect not completely understood
Side A has larger gain, probably because of smaller gap during double bulk process