## Slide 1: SHMS Kaon Aerogel Cherenkov Detector Update
Nathaniel Hlavin
Catholic University of America
Mentor: Tanja Horn
In collaboration with: CUA, FIU, SCU, MSU, JLab, and Yerevan
Jefferson Lab, Newport News, VA
Jamuary 15, 2011

## Slide 2: Outline
Physics motivation
Detector requirements and project overview
Computer simulation: results and optimization
Design overview and outlook for detector

## Slide 3: SHMS Detector System
SHMS base detector system provides particle identification for e, π, p over the full momentum range
  Noble gas Cherenkov: e/π
  Heavy gas Cherenkov: π/K
  Lead glass: e/π
The lack of p/K+ separation does not allow a strange physics program in Hall C at 11 GeV with only the base equipment
The π+/K+ separation is provided by the heavy gas Cerenkov
Need to build kaon aerogel detector for the strangeness program in Hall C

## Slide 4: SHMS (e,e’K+) Program in Hall C
Range of kaon momenta that needs to be covered largely given by the Kaon factorization experiment
To date four experiments have been approved for Hall C at 11 GeV
Experiment | Physics Motivation | SHMS Momenta (GeV/c) | Worst Fore/Bkd Rate Ratio
Color Transparency (E12-06-107) | vanishing of h-N interaction at high Q. exclusive π, K production from nuclei. | 5.1-9.6 | 1(K):10(p)
SIDIS pT (E12-09-017) | extract mean kT of u,d,s quarks in proton. SIDIS π±, K± production. | 1.5-5.0 | 
SIDIS R (E12-06-104) | Measure the ratio R=σL/σT SIDIS, π±, K± production. | 1.5-5.0 | 
Kaon Factorization (E12-09-011) | study of soft-hard factorization in exclusive K+ production. L/T separations vs. Q2, t. | 2.6-7.1 | 1(K):3(p)
There is a strong kaon program proposed for Hall C. We need a kaon detector!

## Slide 5: SHMS (e,e’K+) Program in Hall C
Range of kaon momenta that needs to be covered largely given by the K factorization experiment
To date four experiments have been approved for Hall C at 11 GeV
Experiment | Physics Motivation | SHMS Momenta (GeV/c) | Worst Fore/Bkd Rate Ratio
Color Transparency (E12-06-107) | vanishing of h-N interaction at high Q. exclusive π, K production from nuclei. | 5.1-9.6 | 1(K):10(p)
SIDIS pT (E12-09-017) | extract mean kT of u,d,s quarks in proton. SIDIS π±, K± production. | 1.5-5.0 | 
SIDIS R (E12-06-104) | Measure the ratio R=σL/σT SIDIS, π±, K± production. | 1.5-5.0 | 
Kaon Factorization (E12-09-011) | study of soft-hard factorization in exclusive K+ production. L/T separations vs. Q2, t. | 2.6-7.1 | 1(K):3(p)
There is a strong kaon program proposed for Hall C. We need a kaon detector!

## Slide 6: Meson Reaction Dynamics
However, before one can learn about form factors and GPDs one has to investigate their prerequisites, e.g., factorization of hard and soft physics
  Kaon factorization
We can learn about meson form factors and nucleon Generalized Parton Distributions (GPDs) from these two diagrams of the meson reaction process
Hard Scattering
Fπ,K
GPD
Depending on Q2, we probe either the meson form factors or the GPDs
Low Q2
High Q2
Notes: Picture behind the mechanism

## Slide 7
Difficult to draw a conclusion from current σL/σT ratios
  Limited W (center of mass energy) and Q2 coverage
  Kaon data in resonance region (W<2 GeV)
  Uncertainties from scaling in x, t
High quality σL and σT data for both kaon and pion would provide important information for understanding the meson reaction mechanism
Q2=1.2-2.0 GeV2
Q2=1.9-3.4 GeV2
W<2GeV
t=0.2 GeV2
xB=0.3
t=0.4 GeV2
xB=0.4
Q2 (GeV2)
Q2 (GeV2)
ep → e‘K+Λ
ep → e‘π+n
Q2=1.4-2.2 GeV2
Q2=2.7-3.9 GeV2
Q2=1.2-2.0 GeV2
Q2=1.9-3.4 GeV2
Q2 (GeV2)
R=σL/σT
R=σL/σT
x=0.3
t=0.2
x=0.5
t=0.4
x=0.3
t=0.2
x=0.4
t=0.4
High Q2: Q-n scaling of σL and σT
A test is the Q2 dependence of the cross section:
  σL ~ Q-6 to leading order
  σT ~Q-8
To access physics contained in GPDs, one is limited to the kinematic regime where hard-soft factorization applies
Q2 (GeV2)

## Slide 8: Problematic Pions
QCD scaling works for previous pion data, but the magnitude compared to the QCD prediction is suspicious.
Further kaon experiments could provide data that matches the QCD prediction.
The 12 GeV upgrade allows for kaon production above a Q2 value of 1, and even higher into the hard QCD range.
T. Horn et al., Phys. Rev. Lett. 97 (2006) 192001.
T. Horn et al., arXiv:0707.1794 (2007).
A.P. Bakulev et al, Phys. Rev. D70 (2004)]

## Slide 9: JLab 12 GeV: L/T separated kaon cross sections
σL
σT
E12-09-011: Precision data for W > 2.5 GeV
Approved experiment E12-09-011 will provide first L/T separated kaon data above the resonance region (W>2.5 GeV)
Understanding of hard exclusive reactions
  QCD model building
  Coupling constants
Onset of factorization
T. Horn et al.

## Slide 10: Kaon Aerogel Project
NSF-MRI Consortium: Development of a Kaon Detection System
PI: The Catholic University of America (Tanja Horn)
co-PI: University of South Carolina (Yordanka Ilieva)
co-PI: Mississippi State University (Dipangkar Dutta)
co-PI: Florida International University (Joerg Reinhold)
Current Status: MRI awarded by NSF October 2010 (NSF-PHY-1039446)
Detector design is well underway
PMTs expected to be procured early in 2011 and tested during summer
co-PI: Catholic University of America (Franz Klein)
Drawings will be modified from HMS drawings and machining will begin at CUA
Aerogel negotiations underway

## Slide 11
PID at higher momenta
Up to about 4 GeV/c, the p/K+ separation can be achieved with a refractive index of n=1.030
Up to about 6 GeV/c, n=1.015 can provide adequate p/K+ separation
Chart: 
Index: 1.03
Kaon
Proton
Np.e.
Momentum (GeV/c)
Chart: 
Index: 1.015
Kaon
Proton
Momentum (GeV/c)
Np.e.
N. Hlavin, S. Rowe
pSHMS | n | Kpe | ppe | Discrimination (5 σ)
3.0 | 1.030 (1.015) | 27 (2) | <0.5 (<0.5) | >1000:1 (lower)
3.5 | 1.030 (1.015) | 34 (9) | <0.5 (<0.5) | >1000:1 (lower)
3.9 | 1.030 (1.015) | 36 (12) | 2 (<0.5) | >1000:1 (lower)
4.5 | 1.030 1.015 | 40 15 | 13 <0.5 | 1000:1 >1000:1
5.2 | (1.030) 1.015 | (42) 18 | (24) <0.5 | (30:1) >1000:1
5.5 | (1.030) 1.015 | (43) 19 | (26) 1 | (20:1) >1000:1
6.1 | (1.030) 1.015 | (44) 20 | (31) 6 | (10:1) 200:1
Contribution of knock-on electrons is 2%
Notes: 11
11

## Slide 12
PID at higher momenta
For higher momenta, p/K+ separation is less of an issue
  Kaon rate becomes larger than the proton rate
  Easier to deal with non-peaked proton background
Prediction coincides with Hall C kaon experiment (E93-108)
Advantage of using n=1.03, 1.015 is that they are the standard indices offered by Panasonic (successor of Matsushita)
  Currently no option to manufacture and export aerogels with indices smaller than n=1.015 in large quantities
Prediction of rates for kaons and protons
For flexibility and to allow for future upgrades, design of detector will support use of aerogel with any index of refraction
Future upgrade option for third index, e.g., n=1.0075 would give p/K+ 1000:1 at p=7.1 GeV/c (available from Novosibirsk)
Notes: 12
12

## Slide 13
Transverse Detector Size
Approved experiments requiring kaon ID use 10 cm long targets and a relatively small fractional momentum region
Transverse aerogel size of 90x60 cm would be sufficient
  Also covers the region of highest intensity for experiments using longer targets
Simulation of event distribution at back of aerogel in SHMS detector stack
40-cm target
SHMS
Aerogel detector location
Required aerogel volume per index (10 cm aerogel thickness) is 60 L
  Quote (12/09) from Panasonic: $150,000 (per index)
  Larger quantities are slightly discounted, e.g., $220k/100L - not much benefit
10-cm target
Notes: 13
13

## Slide 14
With two-sided PMT readout, a summed Npe signal is uniform within 10% of the active area of the detector
H. Mkrtchyan
Design studies: length and width of box
Baseline configuration:
110x100x24.5 cm3 box
90x60 cm2 aerogel active area
Active area of 90x60 cm2 covers the envelope of scattered particles from 10 cm targets
To leave the option to cover the tails from the 40 cm target, detector box will have area 110x100 cm2
Box | PMTs | n | Npe
110x100x30 | 7+7 | 1.015 | 7.60
110x80x30 | 7+7 | 1.015 | 8.14
Box | PMTs | n | Npe
110x100x30 | 7+7 | 1.030 | 14.99
110x80x30 | 7+7 | 1.030 | 16.07
Further reduction of box width by 20% (40%) only improves yield by 7% (15%) making further optimization unnecessary
Simulation* of kaon signal
*D. Higinbotham, NIM A414, 332 (1998)

## Slide 15
In this case a considerable gain in signal was achieved by thicker aerogel values
10 cm seems to by far to be the best choice.
Chart: 
| 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 0 | 4.1862 | 5.6468 | 6.3246 | 6.7754 | 6.9708 | 7.1216
 | 0 | 6.7582 | 9.1343 | 10.1935 | 10.7877 | 11.1429 | 11.3573
 | 0 | 8.4445 | 11.3675 | 12.7913 | 13.5474 | 13.936 | 14.2232
10 cm thick
8 cm thick
5 cm thick
Photoelectrons
Momentum (GeV)
n = 1.03
N. Hlavin
Monte Carlo Simulations of Kaon Signal
Design studies: aerogel thickness
Baseline configuration:
90x60x10 cm3 aerogel active volume

## Slide 16
Design studies: PMT selection
Box | PMTs | n | Npe
110x100x30 | 7+7 | 1.015 | 7.60
110x100x30 | 7+7 | 1.030 | 14.99
Box | PMTs | n | Npe
120x100x30 | 8+8 | 1.015 | 7.86
120x100x30 | 8+8 | 1.030 | 15.44
H. Mkrtchyan
Minimum distance between 5” PMTs centers must be 5.875” (14.92 cm)
For 110 cm detector height can fit seven 5” PMTs from each side
Gain for increasing height to fit eight 5” PMTs from each side is negligible
Effective coverage for 7 5” PMTs is 5.1%
  With nine 4” PMTs this would be reduced to 4.2%

## Slide 17
Chart: 
| 2 | 4 | 6 | 8
 | 0 | 3.6211 | 5.6351 | 6.3802
 | 0 | 2.4876 | 3.895 | 4.3911
 | 0 | 3.6168 | 5.6572 | 6.3728
 | 0 | 4.637 | 7.2629 | 8.195
 | 0 | 4.8806 | 7.6653 | 8.6484
 | 0 | 4.5967 | 7.1863 | 8.098
 | 0 | 4.5386 | 7.1322 | 8.0506
Momentum (GeV)
Photoelectrons
90x90 ; 110x100
90x60 (6x6x4)
110x100
110x100
n = 1.015
N
E
W
Bottom
Top
S
N. Hlavin
Monte Carlo Simulations of Kaon Signal
Top and bottom? Left and right?
How many PMTs?
PMTs on one wall
PMTs on two walls
PMTs on three walls
Design Studies: PMT placement
To optimize performance and facilitate access the PMTs will be mounted on the vertical sides of the box

## Slide 18
SHMS Aerogel Design Overview
PMTs
Aerogel Panels
Front View
Side View
Diffusion box will be built as single unit with fourteen 5” PMTs, 7 on each long side of the detector
  Vendor: Hamamatsu, model R1250 (full assembly H6527)
Aerogel tray and diffusion lightbox with PMTs based on proven technology
  Allows for simple detector assembly and easy replacement of the aerogel stack
To cover momenta up to ~6 GeV/c aerogels with refractive indices, n=1.030 and n=1.015 will be purchased
  Vendor: Panasonic*
Active area will be 90x60cm2 with box size 110x100cm2 for future upgrades
  Vendor: Hamamatsu, model R1250 (full assembly H6527)
Total depth ~ 30cm along the optical axis of the SHMS

## Slide 19
PMT Procurement
Negotiations with MIT/Bates about PMTs from ASU detectors from BLAST experiment
  Together with Yerevan group we will evaluate the PMTs this spring
Procurement of PMTs will be completed this spring and extensive testing during the summer at JLab and CUA
  Hamamatsu model R1250
  Photonis XP4500B
Currently developing testing procedures using PMTs from HKS experiment *
*Thanks to Liguang Tang (HU), Joerg Reinhold (FIU), Tohuku University
Constructed test setup and checked with cosmic rate

## Slide 20
NP and Material Science Collaboration
Machining in-house with help from Vitreous State Laboratory
  Machining of detector components can begin once the technical drawings are available
Broad involvement and support for our project in department

## Slide 21
Collaboration with ASU
Panasonic is currently the only large scale aerogel supplier
  Determines aerogel pricing
Studies at Arizona State University to check other vendors* for:
  Quality of aerogel compared to Panasonic
  Capabilities for large scale production (>10L)
*Aspen Aerogel, Boston
Collaboration with Ricardo Alarcon from Arizona State University to search for alternatives

## Slide 22: Outlook
Technical drawings and machining of components starting in next few months
PMT procurement complete this spring
PMT testing and prototype this summer together with students from Catholic University of America, University of South Carolina, Florida International University, and Mississippi State University