## Slide 1: Qweak Instrumentation
Greg Smith
(for the Qweak Collaboration)
Hall C Users Meeting
January 16, 2015

## Slide 2: Qweak Instrumentation Paper
Just accepted in NIM A
arXiv server:
  http://arxiv.org/abs/1409.7100
Jlab pubs JLAB-PHY-14-1959:
  https://misportal.jlab.org/ul/publications/downloadFile.cfm?pub_id=13340
Other instrumentation papers planned:
  LH2 target
  Main quartz detectors
  Compton polarimeter

## Slide 3
  Parameters:
  Ebeam= 1.165 GeV
  <Q2> = 0.025 GeV2
  <θ> = 7.9° ± 3°
  φ coverage = 50% of 2π
  Ibeam = 180 μA
  Integrated rate = 6.9 GHz
  Beam Polarization = 88%
  Target = 35 cm LH2
  Cryopower = 3 kW
Experimental Apparatus
LH2 target
Beam
Collimators
Qweak Toroidal Magnetic Spectrometer (QTor)
Horizontal Drift Chambers
Quartz Cherenkov bars
Downstream Luminosity Monitors
Shield Hut
Used only during low current tracking mode operation
Vertical Drift Chambers
Trigger Scintillators
Luminosity Monitors

## Slide 4: Helicity Timing & Fast Reversal
960 Hz
Old
500 μs
Switching
@ 30 Hz
New
60 μs
Switching
@ 960 Hz
18-bit ADCs sampled at 500 kHz 
464 samples/(Helicity Gate),
started TADC Delay= 42.5 μs (4.1% DT)
after start of TStable
960 Hz helicity reversal
Tsettle= 70 μs (6.7% DT)
Tstable= 971.65 μs
Opto-coupler
mounted directly to Pockels Cell
“Fast” HV transistor switches
Integration
windows

## Slide 5: Photocathode Quantum Efficiency
1/e charge lifetimes with lens of 1.5 m focal length (0.55 mm spot)
and 2.0 m (1.0 mm spot)
QE Profiles before (left) & after (right) 4 weeks @ 180 μA.
1 mm φ laser spot indicated by X
Other improvements:
  New inverted e gun @ 130 kV
    Reduced loss on inj. apertures
100 kV
130 kV
Notes: Laser spot was 1 mm diam., active area ~ 5 mm diameter.

## Slide 6: Polarized Source
8 hour
reversal
960 Hz
reversal
monthly
reversal
± 2.5 kV

## Slide 7: Parameters
Gaussian Fit
(σA = 230 ppm)
Data
ΔA ~ 1 ppm/d
Msr P, Q2, IB, & Yield very well
960 Hz helicity flip (fast!)
MD PMT anode current integrated for each helicity state
  normalized to beam charge
Quartet asymmetries calculated
every 4 ms (cancels linear drifts)
Asymmetry width σA ~ 230 ppm at 180 μA is dominated by counting statistics;
  target noise ~ 50 ppm
  beam charge msrmnt ~ 50 ppm
Also: collimation, shielding, control & msr bkgs & HCBAs, hi luminosity..
σA

## Slide 8: Beam Current Instrumentation
Six temp. stabilized, RF cavity BCMs:
  @1497 MHz, 100 kHz bandwidth
  Two with old analog receivers (1&2)
    Downconverted to 1 MHz
    Demodulated with RMS to DC converters
    DD resolution 100-140 ppm
  Four with new digital receivers (5-8)
    Downconverted to 45 MHz
    Digitally sampled & processed signals
    Rad damage  moved receivers to CR
    18 bit, 1 MHz DACs
    Air-core coax cables  Heliax
    DD resolution ~ 60 ppm
σRMS=115 ppm
σRMS=57 ppm
BCM linearity ~0.5% from 20-180 μA.
Below 1 μA used injector Faraday cup & DS lumis.
Kept IA < 100 ppb with active feedback, adjusting PITA offsets to Pockels Cell.
  Typical msrd IA only 40 ppb/month!

## Slide 9: Precision Polarimetry
Qweak requires ΔP/P ≤ 1%
Strategy: use 2 independent polarimeters
Use new Compton polarimeter (1%/h)
  High Ibeam, non-invasive
  Known analyzing power provided by circularly-polarized laser
Use existing <1% Hall C Møller polarimeter:
  Low beam currents, invasive
  Known analyzing power provided by polarized Fe foil in a 3.5 T field.
Møller Polarimeter
Compton Polarimeter
57 cm

## Slide 10: Compton Electron Detector
Compton edge
Strip 1 closest (7 mm) to beam
Missing strips (2, 6, & 20) have negligible impact on fit

## Slide 11: Compton Systematic Uncertainties
0.3
0.56
0.3
Final
Note: Statistical uncertainties ~ 1%/hour @ 180 μA
Note: DAQ errors could be made smaller still in a new implementation.
Note: No guarantee this can be reproduced in Hall A (different kinematics, detector, bkgs…)

## Slide 12: Neutral line-of-sight Collimation

## Slide 13: Beam Collimator
Target SC
16” GV
SC Window
Beam Collimator
(inside 1st collimator)
Water cooled W-Cu beam collimator
Beam Collimator
14.9 mm φ
47 cm ds of tgt
1.6 kW beam power

## Slide 14: Beam Collimator
Target SC
16” GV
SC Window
Beam Collimator
(inside 1st collimator)
Water cooled W-Cu beam collimator
Beam Collimator
14.9 mm φ
47 cm ds of tgt
1.6 kW beam power

## Slide 15: Maximum angle accepted by triple collimator system

## Slide 16: 1st hot spot, shielded by lintels

## Slide 17
2nd hot spot, shielded by lintels
2nd collimator
Inner edge
hot spot
(looking upstream)

## Slide 18: 3rd hot spot, shielded by beamline Pb

## Slide 19: 4th hot spot, shielded by hi density concrete

## Slide 20: Target Design
World’s highest power and lowest noise cryogenic target ~3 kW
Centrifugal pump
(17 l/s, 7.6 kPa)
3 kW Heater
3 kW HX utilizing
4K & 14K He coolant
35 cm cell (beam interaction volume)
Solid Tgts
Fluid
velocity
beam
beam
(m/s)
IBeam = 180 uA
L = 35 cm (4% X0)
Pbeam = 2.2 kW
Aspot = 4x4 mm2
V = 57 liters
T = 20.00 K
P ~ 220 kPa

## Slide 21: Cell
LH2 Transverse Flow:
1.1 kg/s
15 L/s
3-7 m/s
Electron Beam
180 μA, 4x4 mm2
LH2 length: 35 cm
Al entrance window ~0.1 mm thick, 22.2 mm Φ
Al exit window ~0.125 mm thick over 15 mm Φ,
0.635 mm thick over 173.5 mm
Scattered electron acceptance ±13.9°
13.9°
13.9°
Designed using Computational Fluid Dynamics

## Slide 22: Centering on extended tgt worked well
LH2 Exit window with thin central nipple (125 μm)
Aluminum background targets
2 mm
Dynamic 2 axis motion system (x,y).
Manual cell adjustment mechanism (pre-cooldown) allowed adjustment of z, roll, pitch & yaw.
15 mm

## Slide 23: Target Performance
180 μA
4 x 4 mm2
Tboil=23.2 K
Where ΔAqrt is msrd main detector asymmetry width
(over each helicity quartet)
σtgt (ppm)
ΔAqrt (ppm)
Target Pump Speed (Hz)
22 K
21 K
20 K
19 K
Time (sec)
Time (sec)
Pump speed = 28.5 Hz
Pump speed = 12 Hz
Main Detector Yield (V/μA)
(20 K)
(20 K)
Measured helicity correlated target noise:
At 960 Hz reversal rate, the target noise (~50 ppm) is small compared to our measured helicity
quartet ( ) asymmetry width qrt (~230 ppm).
(statistical power ~ ).
±
±
±
±
22 K
21 K
20 K
19 K

## Slide 24: QTOR Magnet
Manitoba / TRIUMF / MIT-Bates / JLab
Open geometry resistive toroid, for maximum solid angle acceptance
Eight water cooled, dble pancake coils
Separates elastics from inelastics at focus
3-axis Mapper
Power Supply:
150 V, 9100 A
Double pancake coil

## Slide 25: Spectrometer Performance
Radial field distribution at magnet center along beamline, and 1/2-way between 2 coils azimuthally.
θ=
spec
∫Bdl is calculated based on the actual coil positions determined from zero-crossing field mapping msrmnts.
<∫Bdl> is the 8-octant average.
θ is the polar angle, φ the azimuthal angle.
Bφ(r)
3 axis mapper
Octant to octant field uniformity

## Slide 26: Quartz Cerenkov Detectors
Yield 100 pe’s/track with 2cm Pb pre-radiators
Resolution limited by shower fluctuations.
  Simulation of MD face:
  Measured
  Azimuthal direction
Azimuthal symmetry maximizes rate and decreases sensitivity to HC beam motion, transverse asymmetry.
Spectrosil 2000: Eight bars, each 2 m long, 1.25 cm thick
  Rad-hard
  Non-scintillating, low-luminescence
Quartz
Bars
  Azimuthal direction
Charge-normalized Yield
Quartet Asymmetry width
f(tgt, BCMs, HCBA, stats, det. res.)
Results over entire expt
Scaled by sqrt(IB/180)

## Slide 27: More Quartz Detector Results
measured
GEANT4
Main quartz detector pulse height spectrum.
50 pA, LH2, sum from both ends.
Raw Yield
σ = 50 mV
Charge-normalized Yield
σ = 13 mV
Shot
(stat. noise)
~6 min. main quartz detector yield
(mean subtracted)

## Slide 28: Determining the Kinematics
Required uncertainty on Q2 is 0.5%
Combination of tracking and simulation
HDCs before magnet to msr θ
  Q2 = 2E2 (1-cosθ) / [1 + E/M(1-cosθ)]
VDCs & trigger scintillators after magnet to msr light weighted Q2 across quartz bars
radial
azimuthal

## Slide 29: Tracking System
VDC
VDCs
VDC
rotator
HDC
rotator
HDCs

## Slide 30: Tracking Chambers
2 chmbrs/octant in 2 octants.
Rotation systems to access the other octants. Overlap in 1 octant.
Separate electronics, MD bases & DAQ.
Chambers retracted out of acceptance for main (180 μA) measurement.
HDC residual
1 of 12 planes (2 chmbrs)
σfit=178 μm
50 pA
LH2
~ 100 kHz
50 pA
LH2
~ 300 Hz
VDC residual
1 of ~24 wires
(2 chmbrs)
σfit=264 μm
1 cm3 quartz profile scanner
VDC projection
HDC: e’s drift || to plane.
6 planes/chmbr (xuvxʹuʹvʹ) of 32 wires.
5.85 mm pitch. 28x38 cm.
VDC: e’s drift ┴ to plane.
2 planes/chmbr (uv) of 279 wires.
4.97 mm pitch. 205x53 cm.

## Slide 31: The Qweak Collaboration
D.S. Armstrong, A. Asaturyan, T. Averett, J. Balewski, J. Beaufait, R.S. Beminiwattha, J. Benesch,
F. Benmokhtar, J. Birchall, R.D. Carlini1, J.C. Cornejo, S. Covrig, M.M. Dalton, C.A. Davis,
W. Deconinck, J. Diefenbach, K. Dow, J.F. Dowd, J.A. Dunne, D. Dutta, W.S. Duvall, M. Elaasar,
W.R. Falk, J.M. Finn1, T. Forest, D. Gaskell, M.T.W. Gericke, J. Grames, V.M. Gray, K. Grimm, F. Guo, J.R. Hoskins, K. Johnston, D. Jones, M. Jones, R. Jones, M. Kargiantoulakis, P.M. King, E. Korkmaz,
S. Kowalski1, J. Leacock, J. Leckey, A.R. Lee, J.H. Lee, L. Lee, S. MacEwan, D. Mack, J.A. Magee,
R. Mahurin, J. Mammei, J. Martin, M.J. McHugh, J. Mei, R. Michaels, A. Micherdzinska, K.E. Myers,
A. Mkrtchyan, H. Mkrtchyan, A. Narayan, L.Z. Ndukum, V. Nelyubin, Nuruzzaman, W.T.H van Oers,
A.K. Opper, S.A. Page1, J. Pan, K. Paschke, S.K. Phillips, M.L. Pitt, M. Poelker, J.F. Rajotte,
W.D. Ramsay, J. Roche, B. Sawatzky,T. Seva, M.H. Shabestari, R. Silwal, N. Simicevic, G.R. Smith2,
P. Solvignon, D.T. Spayde, A. Subedi, R. Subedi, R. Suleiman, V. Tadevosyan, W.A. Tobias, V. Tvaskis, B. Waidyawansa, P. Wang, S.P. Wells, S.A. Wood, S. Yang, R.D. Young, S. Zhamkochyan
1Spokespersons 2Project Manager Grad Students
95 collaborators
23 grad students
10 post docs
23 institutions:
  JLab, W&M, UConn, TRIUMF, MIT, UMan., Winnipeg, VPI, LaTech, Yerevan, MSU, OU, UVa, GWU, Zagreb, CNU, HU, UNBC, Hendrix, SUNO, ISU, UNH, Adelaide
Notes: Only using lh2 statistics
Black line – day 27 cut-off
Note: our 2.1% goal isn’t here

## Slide 32: Beam Position Instrumentation
Stripline monitors: 2 +/− pairs of antennas
  Readout multiplexed (SEE) every 4.2 μs to eliminate gain drifts in electronics
  Readout every helicity state (960 Hz) into custom-built 18-bit ADCs (TRIUMF)
  24 BPMs in injector beamline
  23 BPMs in Hall C beamline
    5 used for position & angle at LH2 tgt
    Offsets stable to 25 μm
    Position resolution at tgt 1 μm with 5 tgt BPMs
    Angle resolution at tgt 150 nrad
  Slow (1 s) position lock on tgt employed
Notes: SEE = switched electrode electronics