## Slide 1
Precision measurements of the F2 structure function at large x in the resonance region and beyond
S. Malace, PAC35 January 2010, Jefferson Lab
Outline
Motivation
Experimental details
Summary
S.P. Malace*, M. Paolone, S. Strauch, I. Niculescu, G. Niculescu, A. Accardi, A. Albayrak,
O. Ates, M.E. Christy, C. Jackson, C.E. Keppel, M. Kohl, Y. Li, P. Monaghan, A. Pushkapumari,
J. Taylor, T. Walton, L. Zhu, R. Ent, H. Fenker, D. Gaskell, M.K. Jones, D. Meekins,
P. Solvignon, G. Smith, L. Tang, A. Asaturyan, A. Mkrtchyan, H. Mkrtchyan, V. Tadevosyan,
S. Zhamkochyan, G. Huber, S. Danagoulian, P. Markowitz, A. Daniel, T. Horn
University of South Carolina , James Madison University, Hampton University, Jlab,
Yerevan Physics Institute, University of Regina, North Carolina A&T State University,
Florida International University, Ohio University, Catholic University of America
Spokespersons
*Contact Person

## Slide 2
The structure of the Nucleon in QCD
Distribution of quarks and gluons (PDFs) inside the nucleon: fundamental characterization of its structure in QCD
PDFs
connect hadron processes with parton subprocesses
universal: many processes can be calculated with same set of PDFs
important information as to the underlying structure of hadrons
Motivation
Decades of accumulated data + sophisticated QCD analyses => mapping of PDFs over a large kinematic range
PDF
S. Malace, PAC35 January 2010, Jefferson Lab

## Slide 3
S. Malace, PAC35 January 2010, Jefferson Lab
Standard Extraction of PDFs in QCD
Two ideas of QCD + data:
perturbative
Evolution:
LO
NLO
+
+
x dependence obtained from fits to data
Data: DIS ( ), neutrino DIS dimuon production, vector boson production, hadronic jet production,…
Motivation
Knowledge of the x-dependence of PDFs depends on data coverage across x
input (PDF)
perturbative
Factorization:

## Slide 4
S. Malace, PAC35 January 2010, Jefferson Lab
Motivation
Standard Extraction of PDFs in QCD: Uncertainties
pQCD => leading-twist calculation, applicable where nonperturbative corrections negligible
Kinematic cuts reject data from regions where nonperturbative corrections not negligible (large x, low Q2): CTEQ
PDFs: large errors at large x
W2 > 12.25
Q2 > 4
example 1: CTEQ6
data not used

## Slide 5
Motivation
S. Malace, PAC35 January 2010, Jefferson Lab
Standard Extraction of PDFs in QCD: Uncertainties
pQCD => leading-twist calculation, applicable where nonperturbative corrections negligible
Kinematic cuts reject data from regions where nonperturbative corrections not negligible (large x, low Q2): MSTW
W2 > 15
example 2: MSTW
Q2 > 2
data not used
PDFs: large errors at large x

## Slide 6
Motivation
Pushing QCD applicability to large x and low Q2
S. Malace, PAC35 January 2010, Jefferson Lab
CTEQx: A. Accardi et al., arXiv:0911.2254 [hep-ph], accepted to PRD
Relax kinematic cuts to include large x, low Q2 data in PDF fits => include nonperturbative effects in the QCD calculation
leading twist (pQCD) + kinematical higher twist
(target mass corrections)
residual power corrections
NLO global PDF fit to proton and deuteron data with Q2 > 1.69 GeV2 and W2 > 3 GeV2 including now: DIS from SLAC, JLab, FNAL Drell-Yan, W asymmetry data at higher x
cut 0: Q2 > 4 GeV2, W2 > 12.25 GeV2 (standard)
cut 1: Q2 > 3 GeV2, W2 > 8 GeV2
cut 2: Q2 > 2 GeV2, W2 > 4 GeV2
cut 3: Q2 > 1.69 GeV2, W2 > 3 GeV2
(Hall C E00-116)
S. Alekhin, JETP Lett. 82, 628 (2005); S. Alekhin et al., arXiv:0908.2766 [hep-ph]

## Slide 7
Motivation
S. Malace, PAC35 January 2010, Jefferson Lab
Results from CTEQx Fit
no direct constraints from data
Compared to previous analyses:
stronger suppression of d-quark PDF at large x (sensitive to the treatment of nuclear corrections)
greatly reduced experimental errors: 10-20% for x < 0.6 and up to 40-60% at larger x
u and d PDFs stable with respect to choice of target mass correction if flexible enough parametrization of higher twist is used

## Slide 8
Motivation
Quark-Hadron Duality: Extension of PDFs to Larger x
Extending to larger x at finite Q2 => encounter the resonance region
can be treated using the concept of Quark-Hadron Duality
established in F2p from Q2 ~ 1 to Q2 ~ 7 GeV2
Confirmation of duality in both proton and neutron => phenomenon not accidental but a general property of nucleon structure functions
S. Malace, PAC35 January 2010, Jefferson Lab
S.P. Malace et al., Phys. Rev. C 80 035207 (2009)
proton
neutron
S.P. Malace et al., arXiv:0910.4920 [hep-ph]
recently acknowledged in F2n extracted from proton and deuteron data

## Slide 9
Motivation
Data at Large x: Current Status
S. Malace, PAC35 January 2010, Jefferson Lab
W2 < 3 GeV2
data scarce for x > 0.8
very limited Q2 coverage between 10 and 20 GeV2
W2 > 3 GeV2
proton
deuteron

## Slide 10
S. Malace, PAC35 January 2010, Jefferson Lab
Motivation
Motivation: Summary
behavior of PDFs with x of interest e.g. to verify the Drell-Yan-West relation postulate
relates the large x-behavior of F2 with the Q2 behavior of form factors …
Need precision data on proton and deuteron F2 at large x to:
constrain PDFs at large x
and extend studies of local quark-hadron duality in proton and neutron F2
JLab New Milestone HP13 by 2018
“Extract accurate information on spin-dependent and spin-averaged valence quark distributions to momentum fractions x above 60% of the full nucleon momentum”
can use global quark-hadron duality to push to x > 0.8
distinguish different mechanisms of spin-flavor symmetry breaking (d/u at large x)
BONUS/Hall B (E12-06-113)  F2n/F2d
Hall C PR-10-002  precision F2p/F2d in same kinematic region
essential for determining high-energy cross sections at collider energies in search for physics beyond Standard Model etc.

## Slide 11
PR-10-002 @ 11 GeV in Hall C
Experimental details
Extend proton and deuteron F2 structure function precision measurements to larger x and Q2 by measuring H(e,e’) and D(e,e’) cross sections in the resonance region and beyond up to Q2 ~ 17 GeV2 and x~0.99
HMS
SHMS
HMS
+
SHMS
Straightforward extension of E00-116:
For PR-10-002 we need:
11 GeV beam (+ 6.6 GeV for systematic measurements)
10 cm Hydrogen and Deuterium cryogenic targets (+ Al for background measurements)
SHMS and HMS in Hall C
S. Malace, PAC35 January 2010, Jefferson Lab
S.P. Malace et al., Phys. Rev. C 80 035207 (2009)
S.P. Malace et al., arXiv:0910.4920 [hep-ph]

## Slide 12
SHMS:
Kinematics of PR-10-002
HMS
SHMS
HMS
+
SHMS
Experimental details
S. Malace, PAC35 January 2010, Jefferson Lab
intermediate angle measurements: 17 - 35 deg
central momentum range: 2.3 - 6 GeV (spectrometer low limit 2 GeV)
large angle measurements: 42 & 55 deg
central momentum range: 1.2 – 6.7 GeV (spectrometer high limit 7.3 GeV)
17 deg scan: taken with both HMS and SHMS for crosschecks; hydrogen elastic data
HMS:

## Slide 13
Experimental details
Expected Backgrounds
S. Malace, PAC35 January 2010, Jefferson Lab
Electrons scattered on the Al walls of cryogenic target cell => take data for each setting on empty Al (dummy) target
Pion contamination of the electron distribution
E00-116: < 1.8% at E’ ~ 0.8 GeV
deuterium
E00-116: < 0.5% at E’ ~ 0.8 GeV
hydrogen
E00-116: main limitation was the pion rejection in the calorimeter at low momentum
PR-10-002: lowest momentum 1.2 GeV in HMS and 2.3 GeV in SHMS => pion rejection should be sufficient for the proposed kinematics

## Slide 14
Experimental details
Expected Backgrounds
S. Malace, PAC35 January 2010, Jefferson Lab
hydrogen
E00-116: positron cross section
PR-10-002
E00-116: measured and extensively studied
Charge-symmetric background: secondary electrons from neutral pion production in the target and its subsequent decays
PR-19-002: expected to be at most 11% for H and 15% for D at 55 deg, lowest momentum => measure background at 55, 42, 35, 30 deg

## Slide 15
Experimental details
Uncertainties
S. Malace, PAC35 January 2010, Jefferson Lab
Statistical
PR-10-002: shoot for 2% in a W2 bin of 0.1 GeV2, with a 10 cm target and a 40 mA and 11 GeV beam
significant improvement over scarce existing measurements from SLAC
Systematic uncertainties from E00-116 exceeding 1%
Systematic
Quantity Uncertainty ds(%)
Charge-symmetric background 6% - 20% < 2%
Model dependence 0.2% - 5% 0.2% - 5%
Radiative corrections 0.5% - 3.6% 0.5% - 3.6%
PR-10-002: expect reduction, e+ and e- measured at same kinematics with same spectrometer
PR-10-002: expect reduction, for our kinematics elastic/quasielastic contribution small to negligible
E00-116: for W2 > 2 GeV2 within 1%

## Slide 16
Uncertainties
Systematic: need R to construct F2
Experimental details
S. Malace, PAC35 January 2010, Jefferson Lab
E00-116: 2% uncertainty on F2 from R
PR-10-002: R expected to be < 0.15
R-related fractional uncertainty on F2:
Assuming 100% uncertainty on R =>
can be cut in half by a modest 50% determination of R with a lower beam energy (6.6 GeV)

## Slide 17
Experimental details
PR-10-002: Request to Laboratory
S. Malace, PAC35 January 2010, Jefferson Lab
Beam time accounting
SHMS
HMS
PR-10-002 beam time is driven by the large angle measurements: 42 & 55 deg
some overlap in kinematics with PR-10-008 (20 – 35 deg) but small overlap in beam time: < 1 day
PR-10-002: we need 13 days to complete the proposed experiment
PR-10-002: excellent candidate as a commissioning experiment

## Slide 18
Summary
S. Malace, PAC35 January 2010, Jefferson Lab
PR-10-002: extend proton and deuteron F2 structure function precision measurements to larger x and Q2 by measuring H(e,e’) and D(e,e’) cross sections in the resonance region and beyond up to Q2 ~ 17 GeV2 and x ~ 0.99
constrain PDFs at large x
Data would be used to:
We need:
11 GeV beam (+ 6.6 GeV for systematic measurements)
Hydrogen and Deuterium cryogenic targets (+ Al for background measurements)
SHMS and HMS in Hall C
13 days of beam time
use global quark-hadron duality to push to largest x (x > 0.8)
and extend studies of local quark-hadron duality in proton and neutron F2

## Slide 19
Backup Slides