Hall D FDC Clean Room Procedures

Clean room rules;

►No wood or cardboard inside the clean tent.

►Keep paper inside the tent to an absolute minimum.  Do not tear paper inside the tent.

►Clean all parts and material before entry.

►Roll the floor with the sticky roller before beginning work at least once per day.

►If your lab coat, shoe or hair covers become frayed or dirty, replace them.

►While using the clean room, use skin moisturizer on hands and forearms to the elbow daily.

For entry into the clean tent;

●Clean shoes with shoe cleaner.

●Put on hair net and lab coat.

●Sitting on the bench, with your shoes off the sticky mat, put on one shoe cover.  Without touching your covered shoe to the floor, put the covered shoe on the sticky mat.  Put the second shoe cover on and put that covered shoe on the sticky mat.  Do not step off the sticky mat.  Put on gloves, walking on the sticky mat enter through the curtain.

Exiting the clean tent;

●Avoid stepping on the sticky mat on the way out.

●Sitting on the bench, remove and dispose of your hair and shoe covers, hang up your lab coat for reuse.