IKO International, Inc., 91 Walsh Drive, Parsippany, NJ 07054

Mr. Ravi Kiran Anumagalla                                   May 25, 2004

Jefferson Lab

Dear Ravi,

Although I believe that you have understood our suggestion for the rail length, I would like to make sure what I meant by the following sketches.

Since we supply to you one 2-meter rail and 2, 3 or 4 slide units as a set, we will not guarantee the accuracy when TWO sets are butted and slide units travel onto one set to another.

Please understand that we do not have above headache for the standard product lines.  This non-magnetic product carries the ceramics balls so that special care must be taken to obtain the accuracy.

If you have any questions or comments, please feel free to contact us.

Mike Tsuboi

Engineering Manager

# Text boxes

2-meter rail consists of three short sections, such as 800 + 800 + 400.

The configuration will be informed when we make a quote for you.

We guarantee the accuracy of the complete set (rail + slide units) in every length of 2 meters.

The accuracy covers dimensional tolerances (H & N) and their deviation.