Electrical Engineering Concerns, Ron Lauze

- We may see 60Hz beam motion, not seen at higher energy, but visible at low energy. There are a number of potential sources of this noise but recently we have suspected the magnets. Isolating this can and has been very difficult. There is an effort afoot to develop new tools.

- There may be an issue regarding cable lengths for the repositioned diagnostics girder. The fact that the girder moved is not the problem. The cable tray was removed and relocated (I think) and now the run is much longer. Gonzales will be working with Hall C and MECAD to rectify this.

- Who owns (System Owner) the Ion Chambers has been an issue in the not to distant past. Due to their importance, it would be wise to get a handle on that soon. You (we) can talk to Andrew, he was trying to get Abkemeier to own it.

- Last minute changes. These always occur and engineering is typically very accommodating. However, due to time restraints we are often forced to install something that is less than ideal (poorly documented, lack of remote control, sharing controls or readbacks with other devices, etc.). So, please inform engineering of potential changes as soon as they become known.