## Slide 1
Jefferson Lab –
An Introduction
Hugh Montgomery; March 5, 2012

## Slide 2: JEFFERSON LAB
A
C
B
CEBAF’s delivery of beam with unique properties to
three experimental halls simultaneously. Each hall offers different capabilities.
Superconducting electron accelerator provides 100% duty factor beams of unprecedented quality, with high polarization at energies up to 6 GeV.
>1200 active member international user community engaged in exploring quark-gluon structure of matter.
Newport News, VA

## Slide 3: Spin, Current, and Beam Delivery @CEBAF
Under development
<0.5% Atomic Beam Polarimeter (Hall A)
<1% Compton Polarimeter (Hall C)
Notes: In more detail
Three interleaved beams, each 499 MHz
From 180 mA in Hall C/Hall A, to a few nanoamps in Hall B.
Wien Filter: If E/B= bc the no deflection but spin precesses in plane of the electric field.
Note multiple energies in the same RF bunch in the linacs, separated in the bends.

## Slide 4: Electron Scattering: A picture
Friedman, Kendal, Taylor, Nobel Prize 1990
Gross, Politzer, Wilczek, Nobel Prize 2004
Notes: Now more the deep inelastic view, the mess inside the nucleon, note the Z exchange.
Note the Nobel Prizes pretty much attributable to this picture.

## Slide 5: QWeak Experiment
500 MHz Continuous Wave, 180 mA ( 18.9 C one day)
35 cm Hydrogen target ( 2.5 kW )
Quartz Bar detectors, measure the current (not count)
Low current tracking measurements check kinematics
Qw=(1 – 4 sin2 qW)

## Slide 6: World-record Q0 at 2 K and 90 mT
Record obtained on a 1475 MHz single cell cavity
  Made of ingot Niobium
    Usually fine grain Niobium
  Medium purity RRR = 200
    Usual spec RRR > 330
  High Tantalum ~1375 ppm
    Usual spec >600 ppm)
  Heat treated in DOE-NP ARRA-funded UHV furnace at 1400˚C
Reached Q0-value of 4.631010 at 2.0 K and peak surface magnetic field (Bp) of ~90 mT, equivalent accelerating gradient of ~20 MV/m

## Slide 7
E = 120 MeV emittance 5 microns
135 pC pulses @ 75 MHz 150 fs
IR (1-10 microns), 14 kW
UV (down to 300nm)
4 eV in fund. 12eV in
3rd harmonic
2 FELs
Jefferson Lab Light Source
A VUV/IR/THz 4th Generation Light Source
Accelerator R&D and devel.
funded by Navy (ONR) and Air Force
ERL

## Slide 8: 12 GeV Upgrade
Enhanced capabilities in existing Halls
New Hall
CHL-2
Maintain capability to deliver
lower pass beam energies

## Slide 10
Jefferson Lab EIC Site Plan
Also a Brookhaven version: EIC Advisory Committee reports to Aronson and Montgomery

## Slide 11: Jefferson Lab
An exciting laboratory
  Improving infrastructure
Lots of interesting accelerator work
  SRF
  Cryogenics
  FEL/ERL development
Lots of exciting physics
  Understanding the Structure of the nucleu and nucleon, the strong interaction more broadly
  Measuring the weak interaction
  Exploring fundamental symmetries
  WELCOME