## Slide 1: The impact of undulators in an ERL
Jim Clarke
ASTeC, STFC Daresbury Laboratory
FLS 2012, March 2012

## Slide 2: Introduction
The impact of synchrotron radiation emission in an ERL is different to that of a storage ring
An electron that loses energy will not have this energy replaced
There is the danger that upstream undulators will affect the performance of downstream ones
The work presented was generated as part of the 4GLS design study, more details are available in the CDR (http://www.4gls.ac.uk/)
The results should be generally applicable to ERLs but the numerical examples relate to 4GLS of course

## Slide 3: 4GLS Reminder
600 MeV

## Slide 4: Energy Loss
An electron emitting synchrotron radiation in an undulator will lose energy, DE (in eV):
The largest energy loss is for a helical undulator since B(s) is effectively constant along its length
A 10 m long helical undulator with a 1 T transverse field will cause each electron to radiate ~ 4.6 keV on average, which is less than one part in 105 of the electron's energy
For an electron passing through a system of five undulators the total loss by the electron is ~ 23 keV, which is still less than 0.004 % of the electron's energy

## Slide 5: Energy Loss
The electron will also radiate energy as it passes through the arc dipoles.
Incoherent SR for an electron passing through a system of 1 T dipoles making up a 360 path will radiate ~ 5.7 keV on average
But, Coherent SR can be significant if electron bunch is short
CSR loss in 4GLS ~1MeV (~0.16 %). This is ok if loss does not vary with time – need to be confident of this
If assume an electron energy change of 0.005 %, due to a number of undulators being varied, then the change in undulator harmonic wavelength for a later device would be ~0.01 %. Typical harmonic bandwidth ~ 1 %.
This effect more important at higher harmonics which have narrower bandwidths.

## Slide 6: Path Length
Undulators alter the trajectory of the electron beam
  Hence the path length
  The adjustment of an undulator in one straight will affect the electron bunch arrival time at subsequent undulators
  Will affect the synchronisation with an external source but if use electron beam as trigger then should be ok
  An oscillator FEL will be direcly affected
The maximum time delay that an undulator can introduce is the difference between maximum field to when it is at ~zero field (slippage)
  Worse for long wavelengths
An example undulator with a K factor of 5 and a length of 10 m will introduce a time delay in the electron beam undulator exit time of 150 fs for a 600 MeV electron beam
  A helical undulator produces double the time delay (300 fs)

## Slide 7: Path Length
A three-pole chicane magnet arrangement could counteract the effect of undulator gap changes so that the total path length of the electron beam is kept constant.
A chicane with a peak field of 0.5 T and length of 1 m would add time delays of up to ~400 fs
Could use feedforward system to keep path length constant as undulator gap changed
The impact of these extra chicanes on the beam dynamics was not studied

## Slide 8: Photon Pulse Lengthening
The time delay between two photons emitted by the same electron, one at the entrance of the device and one at the exit, is Nl (slippage)
    Worse for long wavelengths
The example undulator with a K factor of 5 and a length of 10 m will introduce a maximum photon pulse lengthening of 163 fs with a 600 MeV electron beam.
A helical undulator with the same K parameter in both planes produces double the pulse lengthening.
In fact these are rather pessimistic estimates and modelling with an FEL code suggests that the actual FWHM only increases by about half these values.
Long wavelength experiments requiring the shortest possible pulses should use short undulators. A planar undulator which is 5 m long and with a K of 3 will only contribute 33 fs of pulse lengthening.

## Slide 9: Emittance Growth
Emission of radiation in an undulator causes a loss of energy by the electron and so if dispersion is present within the undulator this can lead to an emittance growth.
Although dispersion and its derivative will be set to zero at the entrance to an undulator the device itself will generate its own dispersion and so this must be considered to see if the effect is significant.
Approximate emittance growth is
Emittance growth due to a 10 m undulator of 50 mm period and peak field of 1 T is ~10‑7 nm rad, which is many times smaller than the natural emittance – negligible effect.
A second effect on the emittance, due to the change in transverse momentum of the electron, is generally smaller than the effect above by a factor of ~ 0.2 K2, so is also negligible.

## Slide 10: Energy Spread
Since the electrons passing through an undulator will emit photons over a relatively wide energy range in a discrete process the energy spread in the electron beam could increase significantly.
A helical undulator with a period of 50 mm, K value of 5 and length of 10 m would induce an additional energy spread of 0.0002 % (analytical) or 0.0001% (numerical)
Negligible in comparison with the nominal electron energy spread of 0.1 %.

## Slide 11: Bunch Length
An additional consequence of the self dispersion generated by the undulators is the effect this will have on the electron bunch length.
The change in the electron bunch length due to the undulator is given by
For a planar sinusoidal magnetic field R56 can be written as
An example undulator with a period of 50 mm, field of 1 T and length of 10 m, has R56 of 0.08 mm and will contribute an additional 0.3 fs to the electron bunch length – negligible.

## Slide 12: Summary
There are several possible issues which need to be checked
For the 4GLS project (low energy, long wavelength source) the greatest concern was the arrival time variation and photon pulse lengthening
The CSR emission from the dipoles was also a significant issue but it was never studied in enough detail to understand how variable this might be – a constant energy loss is no problem for the undulator beamlines
Impact on beam dynamics in general of the varying focussing and non-linear terms was not studied
The issues raised here (any others?) should also be considered for spontaneous undulator sources mounted after SASE FELs