## Slide 1: THE WISCONSIN SUPERCONDUCTING RF ELECTRON GUN UPDATE R.Legg (JLab); J. Bisognano, R. Bosch, D. Eisert, M. Fisher, M. Green, K. Jacobs, K. Kleman, J. Kulpin, G. Rogers (UW-Madison/SRC); J. Lawler, D. Yavuz (UW-Madison Physics); T. Miller (UIUC) March 6, 2012 DOE Award # DE-SC0005264

## Slide 2: Starting Point: Next Generation VUV/Soft X-ray Source
Probe physical, chemical, and biological systems on their critical temporal, spatial, and energy scales—femtoseconds, nanometers, and millivolts
Performance goals
  Full 6D coherence
  Short pulses
  High repetition rates into megahertz
  High peak and average flux
  Tunability and polarization control
  Many beamlines operating independently and simultaneously to spread costs
Superconducting-linac-driven FEL “farm” is an ideal solution
  CW
  Naturally a coherent process
  Seeding ensures temporal as well as transverse coherence

## Slide 3: Key Gun Parameters
Electric field at cathode – up to 45 MV/m
Peak surface magnetic field – 93 mT
Dynamic power loss into He – 39 W at 4K
Q – 2.5E9
Frequency – 199.6 MHz
RMS bunch length at gun exit – 0.18 mm
Cathode spot ~1 mm for 0.85 mm-mrad thermal emittance (Cs2Te)
At gun exit, dp/p ~ 2.5%, divergence – 7 mrad
Q – 200 pC
Kinetic energy – 4.0 MeV
With smaller spot, can be operated in lower charge modes with lowered emittance
Key Bunch Parameters

## Slide 4
CW Electron Gun is Critical Component
Wisconsin SRF e-gun

## Slide 5
Preparations for final e-beam weld
Bake at JLab to prevent Q-disease
Wisconsin SRF Electron Gun Progress

## Slide 6
Cold Test of Cavity at Niowave Completed and Installation into He Vessel Under Way

## Slide 7: February 7 Acceptance Test Successful
Cryogenic acceptance test at Niowave successfully completed
Test results
  Low field Q0 of 3 109 , as predicted by modeling
  Gradients in 10 MV/m range obtained, limited by test configuration (limited RF power, test coupler, and pumping)
  The cavity showed initial multipactor and field emission but both continued to process throughout the test
  Field is expected to substantially improve with continued processing after final assembly at Wisconsin
This test marks a major milestone in the SRF gun program, demonstrating both Q0 and the potential for high gradients in the gun after final processing planned at Wisconsin

## Slide 8: Q0 vs EACC results
Chart: integrated voltage (MV)
| 0.27140407701805097 | 0.18993997098346749 | 0.35165465224417286 | 0.28748577960967453 | 0.25038964667016433 | 0.24469008246805871 | 0.2855067414231709 | 0.30138134542458106 | 0.3432546010565885 | 0.41458765612020598 | 0.50421570341418542 | 0.51774554103772552 | 0.45985018688720153 | 0.44886564542351925
 | 4782572698.5731 | 3313065741.9856 | 1345513374.5888 | 2803041999.5771 | 3364566499.3834 | 3306970790.2619 | 2685392309.1471 | 2196439771.3762 | 1720680640.8533 | 795732507.2114 | 898031411.8315 | 808628191.504 | 418497777.0913 | 492655093.6383
 | 10000000 | 100000000 | 1000000000 | 10000000000
Gap in the data here shows conditioning progress from one run to the next.
R/Q = 147 Ω

## Slide 9: Frequency Map
Map which starts with a cold cavity at the correct frequency and moves back through the series of production steps producing an expected resonant frequency at each step
Actual cavity frequency was 199.47 MHz due to sign error in permittivity change from air to vacuum; corrected after test
FEA to Evaluate Stress and Deformation
State | Freq, MHz | D Freq, MHz | Volume, in^3 | D volume, in^3
Nominal, 4 K | 199.58953 | - | 6269.213 | 
Remove 1600 lb preload on tuner | 199.65256 | 0.06303 | 6267.753 | -1.46
Warmed to 273 K | 199.3704 | -0.28216 | 6294.653 | 26.9
Skin depth vs temp at 200 MHz | 199.3185945 | -0.05180 | 6295.853 | 1.2
Remove vacuum load | 199.2485945 | -0.07 | 6300.243 | 4.39
Change in permitivity, fvac/fair | 199.1947645 | -0.05383 | 6300.243 | 0
Undo BCP etch | 199.3688075 | 0.174042 | 6282.793 | -17.45
Final weld shrinkage, 0.7 mm | 199.280 | -0.088 | 6294.87 | 12.08
TABLE 1. Steps from cavity blank to final frequency |  |  |  | 

## Slide 10: High TC Solenoid
Specification developed from early field maps
And then we simulated. A lot.
Danfysik fabricating now, delivery in April / May 2012

## Slide 11: RF Coupler, HPA and LLRF
Power is introduced through a ceramic rf window and a tuned resonant structure.
Relatively low power, <10kW, at 1 mA of beam
20 kW solid state amplifier procured
Harris Corporation Broadcast Communications Division
Based on Jlab 12 GeV upgrade module

## Slide 12
Photocathode laser installation week of February 13

## Slide 13
Test Vault Preparations at UW
Clean room for cryomodule assembly
Electron Gun and Beam Diagnostic Line
RF
Photocathode Laser

## Slide 14: Current Scope
Demonstrate single bunch beam dynamics and operation of SRF gun
Low repetition rate drive laser
  Allows option of using doubled or tripled Ti:Sapphire laser
Cu Cathode Used for Initial Operation
  Little chance of cavity contamination from evaporated cathode material
  Cathode will not degrade over time like semiconductor
  No cathode preparation chamber needed

## Slide 15: Summary
Wisconsin SRF electron gun development moving forward as planned
Offers attractive capabilities as CW electron source for FELs and other applications
In the fall, we hope to have made our first low emittance electron bunch

## Slide 16: Coming Attractions
R&D on photocathode materials, including novel approaches, by Angle Resolved Photo Emission Spectroscopy (ARPES) studies on the Aladdin storage ring at SRC
Studies of the laser high harmonic generation (HHG) process for seeding, and other laser beam interactions
Bi thin film in the rombohedral phase. The surface state ~0.4 eV below the Fermi edge (blue spot) only has +2° emission angle.
This involves accessing a specific surface state without thermalization.
G. Bian, T. Miller, and T.-C. Chiang, Phys. Rev. B 80, 245407 (2009)