## Slide 1: Status of the ESS Project
François Javier
Systems Engineering Group
Presented at the DOE Safety Order Workshop
Jefferson Lab, VA, 2017-08-15--17
www.europeanspallationsource.se
11 August, 2017

## Slide 2: European Spallation Source
Located in SWEDEN (Lund) + data management in Denmark (Copenhagen)
ESS is an ERIC – A European Research Infrastructure Consortium
A partnership of 15 European countries
In-kind and cash contributions
  Sweden & Denmark are hosts: Construction 47.5% Cash Investment ~ 97%
  Operations 15%
  Non Host Member Countries
Construction 52.5% In-kind Deliverables ~ 70%
  Operations 85%
  Construction cost: 1.843 B€
  Annual operations cost 140 M€
2-3000 visiting researchers per year
People and organization
    400 employees
    48 nationalities

## Slide 3: ESS : an accelerator driven neutron facility
3
Superconducting Proton Accelerator
Energy: 2 GeV
Rep. rate: 14 Hz
Current: 62.5 mA
Pulse length: 2.86 ms
Average/peak power: 5 MW/125 MW
Neutron production Target
Rotating W target
He-gas cooled
42 beam ports
22 Neutron Instruments

## Slide 4: Overview of site and buildings
G01 G02 G04 | Acc tunnel Klystron gallery Cryo building
D02 | Target building
D01,D03 D04 ,D07,D08 D05,D06 | Experimental halls Experimental labs Substations
E01 E02 E03,E04,E05 | Experimental hall Beamline gallery Experimental labs
B01 B02 | Office building Labs, workshop
F01 F03 F04 | Pump station Logistic center Entrance building
H01 H05,H06 H09 H10 | Central utility bulding High voltage power Waste building Sprinkler central building
5 km north-east of Lund center- 74 hectares -26 buildings

## Slide 5: Target station layout and main systems
Remote Handling Systems
Active Cells Operations
Fluid Systems
Active Liquid Purification system
Primary Water Cooling Systems
Intermediate Water Cooling Systems
Intermediate Water Cooling for Water Systems
Contaminated Tanks
Gas Delay Tanks
Target Systems
Target Wheel & He Cooling
He Purification
Target HVAC System
Monolith Systems
Monolith vessel incl. covers and penetrations, NBW, PBW
Shielding systems
Tuning Beam Dump
Moderator Systems
Water Moderator
Reflector System
Cold Moderator
Target Moderator Cryoplant System

## Slide 6: Instruments
life sciences | magnetism & superconductivity
soft condensed matter | engineering & geo-sciences
chemistry of materials | archeology & heritage conservation
energy research | fundamental & particle physics
1st instrument ready for beam in 2021
8 instruments in user program in 2023
16 instruments in user program in 2025

## Slide 7: Journey to deliver the world’s leading facility for research using neutrons
2014
Construction Starts on Green Field Site
2009
Decision to Site ESS in Lund
2025
ESS Construction Phase Complete
2003
European Design of ESS Completed
2012
ESS Design Update Phase Complete
2019
Machine Ready for
1st Beam on Target
2023
ESS Starts
User Program

## Slide 8
September 2014: Civil construction groundbreaking

## Slide 9: February 2017

## Slide 10: May 2017

## Slide 11: Now
Target monolith and active cells
Accelerator tunnel

## Slide 12: ESS Life Cycle Model and status
Design
Construction
Commissioning
De-commissioning
Operation
ESS generic systems life cycle model
CDR
TRR
ORR
Instruments
Target
Accelerator
What is ahead for the ESS project?
Civil Engineering Construction
  Target Monolith and Active Cell
  Instrument Halls, Laboratories
  Rad Waste Building
  Campus Area (offices, labs, reception building)
Accelerator
  Installation & commissioning
Target
  Construction & commissioning of Monolith, Active Cells
  Design, construction and commissioning of auxiliary systems
Integrated Control Systems
  Design, construction and commissioning
NSS Instruments
  Design, construction and commissioning

## Slide 13: Present ‘Installation permit’ process
Application sent to SSM in May 2016 covering installation and trial operation of Warm LINAC
Significant number of requests for additional information
Delivery of additional documentation (including updated PSAR) completed 3rd March ‘17
SSM trial operation review on hold pending installation review

## Slide 14: Conditional Permit from SSM received 30 June 2017
To install devices intended to generate ionizing radiation
Cover Accelerator, Klystron, and Target buildings
Installation conditioned that SSM received and reviewed
  detailed safety classification of SSC
  IT security procedures for development of software (PSS, TSS)
Conditioned that ESS follows commitments presented in submission
Comprehensive review report received with detailed request for trial operation application
Trial operation is submitted to specific permit

## Slide 15
A BRIEF INTRODUCTION TO SAFETY

## Slide 16: Radiological hazards orders of magnitude for target station Radioactive inventory– Prompt and residual radiation
Monolith area
Utility area
Active cells facility
∼ 4.1017 Bq
∼ 4.1012Bq
∼ 8.1016 Bq
shielding
Designed to attenuate with a criterion of 3 μSv/h
Dose map of the target wheel (irradiated 5 years + 14 days of cooling time) in the active cell.
(2000 Sv/h contact)

## Slide 17: Radiological hazards orders of magnitude for Accelerator Radioactive inventory from activated air – Prompt radiation
Shielding
(concrete + earth)
Closest area off site – max 2 nSv/h
2 μSv/h max on berm
Beam on - 1 W/m loss
Beam on - full beam loss
400 mSv/h max on berm
Closest area off site – max 4 mSv/h
15 DAC max (14 GBq) in the tunnel during operation and beam on (1 W/m loss)

## Slide 18: Safety Framework
The protection level expected is defined through dose limits and reference values provided by the national regulation and SSM conditions.
ESS-0000004 rev 5 (January 2017) |  | 
Operating conditions Initiative event likelihood | Workers limit (effective dose) | Public limit (effective dose)
Normal operation - H1 | 2 mSv/year (average) 10 mSv/year (max) | 0.1 mSv/year (0.05 mSv/year GSO)
Anticipated events - H2 F > 10-2 | 10 mSv/event | 0.1 mSv/occurrence
Unanticipated events - H3 10-4 < F < 10-2 | 20 mSv/event | 1 mSv/occurrence
Improbable events (DBA) – H4 10-6 < F < 10-4 | 20 mSv/event | 20 mSv/occurrence
Highly improbable events – H5 F < 10-6 | 250 mSv/event | 100 mSv/occurrence
Events and circumstances that affect the facility shall be divided in 5 event classes based on frequencies
The safety functions are the functions implemented to stay below these limits
The safety functions are identified through the radiation safety analysis

## Slide 19: Defence in Depth and safety functions grouping
The DiD shall be tailored to the activities and associated safety stakes
A failure of one level shall not be able to propagate to a subsequent level
DiD level 3 shall be independent of DiD level 1 and 2
DiD level 4 shall be independent of DiD level 1-3

## Slide 20: Safety functions identification process
  Safety functions to be performed for normal/planned operation
  Additional safety functions or
  additional requirements on the safety functions identified in step 1
  The combination of the set of functions identified in step 1 and 2 must show, as far as practical and reasonable, a proper implementation of a number of consecutive and independent levels of protection that would have to fail before harmful effects could be caused to people or environment
Step 1 :
Radiological hazard induced by the facility and its operation
Step 2 :
Accident analysis
Step 3 :
Robustness of defence in depth