## Slide 1: LANSCE and TA 53 New Activity Review Process
Lyndsey Fyffe, PhD
August 15, 2017
DOE Accelerator Safety Workshop 2017
Newport News, VA
LA-UR-17-26950

## Slide 2: Outline
August 15, 2017
2017 Accelerator Safety Workshop
New Activity Process Overview
Requirements for Activity Owner
Subject Matter Expert (SME) Reviews
Final Approval
Case Study
14:50

## Slide 3: New Activity Review Scope
Goal: Review new activities for potential safety basis impact to the facility and/or co-located processes
Addresses activities outside of the scope of the safety basis
Applicable to new or changed work activities proposing to start operations in an accelerator associated facility
Exceptions:
  Maintenance or construction activities
  Low hazard activities that do not increase chemical or radiological inventory
  Operations encompassed by the current authorization basis
  Minor modifications to previously approved activities

## Slide 4: New Activity Review Process Flow
New Activity or revision to activity is proposed
New Activity Owner provides detailed description of activity
SMEs review the activity and work with the owner to respond to questions
FOD determines approval and tracks conditions to ensure timely completion
SMEs transmit questions and any conditions of approval to the FOD
Activity commences operations

## Slide 5: Activity Owner Requirements
Goal: Provide sufficient detail for each SME to review the activity and determine applicable regulations and impacts to human health and the environment
Important components:
  Contact information
  Radioactive materials
  Chemicals
  Explosives
  Biological materials
  Facility requirements
  Security requirements
  Waste generation and disposition
Chemical Name | Chemical Form | Max. Amount | How is it tracked?
The Chemical Identification Table is one component of the Activity Owner Form

## Slide 6: SME Reviews
Review the activity and develop an understanding of impacts on the facility and co-located activities through:
  Discussions with the activity owner
  Discussions with other SMEs
  Impact analysis for co-located activities
  Walk downs of the facility
Respond to SME specific questions on the area specific review form to ensure coverage of issues
Discuss concerns with the activity owner
Return completed SME review form to the Facility Operations Director (FOD)
  Provide conditions of approval as necessary

## Slide 7: SME Reviews [1]
Facility Operations Manager
  Tracking of materials (chemical and radiological)
  Facility infrastructure to accommodate the activity
Safety Basis
  Hazard categorization
  Activity documentation
Emergency Operations
  Building run sheet
  First responder exposure assessment
  Emergency planning hazard assessment
  Special emergency response measures
  Building exit concerns
Industrial Hygiene
  Exposure assessments
  Physical hazards
  Ergonomics
  Electrical safety concerns
Radiation Protection
  As Low As Reasonable Achievable (ALARA) review
  Equipment needs (e.g. hand and foot monitors)
  Radiation Protection Support
Criticality Safety
  Criticality Safety Evaluation (CSE) requirements

## Slide 8: SME Reviews [2]
Waste Management
  Waste requirements
  Legacy waste
  Waste minimization
Engineering
  Life safety equipment
  Changes to the facility structure or envelope
  Impact on facility mechanical systems
  Construction, remodeling, decommissioning
Explosives Safety
  Approved explosives list
  Explosive site plan
  Requirements for co-located materials
Biological Materials
  Approval by the Institutional Biosafety Committee
  Biosafety Level of agents or materials
Security
  Facility specific security capability
  Security plan updates
Maintenance
  New or revised preventative maintenance required
  Revisions to facility maintenance plan

## Slide 9: Final Approval
Approval |  | 
FOD/Name | Z Number | Signature
Approved |  | 
Conditionally approved |  | 
Not approved |  | 
Conditions: |  | 
Comments: |  | 

## Slide 10: Case Study: General Actinide Chemistry Activity
New activity requiring lab space co-located within the accelerator footprint
Unaffiliated with accelerator operations
Increases radiological and chemical inventories
Requires use of ventilation hoods, pressure vessel
New Activity Review process identifies several conditions for approval of this work, including:
  Removal of legacy waste
  Waste management review
  Development of an Integrated Work Document (IWD)
  ALARA review
  Review by an Electrical Safety Officer (ESO) and installation of non-GFCI outlet
  Required updates to emergency response protocols

## Slide 11: Conclusions
New Activity Review Process provides quick method for SME review and FOD approval of the activity
SME Reviews highlight potential hazards or issues
Comments, conditions, and contingencies from the SMEs are combined and sent to the FOD for final approval
Process captures issues that might not otherwise be addressed prior to startup

## Slide 12: Thank you Questions/Comments: Fyffe@lanl.gov (505) 665-4584