## Slide 1: SLAC Excess Material Disposition Various Sites
R. Ford, J. Allan, O. Ligeti, Y. Pilastro, S. Rokni

## Slide 2: Outline
  Scope
  Strategy for material disposition
  LINAC S0-10 and Beam Switchyard (BSY) Disposition
        Volumes
  Support of BSY reconfiguration project
  Recycling of Lead (Pb)
  Planned work for FY2018
Summary / Accomplishments

## Slide 3: Disposition strategy: 4-prong approach
Establish clear responsibilities and requirements for managing removed materials (The AMMP)
Pre-characterize materials and equipment
Prepare appropriate space for material processing (area 1, area 2, tent, MSY)
Manage disposition of excess materials in a safe and efficient manner (radioactive waste, hazardous waste, recycling)
Notes: Includes mgt of subcontract

## Slide 4: Prong 2: Radiological and hazardous characterization
  S0-10
    >1000 in-situ measurements
  Beam switchyard
    Majority radioactive – two 40 yd3 bins were recycled
  Beam dump east
    Mostly ESA materials, required survey and sorting and process knowledge determination
Notes:     Co-57, (270 d)
    Co-60, (5.2 y)
    Co-58, (72 d)
    Na-22, (2.6 y)
    Sc-46, (84 d)

## Slide 5: Prong 3: Tent construction, Area 1&2 Prep
This was the heaviest rainy season since 2010

## Slide 6: Prong 4: Manage disposition of materials
Radioactive Waste
Recycling
Hazardous Waste
Manage subcontractor (Gilbane)

## Slide 7: Prong 4: MSY and BDE waste shipments
First Rail Spur Shipment (10 Sea-Lands)

## Slide 8: Waste disposal and recycling statistics
Chart: Total Truckloads
| Rad Waste | Recycling | Haz Waste
FY16 | 23 | 66 | 5
FY17 | 49 | 88 | 3
Chart: Total Tons
| Rad Waste | Recycling | Haz Waste
FY16 | 467 | 427 | 42
FY17 | 292 | 448 | 5
Prevented the accumulation of unneeded materials and prevent a future legacy problem.
DOE-STD-6004

## Slide 9: Area 1 Materials from S0-10

## Slide 10: BSY reconfiguration scope statement
Remove obstructions to future LCLS-II beamlines
Remove unneeded legacy equipment
Design, fabricate, and install a new beamline
Design, fabricate, and install new collimators and Beam Containment System devices to permit continued LCLS operations through the BSY before LCLS-II is installed

## Slide 11: Beam switchyard: progress photos
Removal of materials from this area will prevent unnecessary exposure for future work in the BSY during high-power LCLS-II operations, by preventing their activation
ALARA practice

## Slide 12: BSY: Survey of materials
Two loads were recycled using Material Release Program Procedure
Cost avoidance of ~$100K and 2 Sea-Lands
Remainder disposed as radioactive waste

## Slide 13: BSY
Services Provided for S0-10 and BSY:
Contractor oversight
Staff Augmentation:
  Contract RCT
  Waste Shipper
Waste identification and inventory
Recycling of hold materials i.a.w. DOE-STD-6004 2016 and RPD-010

## Slide 14: Beam dump east: Progress to date
Output: 1 Sea-Land, 1 flatbed, 7 recycling bins, 3 hazardous waste bins, several truckloads of hazardous blocks
Contractor vacuumed the area to remove hazardous debris (lead, cadmium)

## Slide 15: FY2018 Excess material disposition
BTH/undulator hall radioactive waste disposal (LCLS-II)
Beam dump east waste and recycling
Legacy radioactive waste disposal
Lead recycling
    Large amounts of excess lead can be cleared
    Development of clearance protocols is in progress
    Benefits to entire DOE complex

## Slide 16: SLAC Instruments for Common Metal Clearance Measurements
Ludlum Model 2241 meter with
1”x1” NaI probe (DT ~ 0.03 Bg/g; 30 nSv/h) &
small-area GM pancake probe
Field
Gamma Spectrometer
Portal
Gate
Monitor
What about Lead?

## Slide 17: Clearance of Lead (Pb)
DOE Standard DOE-STD-6004 (2016) was developed for clearance of common metals (e.g., Al, Fe and Cu) in accelerator facilities
Unlike common metals, there are no proxy radionuclides for lead clearance measurements in electron accelerators
    Tl-204 (pure beta emitter, Emax = 764 keV, 3.78 yr) dominates activity and risk in lead in most cases
Sensitivity of a small-area (15.5 cm2) GM probe for Tl-204 in lead was calculated with FLUKA to be 8 cpm per Bq/g.
With an average background of 120 cpm, detection threshold of a large-area GM meter (4x15.5 cm2) can be 0.8 Bq/g for Tl-204 inside lead, which is lower than ANSI N13.12 SL of 1 Bq/g.
Lead clearance measurement protocol (e.g., static 1-min measurements with large-area GM probe on contact with a lead brick under maximum background of 180 cpm) is being developed to meet IFB release criterion.

## Slide 18: Summary
Radioactive waste disposal campaign for BSY resulted in disposal of most of the generated BSY waste
    Some waste postponed to FY18
Successful recycling campaign, large cost avoidance
Successful disposal of hazardous waste disposal from BDE yard, substantial reduction in volumes
Continuous and effective safety oversight
Project management capability enabled efficient allocation of resources and meeting of project goals

## Slide 19: Team Work

## Slide 21: Backup

## Slide 22: Scope of LCLS-II material disposition support
  Disposition of excess materials to approved end points from:
          Sectors 0-10 linear accelerator housing (tunnel)
          Klystron gallery
          Beam switchyard (BSY) - Reconfiguration
          Magnet storage yard (MSY)
          LCLS undulator and dump halls (FY18)
  Inventory, characterize, disassemble, package, transport, treat and dispose of low level and mixed radioactive waste, hazardous waste, universal waste, class II waste
  Recycle excess materials impacted by DOE Metal Moratorium, as well as non-impacted materials in the klystron gallery
  Site preparation to facilitate material disposition
  Support for removal of materials from BSY reconfiguration

## Slide 23: BSY sump: Before and after

## Slide 24: Interrelationships and collaboration
Radiation
Protection
Gilbane
Hazardous Waste Ops
Radioactive Waste Disposal
Field Safety
Accelerator Directorate, LCLS-II
Environmental Prot.
F&O
Industrial Hygiene
Security
Procurement
Bldg Inspection Office
Property Control
Legal Dept.
Communications

## Slide 25: Prong 4: Hazardous waste operations
Hazardous Waste:
Concrete and debris with heavy metals (lead, cadmium)
Tanks with specialty gases
FY2016: 42 tons, 5 loads
FY2017: 5 tons, 3 loads
Total: 47 tons, 8 loads
Vacuuming operations prevented runoff into stormwater drains

## Slide 26: BSY: D-10 dump removal

## Slide 27: Beam dump east yard clean-up
Drawing from all disciplines: IH, Field Safety, EP, Hazardous Waste and Radiation Protection
Opportunity to dispose of some of the radioactive waste within the ongoing campaigns (S0-10 and BSY)
The area will be returned to the AD
Next phases (FY18) to include tank removal and radioactive waste disposal