## Slide 1: Hall C Cryogenic Target Status
Dave Meekins
JLab Target Group
January 20, 2017

## Slide 2: Summary of Alterations
External upgrades:
  New/refurbished vessels and ancillary piping and support structure
  New vent cap
  Minor gas panel changes
  New switch panel
  New supply and return piping
  New chamber config
Internal upgrades:
  New loop piping
  New thermometry and heaters
  New cells/blocks
Upgraded controls
Repaired and replaced stripped/damaged components

## Slide 3: Pressure Safety
Hall A and C Cryotargets nearly identical
Alteration of existing system
  Minor changes to gas panel
  Replacement of swap panel
  Refurbishment/replacement of vessels
  New piping to pivot
  New overpressure protection
  New Loop piping
  New Cells/Blocks
All work performed in compliance with ESH&Q 6151 and applicable Codes
  ASME B31.3, ASME PCC-2 (Piping)
  ASME BPVC VIII D1, NB-23 (Vessels)

## Slide 4: Configuration
Top loop 4 and 10 cm cells
  Fluid H2/D2
Bottom two loops 10 cm cells
  Fluid H2/D2
Only two loops can be filled at a time.
  Filled with H2 or D2
  D2 tank can be filled with H2 to give 2nd H2 loop
D2 has been purchased but due to NMCA will most likely not be here in time for run
  Purification of D2 system will be required (Tank purification takes time)

## Slide 5
Target Configuration
Loop 1
  4 cm 1.6” CF cell
  10 cm 1.6 CF cell
Loop 2
  10 cm 2.6” Cell En route
Loop 3
  10 cm 2.6” Cell En route
Solid Targets
  10 cm dummy with C in center (Match rad length of 10 cm LH2)
  4 cm dummy (rad length of 4 cm LH2)
  Optics 1 and 2
  C hole
  C targets 6%, 1.5%, and 0.5%
  1.2% 10B4C and 11B4C
  2% Be (en route)
  BeO

## Slide 6
Dummy and Optics Targets
Targets can be positioned quickly
Positions for
  0
  +/- 2
  +/- 3.75
  +/- 5
  +/- 7.5
  +/- 10 cm
Current Optics Config:
  0 and +/- 10 cm
  +/- 5 cm

## Slide 7
Fully assembled 4cm/10cm combined cell block

## Slide 8: Test Cryostat
New test cryostat (developed in Summer 2016)
Test components at design temperature and pressure
  Temperature below 6K
  Pressures above 200 psi.
Allows testing of fully assembled cell blocks, feedthrus, etc.
Aid in development of future sealing techniques

## Slide 9: Cryogenics
ESR 15K circuit shall be used to cool the target
Hall A target will be operated concurrently
Two target operation will require close coordination between CRYO, Hall C and Hall A.

## Slide 10: Status
Complete
  Tank refurbishment (compliant with 6151)
  Tank support structure repair/painting
  New loops, solid targets*
  New alignment system*
  Upgraded gas panel and piping
    New swap panel
  Upgraded controls
    Software*
    Heaters (higher voltage, lower current)*
    Temp controls (6 per loop)*
    Aux heater controls (all power supplies are in Hall)*
In process
  10 cm production cells (2.6 inch OD)
  Installation of piping
  Installation of cells/blocks
  Electrical upgrades
* Same as Hall A cryotarget