## Slide 1
HPS Collaboration Meeting
JLAB, May 26-27 - 2011
Tracker Design Status
M.Oriunno, SLAC

## Slide 2
Vacuum Chamber | Existing Scattering Chamber Hall B
Vacuum pressure | 10-6 Torr
Max. radiation Dose | 1X1014 2 GeV electrons (~3X1013 1MeV NEQ
Max. Magnetic Field (Dipole field Y) | 0.5 Tesla
Target material and Thickness | 0.125%, Tungsten, 4 um
Target Position (X,Y,Z) from the center of magnet (mm) | 29.87, 0.0, -457.2
Number of active planes | 5 top, 5 bottom
Stereo sensors per plane | 2
Stereo angles L1,L2,L3,L4, L5 (mrad) | (0 / 100 ), (0 / 100 ), (0 / 100 ),(0 / 50 ),(0 / 50 ) mrad (anti-clockwise seen from upstream)
Si dead edges location from the beam (mm) | ±1.5, ±3.0, ±4.5, ±7.5, ±10.5
Z Position (distance from the target along the photon beam) (mm) | 100, 200, 300, 500, 700
X Position (distance from the target) (mm) | 0,0,0,0,0
Y Position (distance from the target) (mm) | Top and Bottom planes move independently along Y. Movement range ±20 mm
Pitch Movement q | ±20 mrad
Whole Teelscope movement x (mm) | ±20 mm
Whole Teelscope movement yaw f | ±20 mrad
Max. Material Budget X/Xo | 2%
Installation and maintenance | In Situ (Scattering Chamber fixed in the magnet)
Si Bias Voltag, Nominal - Maximum | 150 V – 500 V
Operating temperature | 0o C
Front End Readout | APV25
APV heat Load | 2.31 mW / channel x 128 channels = 395 mW
Numberof Chip per sensor | 5
Heat Load per hybrid | 2.0 W
Heat Load per sensor (Leakage Current) | 100 mW
Heat load per sensor Radiative | 1.0 W
Release - 5/18/2011
Functional
Environment
Geometry
Det.Operation
Test Run: List of Requirements
Physics requirements
Eng. requirements

## Slide 3
Target at Z = -457.2 mm
Si Planes along the photon beam
Dist. from target
100 mm (0o/100o)
100 mm (0o/100o)
100 mm (0o/100o)
200 mm (0o/50o)
200 mm (0o/50o)

## Slide 4
Tracker Design
920 mm
150 mm
±50 mrad
±100 mrad

## Slide 5
Tracker Design

## Slide 6
260 mm
Top Plane
Bottom Plane
Linear Guides
Target
Y ± 20 mm
Y ± 20 mm
q ± 20 mrad
Y ± 20 mm
Y ± 20 mm
920 mm

## Slide 7
Vacuum Chamber
Vacuum Chamber
Compression Springs
Actuator
Actuator
beamline
Tracker Motion

## Slide 8
Alignment & Positioning
Motion with 5 independent axis : 2 per half silicon planes, 1 for the target
Additional actuators for the alignment in the horizontal plane (X, q) ?
Bam position information in the scattering chamber : reference system, precision ?
Maximum excursion of the beam due to magnetic filed error, beam loss accident
Does the beam move in X and Y ?
Physical edge of the detector at 1.5 mm, additional clearance is needed ? Beam stability or loss

## Slide 9
Test Run: Experimental Layout

## Slide 10
Integration with vacuum chamber

## Slide 11
x 10 Hybrids | Qt.y | AWG | D conductor (mm) | D total (mmm) | Area (mm2)
Signals | 140 | 26 | 0.405 | 1 | 109.96
Power | 16 | 22 | 0.644 | 1.3 | 21.24
HV | 20 | 24 | 0.511 | 1.16 | 21.14
 |  |  |  | Total | 152.33
 |  |  |  | Total with 30% packaging factor | 198.03
Cooling Tube | 4 |  | 6 |  | 
Motion | 4 |  | 6 |  | 
List of Cables/Pipes

## Slide 15
Installation/Maintenance

## Slide 16
80 mm
Wire scanner 14 um, Tungsten
Target Foils 10 um
Target Design, stationary – not spinning
Vertical movement
± 100 mm
Target Holder

## Slide 17
The Detector Module
Frame Support with High Conductivity Carbon Fibre
K13UD available at FNAL
Cooling on the back plane of the Hybrid :
Cold plate connected to an external chiller
Started the construction of a Thermo-Mechanical mockup
100 mm
40 mm
Cooling
Heat
Heat
CF frame

## Slide 18
Motion
Environment req.s :
High Magnetic Field 5’000 gauss
Vacuum 10-6 torr
Min. 5 independent Degree of Freedom (2 x 2 Si plane, 1 target)
Standard Stepper motors do not operate in magnetic field
Too many d.o.f. to place them outside the fringe field
Piezo-Motors:
Excellent performances in vacuum and mag. field
Asked P&I for a quote for 4 motors + controllers ~ $50’000
Welded bellow actuators
Stroke length
Repeatability
Pneumatic or hydraulic

## Slide 19
Vacuum Chamber
Feed-through
Hydraulic operated (incompressibility)
Need to make small R&D to validate the precision and resolution required
(10um and 50um)
Concerns on thermal stability
Bellow actuator

## Slide 20
Open questions….for this meeting
Confirm the final location of the tracker in the magnet
Alignment strategy with beamline
Number of remotely controlled d.o.f. / actuators
Protection against beam loss accidents