## Slide 1
1- Vacuum chamber proposal
1.1- Stainless steel chamber design and calculations
1.2- Aluminum chamber design and calculations
2- Ecal Crystal support frames
2-1- design
2-2- calculations
3- Ecal assembly design
3-1 Ecal frames and vacuum chamber
3-2 Ecal frame supports principle
3-3 Enclosure + pcb
HPS Ecal and vacuum chamber design

## Slide 2
Vacuum chamber design

## Slide 3
2 mm
3 mm
2 mm
10 mm
10 mm
Honneycomb pillar
Stainless steel vacuum chamber design

## Slide 4
Internal shape in conformity with Jlab information except electron Left hole shifted of 4 mm to right ,elliptic shape R 26.63
Stainless steel vacuum chamber dimensions: front cut view

## Slide 5
Stainless steel vacuum chamber dimensions: top cut view

## Slide 6
Stainless steel vacuum chamber calculation: deformations

## Slide 7
Stainless steal: 304 L WN 1.4306.
Rp0,2 Elastic Strength = 200 Mpa
Rm (Critical Strength) = 500 Mpa
Norm CODAP (Pressure vessel)
Max 2/3 Rp 0.2 = 140 Mpa
Stress max 151 Mpa due to corner of pillar are singularity of calculation and not representative
Max real stress = 130 Mpa
Stainless steel vacuum chamber calculation: stress

## Slide 8
Thickness : 6mm
Thickness : 2mm
Thickness : 20 mm
Thickness : 3mm
Aluminum vacuum chamber design

## Slide 9
Pressure calculated on Honeycomb = 0.97Mpa
Crush strength of Aluminum honeycomb
ECM 3.2-130 (Euro composite)=3.38 Mpa
Aluminum vacuum chamber calculation: deformations

## Slide 10
Aluminum 5083
Rp 0.2 =130 Mpa
Rm = 260 Mpa
Max 2/3 Rp 0.2 = 85 Mpa
Stress max 97 Mpa due to corner of pillar are singularity of calculation and not representative
Max real stress = 70 Mpa
Aluminum vacuum chamber calculation: stress

## Slide 11
The 2 chambers follow the design rules (french CODAP for pressure vessels)
But…
From the mechanical point of view , stainless steel is better :
In terms of manufacturing and welding (more common in industry)
2) The rear side of the horizontal plates of 3 mm (instead 6mm Aluminum) gives a bigger gap for cooling tubes, insulation and preamps
Simulations must also show results with steel
Conclusions about the 2 vacuum chamber design proposal

## Slide 12
HPS Ecal frames design

## Slide 13
Same design as DVCS but simplified (rectangular)
46 crystals on a line
2 spacers to block them
2 metal sheets (thickness= 0,12mm) tensed and glued on the frames
Crystal support frames design

## Slide 14
The frames are stacked one by one (APD control at each line)
Crystal support frames stacking (1)

## Slide 15
The frames are clamped with screws
Each side is clamped with a strong support plate
rear frames
front frames
1 3 Screws on each frame
2 beams added to give more inertia at the assembly
front adjustment of the frames
Crystal support frames stacking (2)

## Slide 16
Front frames
Rear frames
D max =0,042mm
D max =0,07mm
Stress max :12Mpa
Stress max :18Mpa
Crystal support frames calculations

## Slide 17
Assembly design

## Slide 18
The vacuum chamber with the ECAL

## Slide 19
Support
Adjustment system for each block
Top and bottom ECAL independent adjustment

## Slide 20
The vacuum chamber with the ECAL: top view

## Slide 21
The vacuum chamber with the ECAL: front cut view

## Slide 22
Detail of the gaps between ECAL and chamber

## Slide 23
PCB
2 mother board R + L
2 Connection board R + L
Connection similar to DVCS
Copper plate
Connection to the preamps and read-out

## Slide 24
Copper plates with cooling tubes around the Ecal
6 mm foam for insulation
Thermal enclosure