## Slide 1
Hypernuclear spectroscopy in Hall A
  12C, 16O, 9Be, H
  E-07-012
Experimental issues
Results
High-Resolution Hypernuclear Spectroscopy
JLab, Hall A Result
G. M. Urciuoli

## Slide 2
JLAB Hall A Experimental setup
The two High Resolution Spectrometer (HRS) in Hall A @ JLab
Beam energy: 3.7 GeV
sE/E : 2.5 10-5
Beam current: 100 mA
Targets : 12C, H2O, 9Be, H
HRS – QQDQ main characteristics:
Momentum range: 0.3, 4.0 GeV/c
Dp/p (FWHM): 10-4
Momentum accept.: ± 5 %
Solid angle: 5 – 6 msr
Minimum Angle : 12.5°

## Slide 3
good energy resolution
reasonable counting rates
forward angle
septum magnets
do not degrade HRS
minimize beam energy instability
“background free” spectrum
unambiguous K identification
RICH detector
High Pk/high Ein (Kaon survival)
DEbeam/E : 2.5 x 10-5
2. DP/P : ~ 10-4
3. Straggling, energy loss…
~ 600 keV

## Slide 4
JLAB Hall A Experiment E94-107
16O(e,e’K+)16N
12C(e,e’K+)
16O(e,e’K+)
9Be(e,e’K+)
H(e,e’K+)Λ
Ebeam = 4.016, 3.777, 3.656 GeV
Pe= 1.80, 1.57, 1.44 GeV/c Pk= 1.96 GeV/c
qe = qK = 6°
W  2.2 GeV Q2 ~ 0.07 (GeV/c)2
Beam current : <100 mA Target thickness : ~100 mg/cm2
Counting Rates ~ 0.1 – 10 counts/peak/hour
  A.Acha, H.Breuer, C.C.Chang, E.Cisbani, F.Cusanno, C.J.DeJager, R. De Leo, R.Feuerbach, S.Frullani, F.Garibaldi*, D.Higinbotham, M.Iodice, L.Lagamba, J.LeRose, P.Markowitz, S.Marrone, R.Michaels, Y.Qiang, B.Reitz, G.M.Urciuoli, B.Wojtsekhowski, and the Hall A Collaboration
  and Theorists: Petr Bydzovsky, John Millener, Miloslav Sotona
E94107 COLLABORATION
E-98-108. Electroproduction of Kaons up to Q2=3(GeV/c)2 (P. Markowitz, M. Iodice, S. Frullani, G. Chang spokespersons)
E-07-012. The angular dependence of 16O(e,e’K+)16N and H(e,e’K+)L (F. Garibaldi, M.Iodice, J. LeRose, P. Markowitz spokespersons) (run : April-May 2012)
Kaon collaboration

## Slide 5
Kaon Identification through Aerogels
The PID Challenge
Very forward angle ---> high background of p and p
TOF and 2 aerogel in not sufficient for unambiguous K identification !
AERO1
n=1.015
AERO2
n=1.055
π
k
p
ph = 1.7 : 2.5 GeV/c
Protons = A1•A2
Pions = A1•A2
Kaons = A1•A2
p
k
All events
π
k

## Slide 6: RICH Algorithm (G.M. Urciuoli et al. NIMA 612, 56 (2009)
When a charged particle crosses the RICH detector, N Cherenkov photons hit the sensitive RICH
surface and consequently N measurments of the angle , corresponding to the speed of the
particle, are obtained. These N measurments are, with good approximation, Gaussian distributed around , with a variance that is dependent on the RICH and can be determined experimentally and indipendently from the N measurments. Consequently, the sum:
Follows the distribution with N degree of freedom.
Three particle hypotheses : Three possible values Three tests
π
k
P
Usually only one of the three values acceptablle only one particle hypothesis valid

## Slide 7
RICH – PID – Effect of ‘Kaon selection
p
P
K
Coincidence Time selecting kaons on Aerogels and on RICH
AERO K
AERO K && RICH K
Pion rejection factor ~ 1000

## Slide 8: METHOD TO IMPROVE THE OPTIC DATA BASE: An optical data base means a matrix T that transforms the focal plane coordinates in scattering coordinates:
To change a data base means to find a new matrix T’ that gives a new set of values:
:
Because:
this is perfectly equivalent to find a matrix
you work only with scattering coordinates.
.
From F you simply find T’ by:

## Slide 9: METHOD TO IMPROVE THE OPTIC DATA BASE (II)
Expressing:
You have:
just consider as an example the change in the momentum DP because of the change in the data base:
with
a polynomial expression
Because of the change DPDP’ also the missing energy
will change:
In this way to optimize a data base you have just to find empirically a polynomial
in the scattering coordinates that added to the missing energy improves its resolution
:
and finally to calculate

## Slide 10
A Data base cannot be improved if the missing energy does not show any unphysical dependence on scattering coordinates. In fact, in this case any change in the data base will be equivalent to an addition of a polynomial in the scattering coordinates to the missing mass value and will cause an unphysical dependence on scattering coordinates.
Vice versa, to check if the data base is the «best» one, a test has to be performed (for example with a «ROOT» profile) to investigate about unphysical dependence on scattering coordinates of the missing energy.

## Slide 12
Be windows
H2O “foil”
H2O “foil”
The WATERFALL target: reactions on 16O and 1H nuclei

## Slide 13
1H (e,e’K)L
16O(e,e’K)16NL
1H (e,e’K)L,S
L
S
Energy Calibration Run
Results on the WATERFALL target - 16O and 1H
Water thickness from elastic cross section on H
Precise determination of the particle momenta and beam energy
using the Lambda and Sigma peak reconstruction (energy scale calibration)

## Slide 14
Fit 4 regions with 4 Voigt functions
c2/ndf = 1.19
0.0/13.760.16
Results on 16O target – Hypernuclear Spectrum of 16NL
Theoretical model based on :
SLA p(e,e’K+)Λ(elementary process)
16N interaction fixed parameters from KEK and BNL 16ΛO spectra
Four peaks reproduced by theory
The fourth peak (Λ in p state) position disagrees with theory. This might be an indication of a large spin-orbit term SΛ

## Slide 15
Fit 4 regions with 4 Voigt functions
c2/ndf = 1.19
0.0/13.760.16
Binding Energy BL=13.76±0.16 MeV
Measured for the first time with this level of accuracy
(ambiguous interpretation from emulsion data; interaction involving L production on n more difficult to normalize)
Within errors, the binding energy and the excited levels of the mirror hypernuclei 16O and 16N (this experiment) are in agreement, giving no strong evidence of charge-dependent effects
Results on 16O target – Hypernuclear Spectrum of 16NL

## Slide 16
9Be(e,e’K)9LiL (G.M. Urciuoli et al. Submitted to PHYS REV C)
Experimental excitation energy vs Monte Carlo Data
(red curve) and vs Monte Carlo data with radiative
Effects “turned off” (blue curve)
Radiative corrected experimental excitation energy vs theoretical data (thin green curve). Thick curve: four gaussian fits of the radiative corrected data

## Slide 17
An elementary model for the (e,e′K+) reaction with a diﬀerent balance of spin-ﬂip and non-spin-ﬂip amplitudes might help to resolve the disagreement with theory of the relative strenght of the peaks in the doublets

## Slide 18: Binding energy difficult to determine because of the uncertanties on the values of the incident beam energy and of the central momenta and angles of HRS spectrometer Binding energy determined calibrating the spectrum with
Is equal to a shift that is equal for all the targets + a small term that depends unphysically on scattering coordinates

## Slide 19: Conclusion
An exciting hypernuclear physics program was carried out in Hall A at Jlab
Among the several results obtained we can mention:
First evidence of excited core states in
Possible indication of a large spin-orbit term SΛ
Binding Energy BL=13.76±0.16 MeV inmeasured for the first time with high level of accuracy
No strong evidence of charge-dependent effects
Possible diﬀerent balance of spin-ﬂip and non-spin-ﬂip amplitudes in the elementary model for the (e,e′K+) reaction.
Different technical issues solved. This could be of great importance for future expements (not only in the hypernuclear field).

## Slide 20
Spare

## Slide 21
test
Average
Single photon

## Slide 22
12C(e,e’K)12BL M.Iodice et al., Phys. Rev. Lett. E052501, 99 (2007)

## Slide 23: The test is completely independent of the test on the mean and can be used hence together with it.
test test on the variance of the distribution
Calculation of the average of the test on the mean of the distribution
=
The test always gives better rejection ratios than Maximum likelihood method

## Slide 24
Radiative corrections do not depend on the hypothesis on the peak structure producing the experimental data
Non radiative corrected spectra
Radiative corrected spectra