## Slide 1
Alex Bogacz
Ion Booster Ring Design

## Slide 2
MEIC Complex - Baseline Layout
IP
Future IP
Ion Sources
8 GeV Booster
Electron-Ion Collider
Rings
12 GeV CEBAF
5.5-pass CW RLA
Halls A, B, C
Electron Injector
Hall D
SRF Linac
3-10 GeV
8 to100 GeV
3-10 GeV

## Slide 3: Booster (8 GeV, gt = 10)
injection
extraction
RF cavity
Crossing angle:
75 deg.
Injection: multi-turn 6D painting
  0.22-0.25 ms long pulses ~180 turns
  Proton single pulse charge stripping at 285 MeV
  Ion 28-pulse drag-and-cool stacking at ~100 MeV/u
  Ion energies scaled by mas-to-charge ratio to preserve magnetic rigidity
Ekin = 285 MeV – 7.062 GeV
Ring circumference: 273 m
(≈ 2200/8)
3
272.306
0
70
0
7
-7
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Straight
Inj. Arc (2550)
Straight (RF + extraction)
Arc (2550)

## Slide 4
Arc Quadrupoles:
Lq = 40 cm
G = 12-58 Tesla/m
Arc Bends:
Lb = 120 cm
B = 2.73 Tesla
bend ang. = 7.08 deg.
Sagitta =1.8 cm
Straight Quads:
Lq = 40 cm
GF = 12.57 Tesla/m
GD = -24.52 Tesla/m
GF = 12.57 Tesla/m
Booster Lattice (8 GeV, gt = 10)
A. Bogacz
Lattice configured with super-ferric magnets
4
272.306
0
70
0
7
-7
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y

## Slide 5
17.5261
0
70
0
6
-6
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
0
70
0
6
-6
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
17.5261
Perturbed FODO Optics
DGF1
DGF2
17.5261
0
70
0
6
-6
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
17.5261
0
70
0
6
-6
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
2 x 1200 FODO
2 x 900 FODO
DGF1
DGF2
Super-Cell
Super-Cell

## Slide 6
77.8675
0
70
0
6
-6
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
77.8675
0
70
0
6
-6
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Arc Optics
perturbed 900 FODO
Perturbed 1200 FODO

## Slide 7
Optimized Optics – Booster Ring
272.306
0
70
0
6
-6
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
x/ymax = 38/28 m
xx/y = -16/-12

## Slide 8
P. McIntyre
Texas A&M
Bend:
Lb = 120 cm (magnetic length)
Lead ends: 2×22 cm
B = 2.73 Tesla
bend ang. = 7.08 deg.
Sagitta =1.8 cm
Sextupole:
Ls = 10 cm
S = 750 Tesla/m2
50
0
3
-3
BETA_X&Y[m]
DISP_X&Y[m]
8.76306
0
BETA_X
BETA_Y
DISP_X
DISP_Y
Bend
Sextupole
Bend
Correctors
BPM
Quad
Quadrupole:
Lq = 40 cm
G = 12-58 Tesla/m
Correctors (H/V): 10 cm
BPM can: 10 cm
Half-cell cryomodule
Dual-dipole
Quad
Arc Cell - Super-ferric Magnets
Magnet aperture radius:
6srms = 42 mm
8

## Slide 9
35.0522
0
1
0
1
0
Size_X[cm]
Size_Y[cm]
Ax_bet
Ay_bet
Ax_disp
Ay_disp
Beam Envelopes (rms) at Injection (285 MeV)
T = 285 MeV
x = 38 m
g = 0.84
eN_rms = 1 mm mrad
sx = 7 mm
Arc
Arc Super-Cell
bx = 38 m
The magnet aperture radius is 4.2 cm (6 sigma) assuming 285 MeV injection energy. If one lowered the inj energy to 130 MeV, it would increase the radius by factor of 1.25, so it would be 5.2 cm.

## Slide 10: Ion Injection – Transverse Phase-space Painting
55
31.8
30
0
5
-5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Doublet straight injection optics
separation of the injection orbit bump (12s)
B. Erdelyi, NIU

## Slide 11: Linac-to-Booster Transfer Line
Booster injection scheme
  Combined longitudinal and transverse phase space painting
  Components: stripping foil, four-dipole booster orbit bumper system, magnetic and electrostatic septa
Two same-strength quadrupole families of opposite sign
  Eighteen 16 T/m 20/30 cm magnetic/physical length quadrupoles
  Each quadrupole surrounded by 30 cm long corrector and 15 cm long BPM
  Enough quadrupoles for matching to linac and booster as needed
Achromatic 1 m vertical step
  Two 0.5 T 50/78 cm magnetic/physical length dipoles
matching
ions
vertical step
matching
V. Morozov

## Slide 12
Booster-to-Ion Ring Transfer Line
83.8917
0
50
0
6
-6
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
kicker
127.50 Arc
kicker
septum
septum
Lattice based on FODO (900 )
5.5
0
2
-2
Coordinates X&Y[cm]
X
Y
Kickers (2):
L[cm] 120
B[kG] 1.5 angle [mrad] 5
Rise time [ns] Flat Top [ns] Fall time [ns]
300 300 300
Horizontal Extraction: Kicker + Septum
  Enough independent quadrupoles (8) for betatron matching to Ion Ring
Booster Extraction
Ion Ring
Injection
12

## Slide 13: Booster - Space-Charge Issues
Incoherent space-charge tune shift at injection (285 MeV):
  Present baseline: DQsc = 0.1 (for 0.2 Amp coasting beam)
  Consider more aggressive scenario … DQsc ≥ 0.3
Structure resonance crossing and stop-band corrections
  Significant fraction of particles in the beam can move cross third-integer and quarter-integer resonance lines.
  Properly placed quadrupoles and sextupoles could be used to correct the stop-band width of those resonances to minimize the amplitude growth and hence the beam loss.
Halo generation ⇨ beam collimation required

## Slide 14: Ion Booster Optimization for Extreme Space-Charge
The goal of the simulation is to compose the so-called beam-loss tune scan – a fractional beam-loss as a function of the horizontal and vertical tunes - similar to the one carried out for the PS Booster at CERN.

## Slide 15
Mitigation of halo formation and beam loss through comprehensive studies of resonance crossing in the presence of space-charge and implementation of modern resonance compensation techniques.
Implementation of third-integer resonance crossing correction measures by creating anti-resonances via properly placed pairs of sextupoles . They would correct the stop-band width of these resonances to minimize the amplitude growth and hence beam loss.
Define the optimum injection energy, working point tunes, maximum current, as well as to carry out assessment of the acceptable halo and beam loss.
Ion Booster Optimization for Extreme Space-Charge

## Slide 16: Summary
8 GeV Booster design avoiding transition crossing (including transfer lines)
  Low momentum compaction Optics based on perturbed 900 FODO lattice
  Lattice configured with super-ferric magnets (Texas A&M design)
  Injection: Combined longitudinal and transverse phase-space painting
  Extraction: Single kicker and magnetic septum
Future studies of resonance crossing in the presence of space-charge and implementation of modern resonance compensation techniques.
  Define the optimum injection energy, working point tunes, maximum current, as well as to carry out assessment of the acceptable halo and beam loss
No clearly identified technical risks present….

## Slide 17: Backup Slides

## Slide 18: Acceleration - Low Frequency RF Cavities
Booster |  |  |  |  |  | H+ |  |  | 208Pb67+ |  |  | 
Circumference |  | 273 | m |  | Energy | 0.28 | - | 8 | 0.112 | - | 3.2 | GeV
Harmonic Number |  | 1 |  |  | RF Frequency Range | 0.817 | - | 1.274 | 0.578 | - | 1.25 | MHz
Gaps per Cavity |  | 2 |  |  | Ramping Time |  |  | 0.396 |  |  | 0.56 | sec
Cavity Number |  | 1 |  |  | Vgap |  |  | 8.0 |  |  | 5.75 | kV
Cavity Length |  | 2.2 | m |  | Beam Power |  |  | 8.0 |  |  | 1.85 | kW
Total Cavity Length |  | 2.2 | m |  | Power Loss per Cavity |  |  | 41.2 |  |  | 41.2 | kW
Ferrite Toroid Inner Radius |  | 0.25 | m |  | Syn. Phase |  |  | 30.0 |  |  |  | 
Ferrite Toroid Outer Radius |  | 0.5 | m |  |  |  |  |  |  |  |  | 
Ferrite Stack Length |  | 1 | m |  | Acceleration time |  |  | 120 |  |  | 144 | msec
Maximum Vgap |  | 10 | kV |  | Cooling time |  |  | 16 |  |  | 55 | msec
S. Wang
18

## Slide 19: Adiabatic Capture and Acceleration (h =1)
protons
lead ions
B. Erdelyi, NIU
 | H+ |  |  | 208Pb67+ |  |  | 
Energy | 0.28 | - | 8 | 0.112 | - | 3.2 | GeV
RF Frequency Range | 0.817 | - | 1.274 | 0.578 | - | 1.25 | MHz
Ramping Time |  |  | 0.396 |  |  | 0.56 | sec

## Slide 20
Booster-to-Ion Ring Transfer Line - Magnets
83.8917
0
50
0
6
-6
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
kicker
127.50 Arc
kicker
septum
septum
Lattice based on FODO (900 )
Arc Quadrs (17):
Lq = 40 cm
G = 10-25 Tesla/m
Arc Bends (28):
Lb = 120 cm
B = 1.89 Tesla
bend ang. = 4.9 deg.
sagitta = 1.3 cm
Magnetic Septa (2):
Lb = 150 cm
B = 1.5 Tesla
bend ang. = -4.9 deg.
Booster Extraction
Ion Ring Injection
Magnet aperture radius:
6srms = 16 mm
A. Bogacz
20

## Slide 21: Other Boosters - Tunes
  SNS Accumulator: 5.82 / 5.80
  SSC LEB: 11.65 / 11.60
  SPS: 1.82 / 2.72
  SPS Booster: 6.23 / 6.25
  J-PARC RCS: 6.45 / 6.42
  MEIC Booster: 9.87 / 8.85