## Slide 1: Preliminary MEIC Ion Beam Formation Scheme
Jiquan Guo
for the MEIC design study team
Oct. 5, 2015

## Slide 2: Overview of the MEIC Ion Complex
Stage I
  8-100GeV protons
  <=40GeV/u heavy ion
  0.5A beam current
  Collision at up to 476.3MHz
Stage II
  Upgrade to 952MHz SRF system in the e-ring, double the collision rate
  Increase i-ring current to 1-1.5A
  Energy upgrades
IP
Future IP
Ion Source
Booster
MEIC
Collider
Rings
12 GeV CEBAF
Halls A, B, C
Electron Injector
Hall D
SRF Linac
i-SRF +
NCRF
Cooling

## Slide 3: Ion Complex
Major bottleneck: with given aperture, the beam current in the booster ring or collider ring is limited by space charge tune shift, especially at the lowest energy (right after injection from the linac or the booster)
Higher linac/booster extraction energy helps mitigating the SC tune shift and reduces the geometric emittance, but associated with higher cost.
The efficiency of strip injection also has dependence on linac energy.
Need to optimize to reach the performance goal with minimum cost
ion sources
SRF Linac
Booster with DC cooler
collider ring with BB cooler
130MeV H-
42MeV Pb61+
~8GeV H+
~2.7GeV Pb82+
<=100GeV H+
<=40GeV Pb82+
Multi-turn strip injection
Bucket-to-bucket transfer
Coasting beam
bunched beam

## Slide 4: Ion Beam Formation Cycles
Eject the used beam from the collider ring, cycle the magnets
Multi-turn strip-injection of up polarized ion from linac to booster (non-polarized for heavy ions)
Capture beam into a bucket (~0.7× booster ring circumference)
Ramp energy (to 7.9GeV proton or equivalent) and perform DC cooling in the booster
Compress the bunch length to ~0.7/Nh0× of the collider ring circumference (Nh0 is the harmonic # for long bunches)
Bucket-to-bucket transfer the long bunch into collider ring
Repeat step 2-6 for (Nh0/2-1) times, each cycle ~1 min
Switch to down polarized ions and repeat step 1-5 for another (Nh0/2-1) times, total cycles ~Nh0-2
Ramp collider ring to collision energy, perform bunch splitting to harmonic # Nh (~3400-3600)
If needed, manipulate the beam to create several extra empty buckets (476 MHz) in the gap, as required by beam synchronization.
BB cooler
up polarized long bunches
2-4 empty buckets for gaps
down polarized long bunches
2. Accumulating coasting beam
3. Capture to bucket
4/5 Accelerate to 7.9GeV and cool
DC cooler
DC cooler
6. Bunch compression
Step 7/8. Bucket-to-bucket transfer to the collider ring and BB cooling, repeat 26-36 times

## Slide 5: SC Tune Shift in the Booster at Different Injection Energy
Particle | Proton |  |  | Lead |  |  | Deuteron | 
Booster ring circumference (m) | 226.7 |  |  |  |  |  |  | 
Collider ring circumference (m) | 2267 (Nh=3600) |  |  |  |  |  |  | 
Collider ring beam current (A) | 0.5 | 0.5 | 1.0 | 0.5 | 0.5 | 1.0 | 0.5 | 1.0
Collider ring charge (µC) | 3.78 | 3.78 | 7.56 | 3.78 | 3.78 | 7.56 | 3.78 | 7.56
Linac extraction energy (MeV/u) | 121 | 212 | 212 | 42 | 53 | 100 | 66 | 121
Booster cycles | 28 | 14 | 28 | 36 | 28 | 28 | 28 | 28
Booster ring charge (µC) | 0.14 | 0.27 | 0.27 | 0.11 | 0.14 | 0.27 | 0.14 | 0.27
Normalized emittance, step 3 (µm) | 1.66 | 2.25 | 2.25 | 0.95 | 1.07 | 1.47 | 1.20 | 1.66
Booster SC tune shift, step 3 | 0.15 | 0.15 | 0.15 | 0.11 | 0.15 | 0.15 | 0.15 | 0.15
6σ aperture, step 3 (mm) | 39.9 | 40.0 | 40.0 | 39.8 | 39.8 | 39.6 | 39.8 | 39.9
Step 3 ΔνSC limited at 0.15 (won’t be affected by booster circumference)
Beam stay-clear (6σ aperture) limited at 40mm.
Assuming we can get the desired emittance by controlling the DC cooling rate or even scraping
Total allowable charge determined by linac energy (and vice versa).

## Slide 6: Ion Collider Ring SC Tune Shift at Injection Energy
Particle | Proton |  | Lead |  | Deuteron | 
Booster ring circumference (m) | 226.7 |  |  |  |  | 
Collider ring circumference (m) | 2267 (Nh=3600) |  |  |  |  | 
Collider ring beam current (A) | 0.5 | 1.0 | 0.5 | 1.0 | 0.5 | 1.0
Collider ring charge (µC) | 3.78 | 7.56 | 3.78 | 7.56 | 3.78 | 7.56
Booster cycles | 28 | 28 | 36 | 28 | 28 | 28
Booster extraction energy (GeV/u) | 7.9 | 7.9 | 2.65 | 2.65 | 3.55 | 3.55
Booster extraction momentum (GeV/c/q) | 8.79 | 8.79 | 8.79 | 8.79 | 8.79 | 8.79
Booster ring charge (µC) | 0.14 | 0.27 | 0.11 | 0.27 | 0.14 | 0.27
Normalized emittance, step 8 (µm) | 0.5 | 1.0 | 1.0 | 1.5 | 1.0 | 1.2
Collider ring SC tune shift, step 8 | 0.09 | 0.09 | 0.12 | 0.15 | 0.09 | 0.15
6σ aperture, step 6-8 (mm) | 5.19 | 7.34 | 11.7 | 14.3 | 10.4 | 11.4
7.9GeV booster energy is sufficient at least for 1.5A proton and 1.0A Pb beam current in collider ring

## Slide 7: Choosing the Harmonic Number for Bunch Splitting
Nh |  | 3600 |  |  | 3584 |  | 
Circumference (m) |  | 2267 |  |  | 2257 |  | 
Nh0 |  | 16 | 30 | 40 | 16 | 28 | 32
Occupied long bunches |  | 14 | 28 | 36 | 14 | 26 | 30
Gap length (ns, ×2) |  | 472 | 252 | 378 | 470 | 269 | 235
Linac Energy for 0.5A Ib (MeV/u) | Pb | 100 | 53 | 42 | 100 | 56 | 50
 | Proton | 215 | 121 | 100 | 215 | 130 | 115
Linac Energy for 1.0A Ib (MeV/u) | Pb | N/A | 100 | 79 | N/A | 105 | 92
 | Proton | N/A | 215 | 175 | N/A | 225 | 200
Occupied short bunches |  | 3150 | 3360 | 3240 | 3136 | 3328 | 3360
Split scheme |  | ×32×52 | ×5×3×23 | ×5×32×2 | ×7×25 | ×27 | ×7×24
Plenty of options to reduce bunch reprate
Fits the current linac energy
Binary split, might be the easiest
Assuming using sinusoidal RF bucket for bunch splitting, factor>4 splitting is hard. Barrier bucket might help, but needs extensive R&D.
Circumference is ~100m longer than baseline 2150m, might be perfect for additional length needed.
The next choice is Nh=3840 (2418m) with Nh0=30(27 split) and 40 (3×25 split)
Satogata
Booster circumference can be 1/10 of collider ring (Nh0=30 or 40), close to the current figure-8 design; or 1/14 to 1/16 of the collider ring (Nh0=28-32), which may require to change to racetrack design.
Bogacz

## Slide 8: Ion Linac and Sources
Ion sources
stripper
QWR1
HWR
IH
RFQ
QWR2
Ion sources can provide ~4mA 0.5ms polarized H- (~2µC) pulses at ~5Hz, or ~0.02µC per pulse for Pb32+
The linac has a warm front end, three 7-cavity QWR cryomodules and two 7-cavity HWR cryomodules. Pb charge will be stripped once in the linac at ~8.2MeV/u to Pb61+, The output energy from the linac is 42MeV/u for Pb and 130MeV for H-.
Currently SRF linac is the most cost-effective option, and can be upgrade by adding CMs.
Adding one more HWR CM can increase Pb energy to ~55MeV, sufficient to finish 0.5A collider beam injection in 26-28 booster cycles.
Considering the charge stripping efficiency, the booster can finish proton accumulation in a single pulse.
For Pb, each strip-injection cycle may take 10s of pulses, or several seconds. More study on the strip-injection is needed.
Mustapha
Dudnikov

## Slide 9: Adding Extra Bucket for Different Nh
Synchronizing low β ion beam with electron beam may need to change harmonic number in the collider ring by increment of 1, by a total of up to 10. Conventional bunch splitting scheme for certain Nh will not work for Nh+1 (Barrier bucket may work, but needs extensive R&D).
We may split the bunch to Nh, and add extra buckets in the gap by ramping the RF frequency and jump phase in the gap.
Filled with bunch train,
1-1/Nh0 circumference
Gap,
1/Nh0 circumference
After splitting to Nh
f0
f0
Ramping frequency
Ramping complete
/Nh
/Nh
/Nh
Bucket added
Up to 360° phase jump within ~200ns for a low voltage cavity
Harmonic number kept at Nh during ramp
Harmonic number jump to Nh+1

## Slide 10: Summary and Outlook
A preliminary ion beam formation scheme was presented
With Linac energy at 42MeV/u for pb and 130MeV for proton, this scheme is possible to form 0.5A beam current in the ion collider ring for ~30 min. However, we might need to upgrade to 56MeV/u pb to fit certain bunch splitting scheme.
If the ion collider ring beam current needs to be upgraded to 1.0A, energy upgrade is needed in the linac.
7.9GeV booster energy is sufficient for 1.0A collider ring beam current.
The strip injection of the booster ring needs to be studied.
Barrier bucket is a very attractive alternative for bunch splitting and needs to be studied.
Racetrack shape booster can reduce the booster circumference to 1/14 or 1/16 of the ring, which may reduce the cost, and may be required for certain bunch splitting scheme.
Do we need an additional DC cooler in the collider ring?

## Slide 11: Acknowledgements
This work is done by the MEIC accelerator design study group, particularly
Alex Bogacz, Fanglei Lin, Vasiliy Morozov, Fuvia Pilat, Robert Rimmer, Todd Satogata, Haipeng Wang, Shaoheng Wang, Yuhong Zhang (Jefferson Lab)
Peter Ostroumov (ANL)