## Slide 1: Polarimetry in RHIC
Oct. 7, 2015
Haixin Huang
MEIC 2015

## Slide 2: The RHIC p-Carbon CNI polarimeter
Ultra thin Carbon ribbon Target
(5 mg/cm2)
1
3
4
5
6
2
Si strip detectors
(TOF, EC)
18cm
Polarized proton
Recoil carbon
Carbon target
Elastic scattering: interference between electromagnetic and hadronic amplitudes in the Coulumb-Nuclear Interference (CNI) region.
AN(pC)~1%

## Slide 3: Si Ports Design
1, Preamp cards removable for baking
2, Minimizing distance between Si and preamp input
3, Reduce the effect of induced current by beam with fine mesh
(Designed by George Mahler)
Vacuum boundary
Si
Feed through
Fine mesh for electric shield
Preamp card
Detector ports

## Slide 4: Si Detector Readout
Carbon pulse after shaping
~50ns
~300mV
Preamp
shaper
WFD*
(FPGA)
RG59
~300ft
Mode 1
Mode 2
E,T
Mode 3
Identify Carbons using lookup table and records counts bunch by bunch
*WFD=Wave Form Digitizer (420MHz, 8bit )
Si strip detector
IO446-2

## Slide 5: Rate Problem in Run9 and Solution
Run9, s=500 GeV:
METoF2 vs Rate (kHz/strip)
AGS tests, Mar 2010
Problems reproduced at AGS in Run 2010
No problems with new FEE (current sensitive amplifiers)
New amplifier
Old amplifier
0.1 s
10 s

## Slide 6: Carbon Event Selection
The effective energy losses Eloss and time offset t0 are determined from the kinematical fit to the banana-like band
Carbon Events are selected within a Time-Energy window, 400 < T < 900 keV, optimized for minimal background

## Slide 7: Bunch by Bunch Polarization is a Long Shot
Notes: 7

## Slide 8: Operation of p-Carbon Polarimeter
Due to the target orientation and thickness variation, the calibration of p–Carbon polarimeter with polarized jet can not be once and done.
The polarized hydrogen jet needs to be running in parallel.
With upgraded Si detectors, the jet can give polarization error of ±3% for 8 hour store.
In sweep mode, a polarization of ±2% measurement can be done by p-Carbon polarimeter in about 30sec.
Normally, four sets of polarization measurements are done at store: 0, 3, 6, and 8 hours into a store. Each set consists of two polarization measurements done with horizontal and vertical targets, respectively. Besides polarization information, polarization profile information is also obtained.

## Slide 9: Hydrogen Gas Jet and Carbon Ribbon Targets
H-Jet Target
Carbon Ribbon Target
Beam Cross Section

Average Pave
Peak Ppeak
Notes: 9

## Slide 10: Carbon strip target deformation due to electrostatic interaction with the beam at injection energy 24GeV.

## Slide 11: Carbon strip target deformation due to electrostatic interaction with the beam at 255 GeV.

## Slide 12: Hardware Improvements in 2015
  use again 2mm Si-detectors  no gain instabilities
  new target holders
    EM simulation (J. Kewisch) showed beam charge induced high EM fields at target → frame attachment (lightning rod)
    high fields ⇒ high current in target ⇒ heating
    Such fins installed for 32 of 48 targets in 4 pC polarimeters (no room for fins other targets, hit chamber wall)
    Fin size reduced from prototype (don't shadow detectors)
Targets survival

## Slide 13: Target Sweep through Beam

## Slide 14: Summary
The absolute polarization is determined from the polarized hydrogen jet running in parallel
p-Carbon polarimeters at RHIC have consistently performed well in 2011, 2012, 2013, and 2015
They provide information on the beam polarization profile and measures the polarization loss during a RHIC store
Target lifetime has improved thanks to the new fin design of the target holder