## Slide 1: Dual-Frequency Approach to a High Average Current Thermionic Electron Source
Vadim Jabotinski and Alexei Kanareykin
MEIC Collaboration Meeting Fall 2015
Jefferson Lab • October 5-8, 2015
Euclid TechLabs
Gaithersburg, MD Chicago, IL

## Slide 2: Outline
  Target Beam Characteristics
  Bunched Electron Sources and Limitations
  Novel Dual-Frequency Scheme
  Modeling and Simulations
  Power Requirements
  Summary

## Slide 3: Target beam characteristics
  Average current >0.2 A
  Bunch charge 0.5-2 nC
  Linac frequency 748.5 MHz
  Magnetization 1-mm radius in 2-T cooling sol.
                3-mm radius cathode in ~0.2 T.
  Bunch duration 40-150 ps rms
                94-353 ps FWHM
Y. Zhang “Overview of MEIC Cooling Design”
MEIC Collaboration Meeting Spring 2015
R. Suleiman and M. Poelker “200 mA Magnetized Beam for MEIC Electron Cooler” MEIC Collaboration Meeting Spring 2015

## Slide 4: Bunched electron sources. Cathodes
  Cathode: Photo- , Thermionic-, Field Emission
  Extraction & Acceleration: HV DC or pulsed, RF
  Thermionic cathode: Highest Average current
  Drawbacks: E-spread, Duration, Back bombardment
  No good emission gating method
  Photocathode: High brightness, bunch charge
  Drawback: Low average current
  Field emission: Cold, no laser, no heating needed
  Drawbacks: material issues, low bunch charge,
  FEA gives higher charge but larger intrinsic emittance.

## Slide 5: Bunched electron sources. Guns
  Photo-guns (DC or RF accelerating structure)
  - Linac subharmonic freq., low average current
  - CW (LBNL VHF quarter-wave coaxial gun)
  Beam magnetization impossible, large size VHF cavity
  Thermionic guns: Cathode in RF cavity (diode)
  180o, E-spread, Duration, Back bombardment, Beam capture
  HV pulsed (~1.5ms) gridded guns, 1GHz modulation Subharmonic bunching, Low average current,
  Beam capture example: 4500nC emitted for 1nC 10ps FWHM
  Single frequency, gridded, DC bias, DC acc. (IOTs, TRIUMF) Long duration, limited exit energy 300-350keV

## Slide 6: Bunched electron sources. Guns
  Single frequency thermionic electron source, gridded, DC bias, DC acc. (IOTs, TRIUMF)
  Still long bunch duration, limited exit energy 300-350keV
Bidirectional coupler
Single-frequency RF source
Slug tuner
Voltage break
DC Acceleration
Coaxial transmission line
Thermionic cathode
Grid
DC accelerating structure

## Slide 7
  allows shorter bunch length
Dual-Frequency Gating of the Emission
Gating the emission with the
1st harmonic (IOT, TRIUMF)
Gating the emission with the
1st and 3rd harmonics.
Chart: Phase/p
Chart: Phase/p

## Slide 8: Dual-Frequency Gating of the Emission
  FE cathode in RF cavity: Shorter bunch length
  Drawbacks: FE material, RF structure, High power RF sources for both the 1st and 3rd harmonics, CONCEPT
J. W. Lewellen and J. Noonan “Field-emission cathode gating for rf electron guns” Phys. Rev. ST Accel. Beams 8, 033502, 2005
  Thermionic cathode, gridded, DC bias, RF cavity
  Shorter bunch length, injection phase, quality
  Drawback: Inefficient feeding of the 3rd-harmonic power
P. Sprangle et al. “High average current electron guns for high-power free electron lasers” Phys. Rev. ST Accel. Beams 14, 020702, 2011

## Slide 9: Dual-Frequency Thermionic Electron Source
  P. Sprangle et al. “High average current electron guns for high-power free electron lasers” Phys. Rev. ST Accel. Beams 14, 020702, 2011
Experiment (DC acceleration): Inefficient feeding 3rd-harmonic power
S. H. Gold et al. “Development of a high average current rf linac thermionic injector” Phys. Rev. ST Accel. Beams 16, 083401, 2013
Bidirectional coupler
Dual-frequency RF source
1st and 3rd harmonic
3rd harmonic
Slug tuner
Voltage break
cathode bias
Coaxial transmission line
Thermionic cathode
Grid
1st harmonic
Slug tuner
RF accelerating cavity
half-cell
1st harmonic
  shorter bunch length, injection phase, quality

## Slide 10: Dual-Frequency Thermionic Electron Source
  Novel Scheme (exciting the 3rd-harmonic mode)
Bidirectional coupler
Coaxial low pass
harmonic filter
1st harmonic
RF source
748.5 MHz
Slug
tuner
Voltage
break, 700 V DC
Coaxial transmission lines
Cathode region
3rd harmonic RF source
Beam magnetizing solenoid
< 30 mm bore radius
RF accelerating cavity
half-cell, 1st harmonic

## Slide 11: Dual-Frequency Thermionic Electron Source
  Cathode region
Cathode region
3rd harmonic
1st harmonic
Cathode-grid gap
0.25-0.5 mm
Grid
Thermionic
cathode
3mm beam radius

## Slide 12: Dual-Frequency Thermionic Electron Source
  Modeling and Simulations
1st harmonic
3rd harmonic
Dual-frequency emission gating RF structure
Grid region
Thermionic cathode
3mm beam radius
Cathode-grid gap
0.25-0.5 mm
RF accelerating cavity
half-cell, 1st harmonic

## Slide 13: Dual-Frequency Thermionic Electron Source
  Modeling and Simulations
The result is similar to the single-frequency structures (IOT, TRIUMF) and the dual-frequency structures which do not have the off-axis port.
Annotation_2: Electric Field [V/m] (0.7485 GHz)
1st harmonic
1st harmonic (748.5 MHz) fed through the on-axis coaxial port
Electric field magnitude and vector plot

## Slide 14: Dual-Frequency Thermionic Electron Source
  Modeling and Simulations
The S11 plot assumes Mo-conductivity in the 0.25 mm gap. From eigenmode simulations Q is 1779. Based on the field pattern we identify this mode in such a non-standard geometry structure as a variation of the TM020 mode.
3rd harmonic (2.2455 GHz) fed through the off-axis coaxial port
Electric field magnitude and vector plot
Annotation_2: Electric Field [V/m] (2.2455 GHz)
Chart: f- 2.2455 GHz (MHz)
| -1.0007458808149856 | -0.95070858677432524 | -0.90067129273366486 | -0.85063399869300449 | -0.800596704652344 | -0.75055941061168363 | -0.70052211657013441 | -0.65048482252947404 | -0.60044752848881366 | -0.55041023444815318 | -0.50037294040749281 | -0.45033564636683243 | -0.400298352326172 | -0.35026105828462278 | -0.30022376424396241 | -0.25018647020330198 | -0.20014917616264158 | -0.1501118821219812 | -0.10007458808132079 | -5.0037294040660395E-2 | 0 | 5.0037294041549239E-2 | 0.10007458808220963 | 0.15011188212287002 | 0.20014917616353042 | 0.25018647020419083 | 0.30022376424485125 | 0.35026105828551163 | 0.40029835232706085 | 0.45033564636772128 | 0.50037294040838165 | 0.55041023444904202 | 0.60044752848970251 | 0.65048482253036288 | 0.70052211657102326 | 0.75055941061168363 | 0.80059670465323285 | 0.85063399869389333 | 0.90067129273455371 | 0.95070858677521408 | 1.0007458808158745
Measurement_1 (Simulation_1/Iteration 1/Scattering Coefficients (S)) DB(¦S(1, 1)¦) | -4.2429 | -4.5263 | -4.8366 | -5.1769 | -5.5511 | -5.9639 | -6.4205 | -6.9275 | -7.4928 | -8.1263 | -8.8405 | -9.6516 | -10.5814 | -11.6602 | -12.9322 | -14.4656 | -16.375 | -18.8765 | -22.4623 | -28.759 | -51.9142 | -27.6344 | -21.9024 | -18.5052 | -16.0986 | -14.2465 | -12.7517 | -11.5074 | -10.4496 | -9.5363 | -8.7385 | -8.0352 | -7.4109 | -6.8534 | -6.3531 | -5.9023 | -5.4947 | -5.1249 | -4.7886 | -4.4819 | -4.2016

## Slide 15: Power Requirements
  Drive Power ~ Beam loading and Wall losses
  Beam loading >> Wall losses
Chart: Epeak (mm)
| 0 | 1.45566564563039 | 2.9113312912607801 | 4.3669969368911703 | 5.8226625825215601 | 7.2783282281519499 | 8.7339938737823406 | 10.18965951941273 | 11.64532516504312 | 13.10099081067351 | 14.5566564563039 | 16.012322101934291 | 17.467987747564681 | 18.923653393195071 | 20.379319038825461 | 21.834984684455851 | 23.29065033008624 | 24.74631597571663 | 26.20198162134702 | 27.65764726697741 | 29.1133129126078 | 30.568978558238189 | 32.024644203868583 | 33.480309849498973 | 34.935975495129362 | 36.391641140759752 | 37.847306786390142 | 39.302972432020532 | 40.758638077650922 | 42.214303723281311 | 43.669969368911701 | 45.125635014542091 | 46.581300660172481 | 48.036966305802871 | 49.49263195143326 | 50.94829759706365 | 52.40396324269404 | 53.85962888832443 | 55.31529453395482 | 56.770960179585209 | 58.226625825215599 | 59.682291470845989 | 66.960619698997945 | 68.416285344628335 | 69.871950990258725 | 71.327616635889115 | 72.783282281519504 | 74.238947927149894 | 75.694613572780284 | 77.150279218410674 | 78.605944864041064 | 80.061610509671453
Pdrive f, W | 0 | 189.3996 | 383.3486 | 581.8468 | 784.8943 | 992.4911 | 1204.6371 | 1421.3325 | 1642.5771 | 1868.3711 | 2098.7143 | 2333.6068 | 2573.0486 | 2817.0396 | 3065.58 | 3318.6696 | 3576.3085 | 3838.4967 | 4105.2342 | 4376.521 | 4652.3571 | 4932.7424 | 5217.6771 | 5507.161 | 5801.1942 | 6099.7767 | 6402.9085 | 6710.5895 | 7022.8199 | 7339.5995 | 7660.9284 | 7986.8066 | 8317.2341 | 8652.2109 | 8991.737 | 9335.8123 | 9684.437 | 10037.6109 | 10395.3341 | 10757.6066 | 11124.4283 | 11495.7994 | 13420.894 | 13819.5608 | 14222.7768 | 14630.5422 | 15042.8568 | 15459.7207 | 15881.1339 | 16307.0964 | 16737.6081 | 17172.6692
Pdrive f, W | 0 | 188.4383 | 379.5031 | 573.1944 | 769.5122 | 968.4566 | 1170.0276 | 1374.225 | 1581.049 | 1790.4995 | 2002.5766 | 2217.2801 | 2434.6102 | 2654.5669 | 2877.1501 | 3102.3598 | 3330.196 | 3560.6588 | 3793.748 | 4029.4639 | 4267.8062 | 4508.7751 | 4752.3705 | 4998.5925 | 5247.441 | 5498.916 | 5753.0175 | 6009.7456 | 6269.1002 | 6531.0814 | 6795.689 | 7062.9232 | 7332.784 | 7605.2712 | 7880.385 | 8158.1253 | 8438.4922 | 8721.4856 | 9007.1055 | 9295.352 | 9586.2249 | 9879.7244 | 11386.62 | 11695.8787 | 12007.7639 | 12322.2757 | 12639.414 | 12959.1788 | 13281.5701 | 13606.588 | 13934.2324 | 14264.5034
  Cathode radius 3 mm
  Gap 0.25 mm
  Charge 1 nC
  Repetition rate 748.5 MHz
  Average current 0.7485 A
  Peak gap field 7.5 MV/m
  DC bias field -2.8 MV/m
  Power for each harmonic 1 kW

## Slide 16: Examples
  Cathode radius 3 mm
  Operating current density range 10-20 A/cm2 Repetition rate 748.5 MHz
  Bunch duration:
  150 ps rms  1-2 nC , average current 0.7-1.4 A
  40 ps rms 0.27-0.54 nC, average current 0.2-0.4 A
  Cathode: Baria impregnated tungsten dispenser matrix of Type M
  20 A/cm2 DC, 120 A/cm2 pulsed
  Grid: Pyrolytic graphite (PG),
  Mo, Mo-coated PG

## Slide 17: Summary
  Introducing 3rd harmonic for gating thermionic emission improves the beam quality by allowing shorter bunches.
  Existing dual-frequency methods do not realize energy efficient feeding of the 3rd-harmonic in the cathode gap.
  Proposed scheme allows energy efficient feeding of the 3rd harmonic, along with the 1st harmonic.
  The electron source is suitable for cooling of intense proton and ion beams applications.
  The concept can be extended to field emission sources.
  More potential applications: E-source for isotope linacs;
  Fast time resolved microscopy; and spectroscopy.

## Slide 18: Acknowledgements
  I greatly appreciate Jefferson Lab scientists, especially
  Yuhong Zhang, Matt Poelker, Riad Suleiman
  for discussions on the electron sources and
  critical issues for ion cooling applications.