## Slide 1: MEIC Electron Collider Ring Design
Fanglei Lin
MEIC Collaboration Meeting, October 5, 2015

## Slide 2: Electron Collider Design Goal
Electron beam parameters
  3-10 GeV energy
  3A beam current up to 6-7 GeV
  ~1cm bunch length
  small emittance
  < 10MW total synchrotron radiation power
  70% or above polarization
Longitudinal polarization at collision points with a long polarization lifetime
Forward electron detection
Up to two detectors
Provision for correction of beam nonlinearity
Warm magnets
  PEP-II magnets

## Slide 3: CEBAF - Full Energy Injector
e- collider ring
CEBAF fixed target program
  5-pass recirculating SRF linac
  Exciting science program beyond 2025
  Can be operated concurrently with the MEIC
CEBAF will provide for MEIC
  Up to 12 GeV electron beam
  High repetition rate (up to 1497 MHz)
  High polarization (>85%)
  Good beam quality
Electron injection from CEBAF to the collide ring is Jiquan Guo’s talk (next).
Wien Filters and solenoids provide vertically polarized electron beam to the MEIC.

## Slide 4: Transfer Line
Design requirements
  No significant emittance growth
  Room for matching and diagnostic region, compression chicane if needed, a spreader step if needed
  PEP-II magnets (cost)
Realization
  Utilizes PEP-II LER 156 dipoles and 68 quadrupoles
  Dipoles are grouped six as one in FODO cells with 120 phase advance
  Total length of transfer line is 333.25 meters
Injection scheme --- PEP-II-like design
  Dispersion free injection insertion
  Septum + DC + RF kickers
  Vertical injection avoiding parasitic interaction with circulating
  ion beams in the horizontal plane, simplifying the problem of
  masking the detector from particle loss during injection
Courtesy of Y. Roblin

## Slide 5: Complete Electron Collider Layout
Circumference of 2154.28 m = 2 x 754.84 m arcs + 2 x 322.3 straights
Figure-8 crossing angle 81.7
e-
R=155m
RF
RF
Spin rotator
Spin rotator
CCB
Arc, 261.7
81.7
Forward e- detection
IP
Tune trombone & Straight FODOs
Future 2nd IP
Spin rotator
Spin rotator
  Electron collider ring w/ major machine components

## Slide 6: Electron Ring Optics Parameters
Electron beam momentum | GeV/c | 10
Circumference | m | 2154.28
Arc’s net bend | deg | 261.7
Straights’ crossing angle | deg | 81.7
Arc/straight length | m | 754.84/322.3
Beta stars at IP *x,y | cm | 10/2
Detector space | m | -3 / 3.2
Maximum horizontal / vertical  functions x,y | m | 949/692
Maximum horizontal / vertical dispersion Dx,y | m | 1.9 / 0
Horizontal / vertical betatron tunes x,y |  | 45.(89) / 43.(61)
Horizontal / vertical chromaticitiesx,y |  | -149 / -123
Momentum compaction factor  |  | 2.2 10-3
Transition energy tr |  | 21.6
Hor./ver. emittance x,y (normalized/un-normalized) | µm rad | 1093 / 219 (0.056/0.011)
Maximum horizontal / vertical rms beam size x,y | mm | 7.3 / 2.7

## Slide 7: Normal Arc FODO Cell
Complete FODO (Each arc has 34 such normal FODO cell)
  Length 15.2 m (arc bending radius 155 m)
  2 dipoles + 2 quadrupoles + 2 sextupoles
  108/90 x/y betatron phase advance
Dipoles
  Magnetic/physical length 5.4/5.68 m
  Bending angle 48.9 mrad (2.8), bending radius 110.5 m
  0.3 T @ 10 GeV
  Sagitta 3.3 cm
Quadrupoles
  Magnetic/physical length 0.56/0.62 m
  -11.6 and 12.8 T/m field gradients @ 10 GeV
  0.58 and 0.64 T @ 50 mm radius
Sextupoles
  Magnetic/physical length 0.25/0.31 m
  -176 and 88 T/m2 field strengths @ 10 GeV
  for chromaticity compensation only in two arcs
  (strengths will be determined in DA simulations)
BPMs and Correctors
  Physical length 0.05 and 0.3 m

## Slide 8: Matching + Universal Spin Rotator
Matching section: 4 arc FODO cells, all eight 0.56/0.62m-long quads’ strengths < 16.96 T/m @ 10 GeV
Universal Spin Rotator (USR)
  Rotate the polarization between the vertical and the longitudinal from 3 to 10 GeV
  Six 2m-long dipoles with 0.53 T @ 10 GeV
  Two 2.5m-long solenoids and two 5m-long solenoids with maximum field 7 T @ 10 GeV
  Quads have different lengths with maximum strength ~ 25 T/m @ 10 GeV
Matching section
USR
Arc
Straight
Was not optimized. Large contribution to the equilibrium emittance.
Is optimized to reduce the emittance contribution. (not integrated to the ring yet.)

## Slide 9: Electron Polarization Design
IP
Arc
Half Sol.
Half Sol.
Dec. Quad. Insert
Solenoid decoupling
1st Sol. + Dec. Quads
Dipole set
2nd Sol. + Dec. Quads
Dipole Set
P. Chevtsov et al., Jlab-TN-10-026
Electron polarization configuration to achieve: two polarization states simultaneously in the ring with 70% (or above) longitudinal polarizations at IPs
Electron polarization direction
Universal Spin Rotator
Spin tuning solenoid
Detail is in my talk on electron polarization
Schematic drawing and lattice of USR

## Slide 10: Tune Trombone/Straight FODO & Matching Sec.
Tune trombone/straight FODO cell (60 phase advance) and Matching sections
  All quads have a magnetic/physical length of 0.73/0.79 m (PEP-II straight quads)
  Whole ring has 76 such quads, of which 58 with a maximum field < 17.53 T/m @ 10 GeV and 18 with a maximum field ~ 25 T/m

## Slide 11: Chromaticity Compensation
Developed local Chromaticity Compensation Block (CCB)
  Two 5m-long dipoles and four 2m-long dipoles with a maximum field 0.58 T @ 10 GeV
  13 quads (7 families) have a maximum field ~25 T/m @ 10 GeV
  4 sextupoles (2 families) are used for a compensation of local chromaticities from the FFQs
Distributed -I pair sextupoles compensation scheme will also be considered.

## Slide 12: RF Section
RF section
  Relatively small beta functions to improve the coupled beam instability thresholds
  One such RF section in each straight, totally can accommodate up to 32 cavities (old)
  15 quads (2 families) have a maximum field ~25 T/m @ 10 GeV
6.54 m

## Slide 13: IP Region
IP region
  Final focusing quads with maximum field gradient ~63 T/m
  Four 3m-long dipoles (chicane) with 0.44 T @ 10 GeV for low-Q2 tagging with small momentum resolution, suppression of dispersion and Compton polarimeter
Detail of interaction region design will be presented by Vasiliy Morozov.
IP
e-
forward e-
detection region
FFQs
FFQs
Compton polarimetry region
x(m), y(m)
Dx(m)
Baseline Design
x(m), y(m)
Dx(m)
x(m), y(m)
Dx(m)
Optimization
or
e-
IP
IP
e-

## Slide 14: Forward e- Detection & Pol. Measurement
Forward electron detection: Dipole chicane for high-resolution detection of low-Q2 electrons
c
Laser + Fabry Perot cavity
e- beam
Low-Q2 tagger for
low-energy electrons
Low-Q2 tagger for high-
energy electrons
Electron
tracking detector
Photon
calorimeter
e-
ions
IP
forward ion detection
forward e- detection
Compton polarimetry
Local crab cavities
local crab cavities
local crab cavities
Courtesy of A. Camsonne
Electron polarimetry and low-Q2 tagging will be discussed in Dave Gaskell’s talk.
Compton polarimetry has been integrated to the interaction region design
  Same polarization at laser at IP due to zero net bend
  Non-invasive monitoring of the electron polarization

## Slide 15: Complete Electron Ring Optics
IP
The baseline design of MEIC electron collider ring is completed with all required machine elements or space for special machine components.

## Slide 16: Magnet Inventory of MEIC e-Ring
MEIC (total)
  Dipoles: 202
  Quads: 414
  Sextupoles: 136
  Skew quads: 12
  Correctors: 331
Magnet category | PEP-II HER magnet |  | New magnet | 
 | Number | Max. Strength | Number | Max. Strength
Dipole | 168 | 0.3 T | 34 | 0.64 T
Quadrupole | 263 | 17 T/m | 151 | 25 T/m
Sextupole | 104 | 600 T/m2(?) | 32 | 600 T/m2
Skew quadrupole | 12 | 2.33 T/m |  | 
BPM |  |  | 331 | 
Corrector | 283 | 0.02 T | 48 | 0.02 T
PEP-II (total, from SuperB CDR)
  Dipoles: 200
  Quads: 291
  Sextupoles: 104
  Skew quads: 12
  Correctors: 283
Study of PEP-II magnets will be discussed in Tommy Hiatt’s talk.

## Slide 17: Synchrotron Radiation Parameters
Beam current up to 3 A at 6.95 GeV
Synchrotron radiation power is under 10 MW at high energies
Beam energy | GeV | 3 | 5 | 6.95 | 9.3 | 10
Beam current | A | 1.4 | 3 | 3 | 0.95 | 0.71
Total SR power | MW | 0.16 | 2.65 | 10 | 10 | 10
Linear SR power density (arcs) | kW/m | 0.16 | 2.63 | 9.9 | 9.9 | 9.9
Energy loss per turn | MeV | 0.11 | 0.88 | 3.3 | 10.6 | 14.1
Energy spread | 10-3 | 0.27 | 0.46 | 0.66 | 0.82 | 0.91
Transverse damping time | ms | 376 | 81 | 26 | 14 | 10
Longitudinal damping time | ms | 188 | 41 | 13 | 7 | 5
Normalized Emittance | um | 30 | 137 | 425 | 797 | 1093

## Slide 18: Approaches of Reducing Emittance
All following options have been investigated
  Optimizing of sections, such as matching section, spin rotator, etc., to reduce the emittance contribution (30%)
    Pros: do not change the optics of the rest of the ring, except some particular sections
    Cons: ~110m additional space and 16 quads are needed (cost)
  Adding (dipole) damping wigglers (50% @ 5 GeV)
    Pros: do not change the baseline design, fast damping
    Cons: need wigglers (cost), more radiation power (cost), larger energy spread (a factor of 2), not suitable at higher energies
  Offsetting the beam in quads (~ 7 to 8 mm) in arcs (48%)
    Pros: do not change the baseline design
    Cons: larger energy spread (a factor of 2), longer (maybe) bunch length, have to center the sextupoles
  New magnets (instead of PEP-II magnets) ring but still FODO cell arcs (50%)
    Pros: with a small bending angle, dipole has no sagitta issue and the emittance can be reduced
    Cons: all new magnets (cost), large chromaticities
  Different types of arc cell, such as DBA, TME (> 50%)
    Pros: much smaller emittance comparing to the FODO cell
    Cons: more quads, stronger quads, larger ring (cost), large chromaticities

## Slide 19: Optics of Matching Section
In the baseline design
  Regular arc FODO cell: each dipole bending angle , phase advance
  Matching section: each dipole bending angle
New matching section: “missing magnet” dispersion suppressor + beta function matching
  Matching section dipole bending angles
  Regular arc bending angle
  8 extra dipoles (4 FODO cells) are needed
Regular arc FODO cell
Spin rotator
Matching section
Baseline
Regular arc FODO cell
Spin rotator
New

## Slide 20: Optics of Spin Rotator
In the baseline design
  Lattice in the two dipole sets was not optimized to have a small emittance contribution.
In the new design
  Lattice in the two dipole sets is optimized to a DBA-like optics, which has a smaller emittance than that in the baseline design.
Baseline
Dipole set
Dipole set
2nd sol. + decoupling quads
1st sol. + decoupling quads
New
Dipole set
Dipole set
2nd sol. + decoupling quads
1st sol. + decoupling quads

## Slide 21: Emittance @ 10 GeV (example)
Section | Normalized Horizontal Emittance (m) | 
 | Baseline design | New design *
Regular FODO cells in two arcs | 476 | 569
Matching sections between FODO cells and spin rotators | 389 | 6
Spin rotators | 119 | 84
Straight with IP (CCB + Chicane) | 84 | 85
Straight without IP | 0 | 0
Total | 1068 | 745
Extra space needed (m) |  | 111
* Extra ~110 m-long space is needed for 4 extra arc FODO cells, new matching and spin rotator sections.
* Almost the same amount space is also required in the ion collider ring for the vertical chicanes.

## Slide 22: Summary and Outlook
2.2km baseline design of MEIC electron collider ring has been completed
  meeting all requirements on the beam parameters
  incorporating dedicated electron polarization and forward detection design
  accommodating up to two detectors
  considering optics design for special elements, such as RF, etc.
  Incorporating provisions for correction of beam nonlinearity
  using the majority of PEP-II magnets (and vacuum chamber)
To do:
  Optimization of the chromaticity compensation scheme
  Study of error sensitivity
  Further optimization to obtain smaller emittance if needed
Acknowledgements
  A. Camsonne, D. Gaskell, Y.S. Derbenev, J. Grames, J. Guo, A. Hutton, L. Harwood, V.S. Morozov, P. Nadel-Turonski, F. Pilat, R. Rimmer, M. Poelker, R. Suleiman, H. Wang, S. Wang, Y. Zhang, – JLab
  M. Sullivan, U. Wienands  SLAC

## Slide 23
Thank You for Your Attention !

## Slide 24
Back Up

## Slide 25: Magnet Inventory of PEP-II HER
Table from SuperB CDR, March 2007
Dipole field can achieve 0.363 T because it was designed for PEP 18 GeV electron beam
Quadrupoles and sextupoles are used in the MEIC arc and straight FODOs and some matching sections
Sextupoles strength can run up to 600 T/m2 run in PEP (J.R. Rees, SLAC-PUB-1911)

## Slide 26: Damping Wigglers
Damping wigglers in the dispersion-free straight
  Each damping wiggler has nine 0.1m-long and two 0.05m-long 1.6 T dipoles (alternate horizontally-deflecting fields)
  6 damping wigglers in 3 straight FODOs lower the emittance by a factor of 2 at 5 GeV (from 138 to 69 um)
  Total radiation power is 5.5 MW, with 3 MW from 6 wigglers
  6 quads are used to match the lattice functions to the rest of the ring
  Number of wiggler sections can be adjusted
x, y (m)
Dx (*10-3m )
x, y (m)
Dx (*10-3m )
x, y (m)
Dx (*10-3m )

## Slide 27: Damping Wiggler
Damping wiggler in the dispersion-free straight
  24 m long with 240 periods
  1.6 T maximum field with sinusoidal field variation along the electron path
  horizontally deflecting
Straight FODO
Straight FODO
24m long damping wiggler

## Slide 28: Synchrotron Radiation Parameters
 |  | One IP 2154m e-ring w/o DW |  | One IP 2154m e-ring w/ DW | 
Beam energy | Gev | 5 | 10 | 5 | 10
Beam current | A | 3 | 0.71 | 3 | 0.71
Energy loss per turn | MeV | 0.85 | 13.55 | 1.82 | 18.22
Total SR power | MW | 2.5 | 9.6 | 5.5 | 12.9
Norm. H. emittance | um | 138 | 1092 | 59 | 805
Energy spread | 10-3 | 0.45 | 0.91 | 0.94 | 1.14
Trans. damping time | ms | 85 | 11 | 39 | 8
Long. damping time | ms | 42 | 5 | 20 | 4
  At 5 GeV, the energy spread is increase by a factor of 2. In order to keep the bunch length of 1.2cm, the RF peak voltage has to increase by a factor of 3.87. It results that we need 18 PEP-II cavities, instead of 10. (consulting with Shaoheng Wang)
Such a damping wiggler section (with quads) will need 30-40m long straight space.

## Slide 29: Emittance, Energy Spread, Bunch Length
Radiation integrals:
where, is the dispersion, is the quadrupole strength
Damping partition numbers: here
Emittance:
Energy Spread:
Bunch length:
When , or
When , or
Offsetting the beam in quads will introduce a dipole field that generates a curvature.

## Slide 30: FODO Cell (@ 10 GeV)
1st :
Normal quads FODO cell (in MEIC e-ring arcs)
Combined function quads FODO cell
2nd :
Equivalent to offset the beam in quads by 8.2 mm and 7.4 mm, respectively.
Quad settings

## Slide 31: MEIC Electron Collider Ring with New Magnets
Arc dipole length | m | 3.75
Arc quad length / strength @ 12 GeV | m / T/m | 0.56 / 21
Cell length | m | 11.4 (half of ion ring arc cell)
Arc dipole bending angle / radius | deg / m | 2.045 / 105
FODO cells per arc (no spin rotator included) |  | 64
Total arc dipoles |  | 256
Total bending angle per arc | deg | 261.7
Figure-8 crossing angle | deg | 81.7
Arc length (no spin rotator) | m | 729.6
Straight length | m | 369.46
Ring circumference | m | 2198
Beam current @ 10 GeV, arc only | A | 0.785 (@SR power < 10 kW/m)
Normalized emittance @10 GeV | mm mrad | 329
(including spin rotator, IR, etc.) | mm mrad | 329 x 1.7 ~ 559
Notes: Red Interior Page Design 2

## Slide 32: Optics of New Matching Section (I)
New matching section: “missing magnet” dispersion suppressor + beta function matching
  Matching section dipole bending angles
  Regular arc bending angle
  No extra dipole is needed
Regular arc FODO cell
Spin rotator

## Slide 33: Optics of New Matching Section (II)
New matching section: “missing magnet” dispersion suppressor + beta function matching
  Matching section dipole bending angles
  Regular arc bending angle
  8 extra dipoles (4 FODO cells) are needed
Regular arc FODO cell
Spin rotator

## Slide 34: Emittance
Section | Normalized Horizontal Emittance (m) |  | 
 | Baseline design | New design 1* | New design 2**
Regular FODO cells in two arcs | 476 | 665 | 569
Matching sections between FODO cells and spin rotators | 389 | 7 | 6
Spin rotators | 119 | 81 | 84
Straight with IP (CCB + Chicane) | 84 | 82 | 85
Straight without IP | 0 | 0 | 0
Total | 1068 | 835 | 745
Extra space needed (m) |  | 50 | 111
* New design 1: Each regular arc FODO cell dipole bending angle is 2.94. Extra 50 m-long space is needed for new matching and spin rotator sections.
** New design 2: Each regular arc FODO cell dipole bending angle is 2.80. Extra 111 m-long space is needed for 4 extra arc FODO cells, new matching and spin rotator sections.