## Slide 1: Progress of Bunched Beam Electron Cooling Demo
L.J.Mao (IMP), H.Zhang (Jlab)
On behalf of colleagues from Jlab, BINP and IMP

## Slide 2
Motivation
HIRFL-CSR facility
Cooling Experiments @ HIRFL-CSR
Simulation works
Conclusion

## Slide 3
Based on requirements of EIC proposals, high energy electron cooling devices are necessary. The electron beam can be only provided by RF accelerators.
Investigation of beam cooling effects by bunched electron beam
Average cooling time measurements with different bunched electron beam parameters
Peak current; Bunch length; Duty cycle; Repetition frequency…
Weak bunching effect
Bunched ion beam cooling by bunched electron beam
Revolution frequency matching
Motivation

## Slide 4
Heavy Ion Research Facility at Lanzhou (HIRFL)
Heavy ions from D+ to U28+ can be injected, cooled and accelerated in the cooling storage ring.

## Slide 5
35 keV electron cooler @ CSRm
Items | Value
Electron energy | Up to 35 keV (20 keV for this exp.)
Electron current | Up to 3.0 A
Electron beam radius @ cathode | 14.5 mm
Expansion factor in operation | 3.2
Magnetic field @ cooling section | 390 Gs (in operation)
Effective cooling length | 3.4 m
Vacuum condition | 10-11 mbar

## Slide 6
grid
anode
Variable profile electron gun
Grid electrode locates between cathode and anode is used to control the electron emission at the edge of cathode.

## Slide 7
RF modulation on the grid
≈
=
cathode
anode
grid
Ua
Ub+Urf

## Slide 8
Main ion beam parameters
Items | Value | 
Ion type | 12C6+ | 
Circumference of CSRm | 161 m | 
Energy | 7.0 MeV/u | 30 MeV/u
Beta | 0.122 | 0.248
Gamma | 1.008 | 1.032
Revolution time | 4.4 us | 2.2 us
Revolution frequency | 227 kHz | 462 kHz
Harmonic number* | 1, 2, 4 | 1, 2
Stored particle number | >109 | 
Initial momentum spread | 10-3 (RMS) | 
Final momentum spread | 10-5 | 

## Slide 9
Electron cooling experiments @ CSR
Cooling of C6+ ion beam at the energy of 122 MeV/u.

## Slide 10
Cooling
C6+
O8+
122MeV/u
Cooling
C3+
O4+
122MeV/u C3+ @ CSRe
122MeV/u
Electron cooling experiments @ CSR
Energy=122 MeV/u
Beta=0.467, gamma=1.131
F0=1.088 MHz
Df=15 kHz
Dp/p=1/eta*df/(h*f0)=9*10-5

## Slide 11
Electron cooling experiments @ CSR
initial, dp/p=5×10-4
final, dp/p=3×10-5
The momentum spread can be obtained by the fitting of experimental data

## Slide 12
Electron cooling experiments @ CSR

## Slide 13
C6+
O8+
RF bunching
Freq. shift
Cooling
Electron cooling experiments @ CSR

## Slide 14
Electron cooling experiments @ CSR

## Slide 15
Electron cooling experiments @ CSR
122MeV/u
C6+ @ CSRe

## Slide 16
Cooling Dynamic Simulation
RMS dynamic
In each time step
  Sample the ions w.r.t the given emittance
  Calculate IBS rate
  Calculate electron cooling rate
    Total rate
Repeat till the end.

## Slide 17
Only sample the ions that interact with one electron bunch
Coasting ion beam: Gaussian distribution transversely and uniform distribution longitudinally
Calculate the friction force on each ion
Calculate the change of dynamic invariance of each ion
Calculate the cooling rate statistically in the sampled region
Adjust the cooling rate w.r.t. the duty factor
Model of Bunched Electron & Coasting Ion

## Slide 18
Simulation Result
12C6+ beam:
Coasting
Number 5.00E+08
KE = 7 MeV
Cooler:
thin lens
L=3.4 m
B=0.039 T
dx=10 m
dy=17 m
Electron beam:
Bunched
r=2.5 cm
L =0.3 -3 m
Tx =0.05 eV
Ty=0.1 eV
F = 3MHz

## Slide 19
Simulation Result
Iavg=1.7 mA
Iavg=17 mA

## Slide 20
Conclusion
A DC high voltage platform is already delivered to IMP for this experiments.
A RF module for the grid will be developed by the collaboration between Jlab, BINP and IMP
A Schottky detector can be used to investigate the longitudinal cooling effect
A transverse profile will be tested within two months
A simulation work will be done by considering the longitudinal motion equation
The first experiment is planed to be done in May of 2016

## Slide 21
Non destruction profile monitor for CSRm

## Slide 22
Thank you

## Slide 23
place for
emittance meter
Faraday cup
beam stop
cathode
anode
10 cm
collimator
Ø 15 mm